## Slide 1
LCEC Coded Block Flag Coding Under Residual Quadtree
(JCTVC-D375, m19152)

## Slide 2: Current Coded Block Flag Coding
At CU root level
  Coded block flags for Y, U and V are coded jointly
At higher transform depth level
  Four flags of the same video component at a same transform depth level are jointly coded.
Blk0
Blk1
Blk2
Blk3
A coding unit

## Slide 3: Proposed Solution on Coded Block Flag
Transform split flag is jointly coded together with coded block flags
In addition to CU root level, the joint coding of coded block flag and transform split flag is also performed at higher transform depth level
If only one coded block flag left in each block to be coded, the four flags at the same transform depth level are grouped and jointly coded as before

## Slide 4: Test Conditions and Simulations
Test conditions
  Case 1: use default low complexity configurations
  Case 2: use default low complexity configurations, but change the maximum TU depth to 3 for both intra and inter block
Simulations
  Test 1: set both macro LCEC_CBP_YUV_ROOT and QC_BLK_CBP to 0
  Test 2: the current CBP coding with RD fix
  Test 3: proposed scheme

## Slide 5: Test Results on Coded Block Flag (test 2 vs. test 1)
Test 2 vs. Test 1, All intra configuration
 | Intra LoCo TU level 3 |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.8 | -0.7 | -0.4 | -1.8 | -0.3 | 0.3
Class B | -1.9 | -1.0 | -0.7 | -1.9 | -0.4 | 0.0
Class C | -1.4 | -0.8 | -0.8 | -1.4 | -0.6 | -0.5
Class D | -1.1 | -0.6 | -0.7 | -1.1 | -0.4 | -0.5
Class E | -3.2 | -0.9 | -1.4 | -3.1 | 0.7 | -0.1
All | -1.8 | -0.8 | -0.8 | -1.8 | -0.2 | -0.2
Current CBP coding (RD fixed version) vs. initial CBP signaling (with both LCEC_CBP_YUV_ROOT and QC_BLK_CBP set to 0)

## Slide 6: Test Results on Coded Block Flag (test 2 vs. test 1)
Test 2 vs. Test 1, Random access
Current CBP coding (RD fixed version) vs. initial CBP signaling (with both LCEC_CBP_YUV_ROOT and QC_BLK_CBP set to 0)
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.2 | -0.5 | -0.2 | -1.4 | -0.3 | 0.2
Class B | -1.2 | -1.6 | -1.2 | -1.5 | -1.2 | -0.6
Class C | -0.9 | -1.2 | -1.0 | -1.2 | -0.8 | -0.9
Class D | -0.8 | -1.0 | -1.1 | -1.1 | -0.7 | -0.9
Class E |  |  |  |  |  | 
All | -1.0 | -1.2 | -1.0 | -1.3 | -0.8 | -0.6

## Slide 7: Test Results on Coded Block Flag (test 2 vs. test 1)
Test 2 vs. Test 1, Low delay
Current CBP coding (RD fixed version) vs. initial CBP signaling (with both LCEC_CBP_YUV_ROOT and QC_BLK_CBP set to 0)
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.9 | -2.3 | -2.0 | -1.9 | -1.8 | -1.3
Class C | -0.7 | -1.4 | -1.7 | -1.7 | -0.8 | -1.1
Class D | -0.7 | -1.2 | -1.5 | -1.8 | -0.6 | -0.9
Class E | -1.2 | -0.4 | -0.5 | -2.2 | 0.8 | 0.1
All | -0.9 | -1.4 | -1.5 | -1.9 | -0.8 | -0.9

## Slide 8: Test Results on Coded Block Flag (test 3 vs. test 1)
Test 3 vs. Test 1, All intra configuration
 | Intra LoCo TU level 3 |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.3 | -1.2 | -1.0 | -1.8 | -0.3 | 0.3
Class B | -2.3 | -1.4 | -1.2 | -1.9 | -0.4 | 0.0
Class C | -1.7 | -1.1 | -1.1 | -1.4 | -0.6 | -0.5
Class D | -1.3 | -0.9 | -1.0 | -1.1 | -0.4 | -0.5
Class E | -3.7 | -1.4 | -2.0 | -3.0 | 0.7 | -0.1
All | -2.2 | -1.2 | -1.2 | -1.8 | -0.2 | -0.2
Proposed CBP coding vs. initial CBP signaling (with both LCEC_CBP_YUV_ROOT and QC_BLK_CBP set to 0)

## Slide 9: Conclusions
The current CBP signaling with RD fix clearly outperforms the initial residual quadtree CBP signaling
Using the proposed scheme, coding performance can be further improved, especially in case with a maximum TU depth of 3
We propose:
  The RD fix be adopted into HM
  Add the new proposed scheme to the next CE on LCEC