## Slide 1
Presented by Michael Horowitz
JCT-VC Meeting in Daegu, KR
Date January 20-28, 2011
Generalized Slices

## Slide 2: Overview
Introduction
Generalized Slices (GS)
Implementation Details
Syntax
Experiment
Results
Conclusion and Recommendation

## Slide 3: Introduction
Picture partitioning introduces coding loss
Why partition a picture?
  High-level parallel processing
    Picture segments processed by separate processors
    Independence reduces costly inter-processor communication

## Slide 4: Introduction (continued)
  MTU size matching
    Coded slice size > MTU size
      Network fragments oversize packet carrying slice or
      Application uses multiple MTU-sized packets for 1 slice
      Both cases: loss of one fragment  loss of large slice
    Coded slice << MTU size
      Packet header overhead steals coding efficiency
    Coded slice size == MTU size
      Minimizes packet header overhead
      Slice independence ensures received slices can be decoded  error resilience
GS reduces loss due to picture partitioning

## Slide 5: Generalized Slices
Vertical boundaries partition picture into columns

## Slide 6: Features Unique to GS
Not constrained to be rectangular
  Partition flexibility is key for MTU size matching
  Especially important at higher bit rates
Signaled at picture/sequence parameter set
  Low signaling overhead
Low implementation complexity
  H.264/AVC slice groups provide functionality with much higher implementation complexity
Facilitates decoder parallelization
  Outside the scope of HEVC

## Slide 7: Implementation Details
Few mods to AhG-slice source code
  Decoding order: raster scan in columns
  CU availability: CU’s not available across column boundaries
Added PPS syntax coding/parsing
Notes: Emphasize simplicity

## Slide 8: Syntax
Number of columns and widths
Picture parameter set (SPS also possible)
num_columns_minus1
for (i=0; i < num_columns_minus1; i++)
columnWidth[i]

## Slide 9: Experiment
Focus: parallel processing
  Equal size partitions (except at picture boundaries)
  GS partitions
1/3 number of frames specified in common conditions for each sequence

## Slide 10: Random Access Results
GS vs. AhG slice reference Random Access
GS and reference used same number of slices
* Encoding/decoding for GS & AhG slices performed on different machines
Notes: Mention scripts we have developed and offer them

## Slide 11: Low-Delay Results
GS vs. AhG slice reference Low-Delay
GS and reference used same number of slices
* Encoding/decoding for GS & AhG slices performed on different machines

## Slide 12: Intra-only Results
GS vs. AhG slice reference Intra-only
GS and reference simulations used same # of slices
* Encoding/decoding for GS & AhG slices performed on different machines

## Slide 13: Analysis
Gains mostly due to smaller number of slice boundaries
*Result from Low Delay
Content plays a role as well
  Note Class A results
No additional computational complexity
 | Class A | Class B | Class C | Class E
AhG:GS Slice Boundary Ratio | 2.7 | 2.8 | 1.2 | 2.1
GS RA coding gain (Y BD-rate) | 1.6% | 3.6% | 0.5% | 1.9%*

## Slide 14: Conclusion and Recommendation
Coding gains vs. AhG slice reference
  Random Access: 2.0%
  Low Delay: 1.3%
  Intra Only: 1.6%
No additional computational complexity
Complementary with fine granularity slices and entropy slice techniques
Facilitates parallelization at decoder
Recommendation
  Continue evaluation of Generalized Slices for possible adoption into the HM
Notes: Results may be improved with content aware partitioning

## Slide 15: Back-up Slides

## Slide 16: Random Access 1 Slice Results

## Slide 17: Low Delay 1 Slice Results

## Slide 18: Intra-only 1 Slice Results

## Slide 19: 1 Slice Result Summary
For RA GS saves 42% relative AhG slices
For LD GS saves 25% relative AhG slices
For Intra GS saves 60% relative AhG slices