## Slide 1: CE8 Subset1: Cross verification of Mediatek’s deblocking filter by Ericsson
Kenneth Andersson, Andrey Norkin, Rickard Sjöberg
Ericsson

## Slide 2: Summary
The source-code have been re-designed significantly compared to Guangzhou meeting
Mismatch on coding efficiency numbers for some sequences and QPs compared to Mediatek D163. Other mismatches than Toshiba D203.
Pure deblocking time on all-intra increase by 30% compared to TMuC 0.9.
Decoding time increase compared to TMuC 0.9 match Mediatek results.
More blocking artifacts than TMuC 0.9 for random access and low-delay configurations at low bitrates. Similar performance as TMuC 0.9 for all intra coding configurations.

## Slide 3: Source code inspection
8x8 block based filter decision using 4 tables whereas TMuC 0.9 only uses one table
Significant complexity increase for deblocking of intra/intra blocks by directional filtering. Pure deblocking time for all-intra increase by 30%.
Directional filtering is performed across block boundaries.
Filtering approach similar as TMuC 0.9 but using other weak filters and additional filter decisions.
No strong filter is used if both blocks are inter

## Slide 4: Objective performance
BDR performance matches Mediatek
Coding efficiency is not consistently better than TMuC 0.9 on all sequences and conditions, some examples:
  Worse performance on luma for People on Street and Kimono for random access low complexity
  Worse performance on luma for Kimono for random access without ALF
  Worse performance on chroma for Class E sequences for all intra

## Slide 5: Subjective inspection
More blocking artifacts than TMuC 0.9 for random access and low delay for both high efficiency and low complexity for low bitrates.
  Some example sequences are the Vidyo sequences and Kimono
For all intra coding the visual quality was found to be similar as for TMuC 0.9.
The monitor used for the subjective inspection was HP LP2475w.

## Slide 6: Conclusion
The proposal have been significantly changed since Guangzhou meeting.
Mismatch on coding efficiency numbers for some sequences and QPs. Other mismatches than Toshiba results in D203.
Pure deblocking time on all-intra increase by 30% compared to TMuC 0.9.
Decoding time increase compared to TMuC 0.9 match Mediatek results.
Visual inspection of reconstructed video indicate more blocking artifacts for the Mediatek’s deblocking filter than for TMuC 0.9 for both random access and low delay configurations at low bitrates. For all intra the visual quality is similar.