## Slide 1: JCTVC-D380 Reduced complexity PIPE coding using systematic v2v codes
H. Kirchhoffer, D. Marpe, H. Schwarz,
C. Bartnik, A. Henkel, M. Siekmann,
J. Stegemann, and T. Wiegand
Fraunhofer HHI

## Slide 2: Outline
Introduction of a new set of v2v codes for PIPE
Theoretical performance evaluation
Aspects of efficient implementations
Computational complexity
Experimental coding efficiency evaluation
Summary

## Slide 3: Review of the PIPE codig concept
Binarization and context modelling as in CABAC
Modified coding of binary decisions (bins)
  LPB probabilities are quantized
  Separate bin encoders for each class (fixed LPB probabilities)
  Bin encoders use v2v codes for encoding the bins

## Slide 4: Systematic v2v codes
Three different classes of v2v codes
  ‘Unary to Rice’ codes
  ‘Three bin’ code
  ‘Bin pipe’ codes
Each class of code has a simple construction rule

## Slide 5: ‘Unary to Rice’ codes
Maps truncated unary code (mostly) to fixed length
Example for Golomb-Rice parameter n equal to 3:
Index Primary Secondary
1 1 0000
2 01 0001
3 001 0010
4 0001 0011
5 00001 0100
6 000001 0101
7 0000001 0110
8 00000001 0111
9 00000000 1
Can be interpreted as mapping a unary code to a Golomb-Rice code

## Slide 6: ‘Three bin’ code
Primary code is of fixed lengeh (3 bins)
Index Primary Secondary
1 000 0
2 001 100
3 010 101
4 100 110
5 110 11100
6 101 11101
7 011 11110
8 111 11111
For code words 2, 3, and 4, the position of the 1 is coded as integer in the last two bins of the corresponding code word
For code words 5, 6, and 7, the position of the 0 is coded as integer in the last two bins of the corresponding code word
Not parametrizable (only one single v2v code)

## Slide 7: ‘Bin pipe’ codes
Primary code is based on two truncated unary codes (one with all bins inverted)
Secondary code equals primary except that two code words are interchanged
Example for parameter n (max. unary length) equal 4:
Index Primary Secondary
1 0000 111
2 0001 0001
3 001 001
4 01 01
5 10 10
6 110 110
7 111 0000
These bins are ‚piped through‘ (are written without change)

## Slide 8: Systematic code setup
Four bin pipe codes, the three bin code, and four unary to Rice codes are used
One additional bypass bin encoder is used for equiprobable bins
 Totally, 10 coders are used

## Slide 9: Theoretical evaluation of systematic v2v codes
Excess code rate in terms of percentage overhead
Envelope can be seen as characteristic curve of the code setup

## Slide 10: Theoretical evaluation of TMuC v2v codes
Excess code rate in terms of percentage overhead
Envelope can be seen as characteristic curve of the code setup

## Slide 11: New probability interval mapping
A new mapping of CABAC states to v2v codes is derived by evaluating the crossing points of the excess code length curves
States | v2v code
[0, 1] | uncoded
2 | bin pipe 5
[3, 4] | bin pipe 4
[5, 9] | bin pipe 3
[10, 14] | bin pipe 2
[15, 21] | three bin code
[22, 31] | unary to rice 2
[32, 44] | unary to rice 3
[45, 61] | unary to rice 4
62 | unary to rice 5

## Slide 12: Efficient implementations using counters
All systematic v2v codes can be implemented using counters
One byte per coder is sufficient to represent the code word currently being processed
Example for unary to rice codes:
  A counter stores the number of 0s of the unary code word
  A further bin is used to store whether the unary code word is truncated or not
  When a bin is requested by the parser, the counter is decremented and a bin is returned

## Slide 13: Experimental computational complexity evaluation
 | Operations per bin |  | 
 | M decoder | PIPE decoders | 
 |  | Systematic v2v codes | TMuC v2v codes
table lookup | 0.86 | 0.86 | 2.12
shift | 2.18 | 0.17 | 1.63
logical | 1.59 | 0.22 | 1.00
add/substraction | 1.13 | 0.34 | 1.42
decision | 2.21 | 1.71 | 1.42
read | 0.33 | 0.65 | 0.85
Sum | 8.30 | 3.95 | 8.44
Average number of operations per bin is computed based on all bins of the test set

## Slide 14: Memory requirements comparison
 | Memory requirement | 
 | M decoder | PIPE decoder systematic v2v codes
table size | 4 x 64 | 1 x 64
register size | Value - 2 Byte | 9 Byte (1 Byte per coder)
 | Range - 2 Byte | 

## Slide 15: Experimental coding efficency evaluation: systematic v2v codes
 | Intra HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.38 | 0.38 | 0.38
Class B | 0.40 | 0.40 | 0.40
Class C | 0.37 | 0.36 | 0.36
Class D | 0.39 | 0.39 | 0.38
Class E | 0.41 | 0.41 | 0.41
All | 0.39 | 0.39 | 0.39
 | Random Access HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.41 | 0.40 | 0.40
Class B | 0.48 | 0.48 | 0.48
Class C | 0.47 | 0.47 | 0.47
Class D | 0.60 | 0.60 | 0.60
Class E |  |  | 
All | 0.50 | 0.50 | 0.50
 | Low Delay HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.50 | 0.50 | 0.49
Class C | 0.49 | 0.49 | 0.49
Class D | 0.63 | 0.63 | 0.63
Class E | 0.76 | 0.76 | 0.75
All | 0.58 | 0.58 | 0.58
All BD rates are obtained by coding the exact same bin sequences

## Slide 16: Experimental coding efficency evaluation: TMuC v2v codes
 | Intra HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.17 | 0.17 | 0.17
Class B | 0.17 | 0.18 | 0.18
Class C | 0.16 | 0.16 | 0.16
Class D | 0.18 | 0.18 | 0.18
Class E | 0.19 | 0.19 | 0.19
All | 0.17 | 0.17 | 0.17
 | Random Access HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.20 | 0.19 | 0.19
Class B | 0.25 | 0.24 | 0.24
Class C | 0.26 | 0.25 | 0.25
Class D | 0.39 | 0.38 | 0.38
Class E |  |  | 
All | 0.28 | 0.28 | 0.28
 | Low Delay HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.26 | 0.26 | 0.26
Class C | 0.26 | 0.26 | 0.26
Class D | 0.39 | 0.38 | 0.39
Class E | 0.51 | 0.50 | 0.50
All | 0.34 | 0.34 | 0.34
All BD rates are obtained by coding the exact same bin sequences

## Slide 17: Summary
Novel set of v2v codes
  Only 10 instead of 12 v2v codes (as in TMuC) needed
Low complexity
  One single byte is sufficient to store the coding state of each bin encoder or decoder
  Number of operations per bin is lower than for initial PIPE v2v codes or the M coder
Good R-D performance
  Averaged BD rate increase lower than 0.5% relative to CABAC