## Slide 1
<number>
<number>
JCTVC-D385: Adaptive Loop Filtering Using Multiple Filter Shapes
Faouzi Kossentini
4th JCT Meeting in Daegu, KR
20-28 January 2011

## Slide 2: Outline
<number>
<number>
Motivation
Proposed Technique: ALF using two filter shapes
Simulation Results
Performance Analysis
Complexity Analysis
Conclusion and Recommendation

## Slide 3: Motivation
<number>
<number>
TMuC 0.9 ALF worst-case decoder complexity is too high:
  21 coefficients for 9x9 diamond-shaped filter
  21 multiplies & 41 adds per filtered sample
Single filter shape limits coding efficiency.

## Slide 4: Proposed Technique
<number>
<number>
Two sets of filters
  Set #1: 7x7 diamond-shaped filters
  Set #2: 13x13 cross-shaped filters
For each picture, select among following options
  Frame-based ALF using Filter Set #1
  Frame-based ALF using Filter Set #2
  CU-based ALF using Filter Set #1
  CU-based ALF using Filter Set #2
  No ALF filtering

## Slide 5: Proposed Technique
<number>
<number>

## Slide 6: Proposed Technique
<number>
<number>

## Slide 7: Simulation Results
<number>
 | Low Delay HE |  | 
 | Y BD-Rate | U BD-Rate | V BD-Rate
Class A | - | - | -
Class B | -0.4 | -0.1 | -0.1
Class C | -0.6 | -0.4 | -0.5
Class D | -2.2 | -1.5 | -0.8
Class E | -0.3 | 0.2 | 0.0
All | -0.9 | -0.5 | -0.4

## Slide 8: Simulation Results
<number>
 | Random Access HE |  | 
 | Y BD-Rate | U BD-Rate | V BD-Rate
Class A | 0.2 | 0.1 | 0.1
Class B | 0.0 | -0.1 | -0.2
Class C | -0.4 | -0.1 | 0.1
Class D | -1.2 | -0.1 | -0.1
Class E | - | - | -
All | -0.4 | -0.1 | -0.1

## Slide 9: Simulation Results
<number>
 | Intra Only HE |  | 
 | Y BD-Rate | U BD-Rate | V BD-Rate
Class A | 0.2 | 0.0 | 0.0
Class B | 0.1 | 0.0 | 0.0
Class C | 0.1 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0
Class E | 0.2 | -0.1 | -0.1
All | 0.1 | 0.0 | 0.0

## Slide 10: Performance Analysis
<number>
Coding gains relative to TMuC 0.9
  ~0.9% BD-Rate for Low Delay HE
  ~0.4% in BD-Rate for Random Access HE
Coding gains decrease for larger sequences
  The use of two shapes does not provide enough adaptivity for very large video pictures.
  One solution is to split each picture into multiple slices and then generate diamond- and cross-shaped ALF filters for each slice.

## Slide 11: Complexity Analysis
<number>
TMuC 0.9 ALF requires a maximum of 21 multiplications and 41 additions.

## Slide 12: Complexity Analysis
<number>
The new ALF requires a maximum of 13 multiplications and 25 additions.

## Slide 13: Complexity Analysis
<number>
Profile | Enc Time [%] | Dec Time [%]
Low Delay HE | 107 % | 102% (91%)
Random Access HE | 109 % | 100% (90%)
Intra Only | 125 % | 88% (87%)
Average decoding times for the new ALF are lower only for Intra (where mostly 9x9 diamond-shaped filters used in the TMuC 0.9).
Worst-case decoding time of the new ALF is ~90% of that of the TMuC 0.9 (estimated by using only 9x9 diamond-shaped filters).
New ALF does not increase encoding time substantially (except for Intra Only); Encoding time reduced using a parallel implementation.

## Slide 14: Complexity Analysis
<number>
Problem: Cross-shaped filter’s 13-tap vertical filter size too large for some applications
Solution: Reduce vertical size:
  Proposed technique (9 lines)
  Proposed technique (7 lines)

## Slide 15: Proposed Technique (9 Lines)
<number>
<number>

## Slide 16: Simulation Results (9 Lines)
<number>
 | Low Delay HE |  | 
 | Y BD-Rate | U BD-Rate | V BD-Rate
Class C | -0.4 | -0.3 | -0.4
Class D | -0.8 | -1.1 | -0.3
Class E | -0.1 | 0.0 | -0.1
All | -0.4 | -0.5 | -0.3

## Slide 17: Proposed Technique (7 Lines)
<number>
<number>

## Slide 18: Simulation Results (7 lines)
<number>
 | Low Delay HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | - | - | -
Class C | -0.2 | -0.2 | -0.1
Class D | -0.2 | -0.7 | 0.0
Class E | 0.7 | -0.2 | -0.3
All | 0.1 | -0.4 | -0.2

## Slide 19
Conclusion
Lower worst-case decoder complexity for non-Intra (~10%)
Lower average/worst-case decoder complexity for Intra (12%/13%)
Slightly higher encoding times (w/o a parallel implementation)
Parallel-friendly encoding algorithm
Improved coding efficiency (13, 9 lines)
  ~0.9% in BD-Rate for Low Delay HE (13 lines)
  ~0.4% in BD-Rate for Random Access HE (13 lines)
  ~ 0.4% in BD-Rate for Low Delay HE (9 lines)
Same coding efficiency (7 lines)
Recommendation
  Continue evaluation of ALF using multiple shapes for possible adoption into the HM.

## Slide 20: Simulation Results: Low Delay HE
<number>
Sequences |  | Proposed technique | Proposed technique (9 lines) | Proposed technique (7 lines)
S08 | Basketball Drill | 0.0 | 0.3 | -0.1
S09 | BQMall | -0.5 | -0.3 | -1.3
S10 | PartyScene | -1.9 | -1.4 | 0.0
S11 | RaceHorses | -0.2 | -0.2 | 0.3
S12 | BasketballPass | 0.2 | 0.2 | 0.3
S13 | BQSquare | -8.1 | -2.7 | -1.3
S14 | BlowingBubbles | -0.6 | -0.5 | -0.3
S15 | RaceHorses | -0.3 | -0.2 | 0.8
S16 | Vidyo1 | -0.4 | -0.3 | 0.0
S17 | Vidyo3 | -0.2 | 0.1 | 1.7
S18 | Vidyo4 | -0.4 | 0.0 | 0.4
 | Class C | -0.65 | -0.40 | -0.2
 | Class D | -2.20 | -0.80 | -0.2
 | Class E | -0.33 | -0.10 | 0.7
 | All | -1.06 | -0.43 | 0.1