## Slide 1: constrained intra source code implementation
JCTvc-D386
Rickard Sjöberg, jonatan samuelsson
ericsson AB

## Slide 2: summary
Constrained Intra has been part of all TMuC and HM specifications
It enables Intra macroblock refresh and may also be important for future scalability extensions
The BD-rate penalty of Constrained Intra is in the 1.5 to 2.0 percent range
It is not yet implemented in the source code
=> Ericsson decided to implement Constrained Intra
Our first target was to implement constrained intra exactly as it is done in AVC
But we found that Intra prediction in a quad-tree framework was undefined
  Incidentally, we choose the same Intra prediction scheme as document D094 from Panasonic
Otherwise, implementation impact of Constrained Intra is very small
  Changes to GetPUAbove(), GetPULeft() etc to add check for block types of neighboring blocks
  Changes to initAdiPattern() and initAdiPatternChroma() to check all neighboring blocks
We propose:
That Constrained Intra is implemented into HM
Either the NEC (D086) method or the Panasonic (D094) method
Ericsson volunteer to carefully cross-check the implementation

## Slide 3: Intra prediction method 1
Interpolation when two neighboring prediction pixels are available (p1+p2+1)>>1
Extrapolation when only one neighboring prediction pixel is available
Use (128 << increased_bit_depth) when no prediction pixels are available (e.g. first CU in a slice)
Identical to the D094 method

## Slide 4: Intra prediction method 2
Decisions taken on pseudo-PUs of same size as the current PU
If any Inter PU is found, all pseudo-PU pixels are marked not available for prediction
Identical to the D086 method

## Slide 5: summary
Our Proposal:
That Constrained Intra is implemented into HM
Either the D094 method or the D086 method
Ericsson volunteer to carefully cross-check the implementation
D094
D086

## Slide 6: results constrained intra on/off