## Slide 1: Improvement of AIS techniques by switching interpolation filters
Ehsan Maani
Ali Tabatabai

## Slide 2: Intra Smoothing
Adaptive Intra Smoothing
  Consists of adaptively applying low-pass (smoothing) filters to the reconstructed block boundaries before prediction
Different techniques
  High complexity mode decision search with PU-level signaling [JCTVC-A116]
  Fast mode decision with PU-level signaling [JCTVC-C302 ]
  Mode dependent smoothing (no signaling) [JCTVC-D282]
  Hybrid mode dependent (with signaling) [JCTVC-D282]

## Slide 3: Switching interpolation filters
All AIS techniques have two operating modes
  1) Filtering on:
    No change is proposed (Smoothing filtering, linear interpolation)
  2)Filtering off:
    A different interpolation method is proposed. Instead of the linear interpolation method used in TMuC 0.9 or in case (1) above, a set of 4-tap filters is proposed
    32 4-tap filters based on Cubic interpolation is proposed. One filter for each sub-pel location
full-pel
half-pel
quarter-pel
1/8th-pel
Each fractional-perl location has its own specific filter

## Slide 4: Implementation
When AIS flag for a block is set to off (no filtering), then:
  A different interpolation technique (a set of 4-tap filters) is used when interpolation is needed during the process of directional Intra prediction
    Traditionally, a 2-tap filter (linear) is used
When AIS flag is on
    Traditional 2-tap (linear) interpolation filters are used when needed
Method to find the AIS flag/Smoothing filter

## Slide 5: Results
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.5 | -0.6 | -0.7 | -1.3 | -0.8 | -0.8
Class B | -0.7 | -0.5 | -0.6 | -1.3 | -0.7 | -0.6
Class C | -0.4 | -0.4 | -0.4 | -0.6 | -0.5 | -0.6
Class D | -0.5 | -0.6 | -0.6 | -0.8 | -0.6 | -0.6
Class E | -0.8 | -0.8 | -1.0 | -1.8 | -0.9 | -0.8
All | -0.6 | -0.6 | -0.6 | -1.1 | -0.7 | -0.7
Enc Time[%] | 103% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
Table 3. Results of FIS with switching interpolation method.
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.7 | -0.7 | -0.9 | -1.6 | -0.8 | -0.9
Class B | -0.9 | -0.9 | -0.9 | -1.4 | -0.8 | -1.0
Class C | -0.6 | -0.6 | -0.7 | -0.9 | -0.6 | -0.7
Class D | -0.6 | -0.7 | -0.6 | -0.8 | -0.6 | -0.6
Class E | -1.2 | -1.2 | -1.2 | -2.0 | -1.2 | -1.0
All | -0.8 | -0.8 | -0.9 | -1.3 | -0.8 | -0.8
Enc Time[%] | 104% |  |  | 108% |  | 
Dec Time[%] | 101% |  |  | 102% |  | 
Table 5. Results of HIS with switching interpolation method.
HIS with switching interpolation method
FIS with switching interpolation method.