## Slide 1: Mode dependent residual coding
Peisong Chen, Rajan Joshi, Yufei Zheng, Muhammed Coban, Marta Karczewicz

## Slide 2: Introduction
In this contribution, we compare several different combinations of mode dependent transform and coefficient scan.

## Slide 3: 2-D separable transform (JCTVC-C080)
TransformIdx | Vertical 1D Transform | Horizontal 1D Transform
0 | KLT | DCT
1 | DCT | KLT
2 | DCT | DCT
3 | KLT | KLT
Four combinations of horizonal and vertical transforms
Map each intra prediction direction to a TransformIdx

## Slide 4: Combination 1: mode dependent scan
Three different scan orders: Zig-zag, horizontal and vertical scan
The selection of scan order depends on the transform block size and the spatial prediction direction. There is no signaling.

## Slide 5: Combination 2: signaled scan
Still three scan orders: zig-zag, horizontal and vertical.
The scan order is explicitly signaled.
The encoder has to test each scan order.

## Slide 6: Combination 3: transform and scan combination
Scan | Horizontal transform | Vertical transform
Zig-zag | Same as method 1 | 
Horizontal scan | KLT | DCT
Vertical scan | DCT | KLT

## Slide 7: Summary
Combination | BD-rate |  |  | Encoding Time | Decoding Time
 | Y | U | V |  | 
One KLT+ one DCT with fixed scan | -2.3 | -2.6 | -2.6 | 106% | 106%
Scheme 2 | -2.6 | -3.0 | -2.9 | 135% | 111%
Scheme 3 | -3.1 | -1.9 | -1.9 | 296% | 112%

## Slide 8: Mode Mapping
Vertical T2 Horizontal T1
Vertical T1 Horizontal T2
Vertical T1 Horizontal T1
DC mode Vertical T2 Horizontal T2