## Slide 1: Extension of uni-prediction simplification in B slices
JCTVC-D421 / m19400
Y. Suzuki & TK Tan
NTT DOCOMO, Inc.

## Slide 2: Summary
Background
  Uni-prediction simplification in B slices was adopted at the last meeting based of JCTVC-C278 and JCTVC-C285
  Pred_L1 is removed from inter_pred_idc when List 0 and List 1 are identical.
    Syntax for inter_pred_idc changes depending on contents of List 0 and List 1
Proposed Extension
  Combine Pred_L0 and Pred_L1 into a single Pred_LC.
  Inter_pred_idc always indicate Bi-pred or Pred_LC, only.
  Affects entropy coding and encoder search only.
Benefits
  Cleaner solution and more general
  Remove redundancy in cases other than just when List 0 and List 1 are identical.
    List 0 and List 1 have same elements but in different order,
    List 0 and List 1 have overlapping entries
    List 1 is a subset of List 2, and vice-versa.
Results
  -0.3% to -1.0% BD-rate improvements
  6% to 30% reduction in encoding time. (encoder only option is possible)
Conclusions
  This proposal is a generalization of the current HM method and it is proposed that the simplification be extended with this proposal.

## Slide 3: Creating a Combine List

## Slide 4: OLD (C500) Common Conditions
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class B | 0.0 | 0.0 | -0.1 | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | -0.1
Class D | 0.0 | 0.0 | 0.2 | 0.0 | 0.0 | -0.1
Class E |  |  |  |  |  | 
All | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.0 | -0.2 | 0.0 | 0.0 | 0.0
Class C | 0.0 | -0.1 | 0.0 | 0.0 | 0.0 | 0.0
Class D | 0.0 | -0.6 | 0.5 | 0.0 | 0.0 | 0.0
Class E | 0.0 | 0.0 | -0.2 | 0.0 | 0.0 | 0.0
All | 0.0 | -0.1 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 102% |  | 

## Slide 5: 2 references in L0 and L1 – Random Access
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.8 | -2.3 | -2.3 | -1.6 | -1.8 | -1.6
Class B | -2.7 | -2.4 | -2.3 | -2.3 | -0.9 | -0.7
Class C | -2.4 | -1.7 | -2.0 | -2.9 | -1.8 | -1.7
Class D | -1.4 | -1.0 | -0.9 | -3.3 | -1.4 | -0.9
Class E |  |  |  |  |  | 
All | -2.2 | -1.8 | -1.8 | -2.6 | -1.4 | -1.1
Enc Time[%] | 150% |  |  | 179% |  | 
Dec Time[%] | 101% |  |  | 103% |  | 
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.0 | -2.7 | -2.7 | -2.1 | -2.1 | -2.1
Class B | -3.1 | -3.0 | -3.0 | -2.9 | -1.6 | -1.2
Class C | -2.5 | -2.0 | -2.2 | -3.2 | -2.2 | -2.0
Class D | -1.8 | -1.4 | -1.2 | -3.8 | -1.9 | -1.4
Class E |  |  |  |  |  | 
All | -2.5 | -2.3 | -2.3 | -3.1 | -1.9 | -1.6
Enc Time[%] | 137% |  |  | 158% |  | 
Dec Time[%] | 101% |  |  | 103% |  | 
Proposed extension with 2 ref in L0 & L1
vs.
HM0.9
JCTVC-C500
HM0.9 with 2 ref in L0 & L1
vs.
HM0.9
JCTVC-C500

## Slide 6: 4 ref in L0 and 2 ref in L1 – Random Access
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.1 | -2.8 | -2.6 | -1.4 | -2.0 | -1.8
Class B | -3.6 | -3.0 | -2.9 | -3.0 | -1.3 | -1.0
Class C | -3.0 | -2.3 | -2.5 | -3.4 | -1.9 | -1.9
Class D | -1.7 | -1.2 | -1.0 | -3.7 | -1.5 | -1.3
Class E |  |  |  |  |  | 
All | -2.7 | -2.3 | -2.2 | -3.1 | -1.6 | -1.4
Enc Time[%] | 204% |  |  | 251% |  | 
Dec Time[%] | 101% |  |  | 97% |  | 
Proposed extension with 4 ref in L0 & 2 ref in L1
vs.
HM0.9
JCTVC-C500
HM0.9 with 4 ref in L0 & 2 ref in L1
vs.
HM0.9
JCTVC-C500
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.6 | -3.5 | -3.4 | -2.3 | -2.7 | -2.5
Class B | -4.2 | -3.6 | -3.6 | -3.7 | -2.1 | -1.8
Class C | -3.3 | -2.8 | -2.9 | -4.0 | -2.6 | -2.4
Class D | -2.3 | -1.6 | -1.5 | -4.6 | -2.1 | -1.9
Class E |  |  |  |  |  | 
All | -3.3 | -2.8 | -2.8 | -3.9 | -2.3 | -2.1
Enc Time[%] | 191% |  |  | 235% |  | 
Dec Time[%] | 101% |  |  | 98% |  | 

## Slide 7: 4 ref in L0 and 2 ref in L1 – Low Delay
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -2.5 | -3.0 | -3.3 | -2.9 | -3.5 | -4.1
Class C | -2.4 | -2.2 | -2.2 | -3.6 | -4.8 | -4.7
Class D | -2.6 | -3.6 | -2.7 | -5.2 | -6.5 | -6.6
Class E | -4.2 | -5.9 | -7.2 | -3.8 | -2.7 | -4.1
All | -2.8 | -3.5 | -3.6 | -3.8 | -4.4 | -4.9
Enc Time[%] | 163% |  |  | 183% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
Proposed extension with 4 ref in L0 & 2 ref in L1
vs.
HM0.9
JCTVC-C500
HM0.9 with 4 ref in L0 & 2 ref in L1
vs.
HM0.9
JCTVC-C500
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -2.8 | -3.1 | -3.4 | -3.6 | -3.9 | -4.3
Class C | -3.0 | -2.8 | -2.8 | -4.7 | -5.5 | -5.6
Class D | -3.5 | -4.1 | -3.4 | -6.4 | -7.1 | -7.5
Class E | -4.8 | -7.4 | -8.4 | -5.0 | -3.4 | -4.8
All | -3.4 | -4.1 | -4.2 | -4.8 | -5.0 | -5.5
Enc Time[%] | 120% |  |  | 129% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 8: Summary Results
 | 2 ref in L0, 2 ref in L1 |  | 4 ref in L0, 2 ref in L1 |  |  | 
 | Random access | Random access LoCo | Random access | Random access LoCo | Low delay | Low delay LoCo
Average Y BD-rate | -0.3% | -0.5% | -0.6% | -0.8% | -0.6% | -1.0%
Enc Time[%] | 91% | 88% | 94% | 94% | 74% | 70%