## Slide 1: BoG on 3.1 Skip/Direct/Merge
W-J. Han & TK Tan

## Slide 2: BoG on 3.1 Skip/Direct/Merge
BoG report JCTVC-D441
  T. K. Tan, W.-J. Han, B. Bross , J. Jung, K. McCann, Y. Suzuki, G. Clare, H. Schwarz, J. Chen
Background of things already agreed in Group A
  Disable NxN PU split for CUs > 8x8
  Direct mode off
  Temporal Center
Topics
  Implementing CU partial merge (JCTVC-D233) using PU Merging
  Further discussion on 3.1.e vs. 3.1.t

## Slide 3: Implementing CU partial merge (JCTVC-D233) using PU Merging
Perform simulation with
  3.1.e (PU merging, Mrg Skip) &
  3.1.t (PU merging, AMVP Skip)
Apply restrictions
  Encoder only
  Encoder & Decoder
Result:
  All variants achieve the same encoder speedup as JCTVC-D233
  Encoder only change has a loss up to 1.5%
Recommends
  To adopt PU partial merging (PU level merge with restrictions)
  When CU is split into 2NxN or Nx2N then
    the first PU is inferred to be merged
    the second PU signaling follows JCTVC-D314 (allows either merge flag or MV coding)

## Slide 4: Further discussion on 3.1.e vs. 3.1.t
The difference between 3.1.e and 3.1.t is that in 3.1.t skip is enabled with derivation of the MV from MV Coding, in 3.1.e, there is no skip mode but there is a merge with no residual.
Recommends to create a CE on MV Derivation Process
  Reference of the CE
    Take 3.1.t (Direct off is included)
    Partial Merge (encoder and decoder restriction)
    Disable NxN PU split
    Temporal Center