## Slide 1: Requirements of very low delay applications (JCTVC-E061, m19571)
5th JCT-VC meeting, Geneva/Switzerland
2011/3/16-23
K.Kazui, S.Shimada, J.Koyama, and A.Nakagawa

## Slide 2: Outline
We have proposed the new high-level syntax and semantics for minimizing the loss of coding efficiency in very low delay coding.
The proposed semantics guarantees the correct reconstruction of pictures after a recovery point by disabling in-loop filter at the region boundary between an area refreshed by an intra MB line and a non-refreshed area.
This contribution shows by simulation that significant degradation remains several refresh cycles after the recovery point if in-loop filter is enabled at the region boundary.
Real-time applications such as on-the-spot broadcasting require correct reconstruction of pictures just after the recovery point. Significant degradation caused by in-loop filter at the region boundary is not allowed.
The proposed syntax and semantics fulfill the requirement with the minimal loss of coding efficiency.
We request to start discussing the support of very low delay coding in HEVC.

## Slide 3: Background
We stated the need and the merit of the new high-level syntax and semantics for minimizing the loss of coding efficiency in very low delay coding.
  The new syntax describes the region boundary between a refreshed area refreshed by an intra MB line and a non-refreshed area in a picture.
  The new semantics disables in-loop filter (including deblocking filtering and ALF) at the region boundary in order to avoid degradation of reconstructed pictures caused by the contamination of refreshed pixels from non-refreshed pixels.
  The conventional multiple slices insertion scheme also can disable in-loop filter at the region boundary. However, the coding efficiency degrades because the scheme requires the insertion of a slice header at each MB line.
One of the chairpersons commented on the property of correct reconstruction at the 4th meeting. (Excerpt from JCTVC-D500)
  In JCTVC-D052, the benefit is shown relative to a method that disable the loop and deblocking filters globally. It was suggested to also compare against a scheme where the filter is switched on (i.e. a little bit of drift would occur, which may not be too severe as it is due to spatial filtering). In that case, this would not imply normative changes and an SEI message would be sufficient.

## Slide 4: Simulation
We simulated the degradation of reconstructed pictures after a recovery point when in-loop filtering at the region boundary is enabled.
Software
  The vertical intra MB line refresh scheme is implemented onto HM0.9 software. The proposed new syntax and semantics are not included.
  For encoding, the search range of motion estimation and the direction of intra prediction are restricted.
  For decoding, all reconstructed pixels in the first IDR picture (POC=0) are reset to 0 in order to simulate the recovery from the second picture (i.e. the entry of the first recovery point).
  In-loop filter is enabled by setting configuration parameters.
Restriction of search range in ME
Restriction of direction of intra prediction

## Slide 5: Results (1/5)
Frame@POC 1 (Entry of 1st Recovery point)
Original input
Deblocking On, ALF Off
Low delay mode QP 22 Refresh cycle = 30 (=1920/64)
Deblocking On, ALF On
refresh direction
Vertical Intra LCU line

## Slide 6: Results (2/5)
Frame@POC 30 (End of 1st refresh cycle)
Original input
Deblocking On, ALF Off
Deblocking On, ALF On

## Slide 7: Results (3/5)
Frame@POC60 (End of 2nd refresh cycle)
Original input
Deblocking On, ALF Off
Deblocking On, ALF On

## Slide 8: Results (4/5)
Frame@POC120 (End of 4th refresh cycle)
Original input
Deblocking On, ALF Off
Deblocking On, ALF On

## Slide 9: Results (5/5)
8
Copyright 2010 FUJITSU LIMITED
Frame@POC120 (End of 4th refresh cycle)
Original input
Deblocking On, ALF Off
Deblocking On, ALF On
Original input

## Slide 10: Observation
  Significant degradation remains several refresh cycles after the recovery point.

## Slide 11: Requirement of broadcasting application
Very low delay coding is used for on-the-spot broadcasting.
  Live report from the scene of an event
  Road race program, etc
On-the-spot broadcasting uses a field pickup unit to transmit the video of a "spot" over a wireless channel to a TV station.
  Bit error is unavoidable when a wireless channel is used.
The correct reconstruction of pictures just after the recovery point is necessary.
  In particular, broadcasting requires high-quality video transmission.
  This requirement is also applied to other real-time applications such as TV-conference over a wireless channel.
Degradation of reconstructed pictures when in-loop is enabled at the region boundary is not allowed in real-time video transmission applications.

## Slide 12: Requirement of broadcasting application (Cont.)
The proposed new high-level syntax and semantics satisfy the need of real-time video transmission applications.
  Correct reconstruction of pictures just after the recovery point is guaranteed.
Coding gain of the proposed scheme over conventional schemes is significant.
  VS. multiple slices insertion scheme. (JCTVC-C021)
    9.0% (64x64 LCU) and 15.9% (32x32 LCU) on average.
    11.5% (64x64 LCU) and 19.8% (32x32 LCU) for BQMall sequence.
  VS. in-loop filter off (JCTVC-D052)
    6% on average
    13.8% for Kimono sequence

## Slide 13: Conclusion
The proposed scheme guarantees the correct reconstruction of pictures after a recovery point. This feature is necessary for real-time applications over a wireless channel such as on-the-spot broadcasting.
We request to start discussing the support of very low delay coding in HEVC.
  Generalized slice scheme proposed in the 4th meeting has the similar functionality to the proposed scheme. However, the mechanism for interoperable very low delay coding is still lacking
    The scanning order of a LCU for entropy coding (i.e. raster-scan in a picture)
    The new buffer model which defines the decoding time of a group of LCUs.