## Slide 1: Improvement on simplified motion vector prediction (JCTVC-E062, m19572)
5th JCT-VC meeting, Geneva/Switzerland
2011/3/16-23
K.Kazui, S.Shimada, J.Koyama, and A.Nakagawa

## Slide 2: Outline
We propose the improvement of SMVP (Simplified MV Prediction) in HM2.0.
The proposed scheme enhances the deviation process of the MV predictor candidates from spatially-neighboring PU partitions.
  The original SMVP scheme selects a MV with the same reference index of the target MV as a candidate. If there is no such a MV in spatially-neighboring PU partitions, a spatial MV predictor candidate is considered as “not available”.
  On the contrary, the proposed scheme selects a MV with the different reference index from the target MV only if there is no a MV with the same reference index of the target MV in spatially-neighboring PU partitions.
  The proposed scheme does not require syntax change.
  Additional computation complexity is small.
The coding gain is 0.5%-0.8% in random access configurations
  Large coding gain is obtained for sequences with frequent occlusion of background.
  4.2-4.5% for Keiba sequence

## Slide 3: SMVP (Simplified Motion Vector Prediction)
SMVP was adopted in HM2.0.
  Original contributions are JCTVC-B094 and JCTVC-D231.
SMVP simplifies the deviation process of MV predictor candidates.
  The maximum number of candidates is reduced to three.
    MVtemp: Centered Temporal Predictor proposed in JCTVC-D164
    MVleft: MV in one of the neighboring PUs left to the current PU
    MVtop: MV in one of the neighboring PUs above the current PU
Mvleft and MVtop are searched from the groups of neighboring PU left to/above the current PU.
  Only a MV with the same reference index of the target MV is chosen.
The search direction of MVleft and MVtop

## Slide 4: Problem of SMVP
The number of MV predictor candidates is reduced when there is no MV with the same reference index of the target MV in the neighboring PUs.
As the result, the coding efficiency of a MV decreases.
Example: MVleft is not available because the reference index of MVs in left PUs is L0[0], while the reference index of the MV in the current PU is L0[1].

## Slide 5: Outline of the proposed scheme
MVs with different reference index from the target MV is chosen as a candidate only if the reference indexes of all MVs in neighboring are different from that of the target MV.
  The same PU search direction of SMVP is used.
  The chosen MV is scaled according to POC value of its reference picture.
Coding efficiency of a MV improves without significant increase of computational complexity.
Example: The scaled MV of left PU, ( -2x, 0 ), is chosen as MVleft

## Slide 6: The proposed scheme in detail
Priority is assigned to all MVs in neighboring PUs according to the reference indexes of those MVs. A MV with highest priority is chosen as a candidate.
  A MV with the reference index closer to that of the target MV is prioritized.
  A MV with different direction can be a candidate.
Example of priority of a MV according to its reference index
The candidate indexes of MVleft and MVtop is swapped when all of the following conditions are met.
  MVtemp is not available.
  Priority of MVleft is less than 0.
  Priority of MVtop is 0

## Slide 7: Flowchart
The flowchart of the deviation process of MVleft

## Slide 8: Simulation result
High coding gains for sequences with frequent occlusion of background objects.
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Keiba (416x240, 30Hz) | -4.2 | -4.0 | -3.8 | -4.5 | -4.1 | -3.7
SteamLocomotive | -1.6 | -2.6 | -3.6 | -2.2 | -2.2 | -2.4
RaceHorses (ClassC) | -0.8 | -1.0 | -1.0 | -1.2 | -1.4 | -1.3

## Slide 9: Simulation result (cont.)
Proposal vs. HM2.0 |  |  |  |  |  | 
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.6 | -1.1 | -1.4 | -1.0 | -1.3 | -1.4
Class B | -0.4 | -0.3 | -0.2 | -0.7 | -0.5 | -0.4
Class C | -0.6 | -0.7 | -0.7 | -0.8 | -0.7 | -0.7
Class D | -0.5 | -0.6 | -0.6 | -0.7 | -0.7 | -0.6
Class E |  |  |  |  |  | 
All | -0.5 | -0.6 | -0.7 | -0.8 | -0.8 | -0.8
Enc Time[%] | 104% |  |  | 102% |  | 
Dec Time[%] | 103% |  |  | 105% |  | 
Proposal vs. HM2.0 |  |  |  |  |  | 
 | Low Delay |  |  | Low Delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | 0.2 | -0.1 | -0.3 | -0.2 | 0.2
Class C | -0.1 | 0.0 | 0.0 | -0.5 | -0.3 | -0.3
Class D | -0.2 | -0.3 | -0.1 | -0.2 | 0.4 | 0.1
Class E | -0.5 | -0.2 | -0.2 | -0.7 | -0.1 | -0.4
All | -0.2 | 0.0 | -0.1 | -0.4 | -0.1 | -0.1
Enc Time[%] | 110% |  |  | 103% |  | 
Dec Time[%] | 103% |  |  | 104% |  | 
0.5-0.8% coding gain in random access configurations

## Slide 10: Simulation result (cont.)
Measurement of the encoding time increment and the decoding time increment may be inaccurate because the simulation was done in a cluster environment.
Additional simulation shows that the encoding time increment is 3% and the decoding time increment is 1%.
  All simulations were done sequentially in one CPU.
  The lengths of all sequences are reduced to 2GOPs (i.e. 2 seconds) because of time constraints.
  The option “-o” is omitted for measurement of the decoding time increment.
Further evaluation is necessary.

## Slide 11: Conclusion
The proposed scheme improves the deviation process of the MV predictor candidates in HM2.0.
Coding gain is 0.5-0.8% on average, up to 4.2-4.5%.
  Large coding gain is obtained for sequences with frequent occlusion of background objects.
We request to evaluate the proposed scheme in a CE.
  Further evaluation of computational complexity is necessary because the simulation was executed in a cluster.