## Slide 1: CE5: Adaptive Coding of InterPredMode Syntax Element (JCTVC-E072)
Wen Zhang, Ming LI, Ping Wu

## Slide 2: Previous work
In JCTVC-D275, an adaptive coding method is proposed for inter prediction modes related syntax elements.
A syntax element named pred_mode_coding_type is introduced to P/B-slice header to indicate different coding types used in current slice to code the syntax elements of InterPredMode.
Coding type is defined as type of coding order of the InterPredMode related elements.
The encoder determines pred_mode_coding_type for the current slice according to the statistical results of the occurrence of the inter-frame prediction modes obtained from the previous coded slices.

## Slide 3: Improvement
Based on HM2.0, CU split flag is involved in this adaptive coding method with pred_mode_coding_type defined as
SKP_MRG_TER_TRA | Coding SkipFlag first, then MergeFlag, InterFlag
SKP_TER_MRG_TRA | Coding Skipflag first, then InterFlag, MergeFlag
SKP_TRA_MRG_TER | Coding Skipflag first, then IntraFlag, MergeFlag
MRG_SKP_TER_TRA | Coding MergeFlag first, then SkipFlag, InterFlag
MRG_TER_SKP_TRA | Coding MergeFlag first, then InterFlag, SkipFlag
MRG_TRA_SKP_TER | Coding MergeFlag first, then IntraFlag, SkipFlag
TER_SKP_MRG_TRA | Coding InterFlag first, then SkipFlag, MergeFlag
TER_MRG_SKP_TRA | Coding InterFlag first, then MergeFlag, SkipFlag
TER_TRA_SKP_MRG | Coding InterFlag first, then IntraFlag, SkipFlag
TRA_SKP_MRG_TER | Coding IntraFlag first, then SkipFlag, MergeFlag
TRA_MRG_SKP_TER | Coding IntraFlag first, then MergeFlag, SkipFlag
TRA_TER_SKP_MRG | Coding IntraFlag first, then InterFlag, SkipFlag

## Slide 4
Moreover, CU split flag is jointly coded with the InterPredMode flags, which employs the coding types indicated by split_flag_coding_type as below
The coding order of the split flag is signaled based on the already determined coding order of InterPredMode flags among different quad-tree layers of CU.
SPT_FLAG_1ST | SplitFlag in 1st coding order of inter prediction mode
SPT_FLAG_2ND | SplitFlag in 2nd coding order of inter prediction mode
SPT_FLAG_3RD | SplitFlag in 3rd coding order of inter prediction mode
SPT_FLAG_END | SplitFlag in last coding order of inter prediction mode

## Slide 5: Slice header syntax
slice_header( ) { | C | Descriptor
first_lctb_in_slice | 2 | ue(v)
slice_type | 2 | ue(v)
pic_parameter_set_id | 2 | ue(v)
frame_num | 2 | u(v)
if( IdrPicFlag ) |  | 
idr_pic_id | 2 | ue(v)
pic_order_cnt_lsb | 2 | u(v)
if( slice_type = = P ¦ ¦ slice_type = = B ) { |  | 
pred_mode_coding_type | 2 | ue(v)
split_flag_coding_type_depth0 | 2 | ue(v)
split_flag_coding_type_depth1 | 2 | ue(v)
split_flag_coding_type_depth2 | 2 | ue(v)
num_ref_idx_active_override_flag | 2 | u(1)

## Slide 6: Experimental Results
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | #VALUE! | #VALUE! | #VALUE! | -0.1 | -0.1 | -0.1
Class B | #VALUE! | #VALUE! | #VALUE! | 0.2 | 0.1 | 0.1
Class C | #VALUE! | #VALUE! | #VALUE! | -0.1 | 0.0 | 0.0
Class D | #VALUE! | #VALUE! | #VALUE! | -0.4 | -0.3 | -0.2
Class E |  |  |  |  |  | 
All | #VALUE! | #VALUE! | #VALUE! | -0.1 | -0.1 | 0.0
Enc Time[%] | #NUM! |  |  | 100% |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | -0.2 | -0.3 | 0.0
Class C | #VALUE! | #VALUE! | #VALUE! | -0.5 | -0.3 | -0.4
Class D | #VALUE! | #VALUE! | #VALUE! | -0.6 | -0.7 | -0.4
Class E | #VALUE! | #VALUE! | #VALUE! | 0.1 | -0.4 | -0.3
All | #VALUE! | #VALUE! | #VALUE! | -0.3 | -0.4 | -0.3
Enc Time[%] | #NUM! |  |  | 100% |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 

## Slide 7: Conclusions
In this document, an alternative adaptive coding method for InterPredMode information is proposed, which works at slice level.
As demonstrated by the experimental results, the proposed method achieves an average efficiency improvement of 0.2% with none computational complexity increment/decrement.
It is recommended to further study this syntax elements adaptive coding at slice or frame level in a CE or AHG.
We would like to thank Qualcomm for their cross-check work.