## Slide 1: Mode Dependent 2-step Transform for Intra Coding
Youji Shibahara
Takahiro Nishi
Panasonic Corporation
JCTVC-E074
5th JCT-VC Meeting: Geneva, CH, 16-23 March, 2011

## Slide 2: Introduction
The KLT which is designed for intra prediction residual is an effective technology in terms of coding efficiency.
However, its complexity is higher than DCT’s in terms of number of operation and encoder/decoder software runtime.
This contribution presents an approach for the unification of Mode Dependent Transform and 2 step transform, which encoding / decoding runtimes are comparable with those of HMV2 software
<number>

## Slide 3: Proposed Method (1)
2-step Transform
  Used for 8x8, 16x16 and 32x32 transform blocks
  First Transform is either of Chen-DCT or AVC transform.
  Second transform is 4x4 KLT, and it is applied to low frequency component.
   Reduction of number of operation
Mode Dependent
  2nd KLT is controlled according to the table on intra prediction mode.
  No explicit signaling to select 2nd KLT matrix.
  No need for additional RD loop in encoder
   Reduction of encoding run time
<number>

## Slide 4: Proposed Method (2)
DDST model based 2nd transform matrix
  The transform matrix is defined based on optimal DST model
  The covariance matrix for 2nd KLT is derived by M2 = T M1 TT
    M1 is the covariance matrix presented in JCTVC-B24 (I2R) and JCTVC-C108(Samsung)
    M1 is modified to have a gentle sloop, 50%.
  One matrix for all large transform blocks.
    The matrix which is designed for transform 8x8 block are used for other larger transform blocks, 16x16 and 32x32.
   Utilization of the study of optimal transform for intra residual
Adaptive DST/DCT transform is used for 4x4 transform block
  2-step transform is not used, since DST 4x4 is low complex
    The number of operation / block is O(N^3). N is a width of transform block
    But its for 4x4 block is smallest in all transform block sizes.
<number>

## Slide 5: Experimental Results
Table below shows results of proposed method with reference to HM version 2 (negative BD-rate value indicates gain).
<number>
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.2 | -1.3 | -1.2 | -1.6 | -0.5 | -0.4
Class B | -0.9 | -1.0 | -1.1 | -1.5 | -0.7 | -0.7
Class C | -1.1 | -1.2 | -1.1 | -1.7 | -1.0 | -1.0
Class D | -1.1 | -1.0 | -1.0 | -1.6 | -0.8 | -0.8
Class E | -1.7 | -2.2 | -2.0 | -2.4 | -1.0 | -1.3
All | -1.1 | -1.3 | -1.2 | -1.7 | -0.8 | -0.8
Enc Time[%] | 101 % |  |  | 104 % |  | 
Dec Time[%] | 102 % |  |  | 105 % |  | 
 | Random Access |  |  | Random Access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.6 | -0.3 | -0.5 | -0.7 | -0.2 | 0.1
Class B | -0.4 | -0.4 | -0.4 | -0.7 | -0.2 | -0.2
Class C | -0.6 | -0.6 | -0.5 | -0.8 | -0.5 | -0.4
Class D | -0.5 | -0.4 | -0.3 | -0.7 | 0.1 | -0.2
Class E |  |  |  |  |  | 
All | -0.5 | -0.4 | -0.4 | -0.7 | -0.2 | -0.2
Enc Time[%] | 100 % |  |  | 100 % |  | 
Dec Time[%] | 100 % |  |  | 100 % |  | 

## Slide 6: Comparison with DST8x8 (1)
50% reduction of total operation count
    Reduced to 13 % multiply operation count
    Reduced to 52 % total operation count
Proposed MD 2step | E098
Mults | 128
Adds | 768
Shifts | 368
Total | 1264
Reference Adaptive DST | E074 | E125
Mults | 1024 | 
Adds | 1024 | 
Shifts | 352 | 
Total | 2400 | 
 Large complexity reduction to 1step adaptive DST/DCT

## Slide 7: Comparison with DST8x8 (2)
Comparable performance
Reference Adaptive DST | E074 | E125
4x4 | DST | DST
8x8 | DST | DST
16x16 | - | -
32x32 | - | -
Gain @ Intra HE | 0.9 | 1.0
Gain @ Intra LC | 1.7 | 1.8
Proposed MD 2step | E098
4x4 | DST
8x8 | MD 2step
16x16 | MD 2step
32x32 | MD 2step
Gain @ Intra HE | 1.1
Gain @ Intra LC | 1.7
 Comparable performance to 1step adaptive DST/DCT

## Slide 8: Conclusions
This contribution proposes a low complexity unification of Mode Dependent Transform and 2-step transform for large transform blocks.
  The increase of encoding runtime can be small by mode dependency
  The increase of number of operation can be small by 2-step transform
  It provides 1.1% and 1.7% gain for Intra HE and Intra LC
We recommend JCT-VC to adopt the mode dependent 2-step transform for large transform blocks (8x8-32x32) into HM.
<number>

## Slide 9: Thank you

## Slide 10: Proposed Method (3)
Bit-width: 32 bit
Memory requirement:
  one 4x4 7bit transform matrix for large blocks
  one 4x4 7bit transform matrix for 4x4 blocks
  one 34 2bit array. (same table is already included in HMV2)
  No additional de-Quantization table.
Operation other than transform
  No additional operation for norm adjusting
    The multiply of de-quantization table is applied against the input of inverse 1st (core) transform. It is not changed from the HM dataflow.
  Adaptive shift up/down operation
    There were two shift operations to be applied. 1st one is a shift up for the de-Quantization, (QP %6) and 2nd one is a shift down for the reduction of inverse 2nd transform output. They are canceled each other and the shift up/down is done once according to the resulting relative number
  Conditional shift down
    It is invoked when both horizontal and vertical inverse 2nd transform are done.
<number>