## Slide 1: CE12 Subtest 1: Improved Deblocking Filter
Jicheng An, Qian Huang, Xun Guo, Yu-Wen Huang and Shawmin Lei
MediaTek Inc.
Presented by Xun Guo
5th JCT-VC Meeting in Geneva
16-23 March, 2011
Notes: <number>

## Slide 2: Overall Summary
An improved deblocking filter (IDF) is proposed
  Modified luma deblocking filter
  Modified chroma deblocking filter
BD-rate reductions
  Y component (1.2% on average)
    1.3%, 1.5%, 0.9%, 1.1%, 0.9%, 1.2% for HE-AI, LC-AI, HE-RA, LC-RA, HE-LD and LC-LD
  U component (1.8% on average)
    1.4%, 3.0%, 1.8%, 1.8%, 0.7%, 1.8% for HE-AI, LC-AI, HE-RA, LC-RA, HE-LD and LC-LD
  V component (1.7% on average)
    1.6%, 3.4%, 0.7%, 1.9%, 0.9%, 1.9% for HE-AI, LC-AI, HE-RA, LC-RA, HE-LD and LC-LD
No encoding and decoding time increase
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 3: Outline
Introduction
Proposed IDF algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 4: Deblocking Filter in HM2.0
Filtering process is based on 8x8 block
Filtering decision
  Determine whether a boundary should be filtered
  Only the pixels of line 2 and line 5 are used
Filter selection
  Determine whether a weak filter or a strong filter is used
  Perform Line by line
<number>
Copyright © MediaTek Inc. All rights reserved.
Line 2
Line 5
Notes: <number>

## Slide 5: Outline
Introduction
Proposed IDF algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 6: Proposed IDF Algorithm
Based on DF in HM2.0
  Filtering process is based on 8x8 block
  Two pixel lines are used in filter decision process
Modifications
  Luma deblocking filter
    Boundary strength (BS) derivation
    Filtering conditions
      filtering decision
      filter selection
    Thresholds and clipping values
    weak filter operation
  Chroma deblocking filter
    Filtering process
      4:2:0, 8x8 -> 4x4
    Add filtering decision
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 7: Modified Luma Filter – Modification 1
For a boundary, BS=2 if
  One of the neighboring blocks has non-zero transform coefficients
Inherited from H.264
  Make sense when transform size is equal to prediction size
  TU can be larger than PU in HEVC
Suggested modification
  Only check for TU boundary
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 8: Modified Luma Filter – Modification 2
Modification of filter decision conditions
  Also measure the gradient across block boundary
  3 conditions for i=2 and 5 are true, the boundary is decided to be filtered
    |p0i – q0i| < Tα
    |p1i – p0i| < Tβ
    |q1i – q0i| < Tβ
  Tα and Tβ are derived using α and β
Modification of filter selection conditions
  Also measure the gradient across the second pixel
  For each line, 2 conditions are true, strong filter is used, otherwise, weak filter is used
    |p0i – q0i| < (α >> 2) – (α >> 4)
    |q1i -q0i | + |q2i -q0i | + |q3i -q0i | + |p1i -p0i | + |p2i -p0i | + |p3i -p0i | < ((β-4)<<2)
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 9: Modified Luma Filter Modification 3&4
Thresholds and clipping values
  Add one more threshold, α, for filtering decision
  Modified clipping values to filter more in large QP
Weak filter operation
  Modified coefficients for computing delta value
  Additional condition for the second pixel from the boundary
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 10: Modified Chroma Filter
Filtering unit size
  Change according to sampling format
  For 4:2:0, 4x4 is used
  For 4:2:2, 4x8 is used
  For 4:4:4, 8x8 is used
Add Filtering decision
  A or B is intra coded
  The same conditions with luma component
    For filtering unit of 4x4, line 1 is used instead of line 2 in luma
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 11: Outline
Introduction
Proposed IDF algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 12: Experiments
Recommended test conditions in JCTVC-D600
Experiment 1 – modified luma filter and chroma filter
Experiment 2 – modified chroma filter only
Thank Ericsson and Sony for cross-verifying our results (E256, E071).
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 13: Results for Experiment 1
<number>
Copyright © MediaTek Inc. All rights reserved.
 | HE-AI |  |  | LC-AI |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.9% | -1.0% | -1.3% | -2.4% | -2.1% | -2.0%
Class B | -1.2% | -1.2% | -1.8% | -1.4% | -2.8% | -3.0%
Class C | -1.0% | -2.1% | -2.1% | -1.2% | -3.6% | -4.1%
Class D | -0.9% | -2.0% | -2.2% | -1.1% | -4.0% | -4.4%
Class E | -1.3% | -0.3% | -0.5% | -1.5% | -2.5% | -3.3%
All | -1.3% | -1.4% | -1.6% | -1.5% | -3.0% | -3.4%
Enc Time[%] | 100% |  |  | 97% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 |  | HE-RA |  |  | LC-RA | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.2% | -0.9% | -1.2% | -1.6% | -1.4% | -1.4%
Class B | -0.9% | -1.6% | -1.7% | -1.2% | -1.7% | -1.6%
Class C | -0.8% | -2.5% | -2.4% | -0.8% | -2.3% | -2.5%
Class D | -0.7% | -2.2% | -2.4% | -0.7% | -2.0% | -2.2%
Class E |  |  |  |  |  | 
All | -0.9% | -1.8% | -1.9% | -1.1% | -1.8% | -1.9%
Enc Time[%] | 100% |  |  | 98% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | HE-LD |  |  | LC-LD |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.8% | -0.7% | -0.9% | -1.2% | -0.6% | -0.3%
Class C | -0.9% | -1.0% | -1.1% | -1.1% | -1.0% | -1.2%
Class D | -1.1% | -0.7% | -1.2% | -1.0% | -0.7% | -0.6%
Class E | -0.9% | -0.3% | -0.2% | -1.4% | -1.9% | -1.7%
All | -0.9% | -0.7% | -0.9% | -1.2% | -1.0% | -0.9%
Enc Time[%] | 101% |  |  | 98% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 

## Slide 14: Results for Experiment 2
Copyright © MediaTek Inc. All rights reserved.
<number>
 | HE-AI |  |  | LC-AI |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0% | -1.1% | -1.3% | 0.0% | -2.2% | -2.1%
Class B | 0.0% | -1.4% | -2.0% | 0.0% | -2.7% | -2.8%
Class C | 0.0% | -2.3% | -2.3% | 0.0% | -3.4% | -3.9%
Class D | 0.0% | -2.1% | -2.4% | 0.0% | -3.6% | -4.0%
Class E | 0.0% | -0.3% | -0.5% | 0.0% | -2.5% | -3.3%
All | 0.0% | -1.5% | -1.8% | 0.0% | -2.9% | -3.2%
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 |  | HE-RA |  |  | LC-RA | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0% | -0.9% | -1.3% | -0.1% | -2.2% | -2.1%
Class B | 0.0% | -1.6% | -1.8% | 0.0% | -1.8% | -1.7%
Class C | -0.1% | -2.7% | -2.4% | -0.1% | -2.7% | -3.0%
Class D | 0.0% | -2.0% | -2.4% | 0.0% | -2.1% | -2.3%
Class E |  |  |  |  |  | 
All | 0.0% | -1.8% | -2.0% | 0.0% | -2.2% | -2.2%
Enc Time[%] | 100% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | HE-LD |  |  | LC-LD |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.4% | -0.7% | 0.0% | -0.8% | -0.5%
Class C | 0.0% | -1.0% | -1.1% | 0.0% | -1.2% | -1.4%
Class D | -0.1% | -0.6% | -1.0% | 0.0% | -0.9% | -0.7%
Class E | -0.1% | -0.3% | -0.4% | 0.0% | -1.6% | -1.7%
All | -0.1% | -0.6% | -0.8% | 0.0% | -1.1% | -1.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 

## Slide 15: Decoding Time
 | HM 2.0 [s] | Experiment 1 [s] |  | Experiment 2 [s] | 
HE-AI | 69.3 | 68.1 | 98.3% | 68.7 | 99.1%
LC-AI | 30.0 | 29.9 | 99.7% | 30.0 | 100.0%
HE-RA | 33.7 | 33.9 | 100.6% | 33.4 | 99.2%
LC-RA | 18.5 | 18.6 | 100.3% | 18.5 | 99.8%
HE-LD | 28.1 | 27.8 | 99.1% | 28.1 | 100.0%
LC-LD | 15.9 | 16.0 | 100.5% | 15.9 | 100.0%
Average |  |  | 99.7% |  | 99.7%
Copyright © MediaTek Inc. All rights reserved.
<number>
Decoding time is measured on a single machine
Both test 1 and test 2 have similar decoding time as that of HM2.0

## Slide 16: Conclusions
An improved deblocking filter (IDF) algorithm has been investigated
Average BD-rate reductions are 1.2%, 1.8% and 1.7% for Y, U and V
Improvements can be observed in subjective quality for some cases
No big difference in subjective quality between IDF and HEVC DF in most cases
The complexity of IDF is almost the same to that of HEVC DF
Propose to be accepted or partially accepted by HEVC
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 17
<number>
Copyright © MediaTek Inc. All rights reserved.