## Slide 1: Adaptive Inter Mode Coding for LCEC
Ximin Zhang, Shan Liu, Shawmin Lei
JCTVC-E080
Copyright © MediaTek Inc. All rights reserved.
Presented by Ximin Zhang
5th JCT Meeting in Geneva
16-23 March, 2011
Notes: Cross check by Samsung E-407, SONY E-469

## Slide 2: Introduction
coding_tree( x0, y0, log2CUSize ) { | Descriptor
... | 
split_coding_unit_flag[ x0 ][ y0 ] | u(1) ¦ ae(v)
... | 
} | 
coding_unit( x0, y0, log2CUSize ) { | Descriptor
if( slice_type != I ) | 
skip_flag[ x0 ][ y0 ] | u(1) ¦ ae(v)
… | 
if( slice_type != I ¦ ¦ log2CUSize = = Log2MinCUSize ) | 
pred_mode | u(v) ¦ ae(v)
... | 
} | 
prediction_unit( x0, y0, log2PUWidth, log2PUHeight, PartIdx ) { | Descriptor
… | 
if( !InferredMergeFlag && NumMergeCand > 0 ) | 
merge_flag[ x0 ][ y0 ] | u(1) ¦ ae(v)
… | 
} | 

## Slide 3: Analysis
 | Split | SKIP | 2Nx2N | 2NxN | Nx2N | NxN | INTRA
Code word length | 1 | 2 | 3+ | 4+ | 5+ | 6+ | 7+
The optimal syntax coding should be content dependent
Use a set of adaptive code words for each mode in each depth corresponding to the frequency of their appearance

## Slide 4: Proposed solution
 | Coding syntax
Mode1[uiDepth] | Syntax[Index (Mode1 [uiDepth])]
Mode2[uiDepth] | Syntax[Index (Mode2 [uiDepth])]
Mode3[uiDepth] | Syntax[Index (Mode3 [uiDepth])]
Mode4[uiDepth] | Syntax[Index (Mode4 [uiDepth])]
Mode5[uiDepth] | Syntax[Index (Mode5 [uiDepth])]
Mode6[uiDepth] | Syntax[Index (Mode6 [uiDepth])]
Mode7[uiDepth] | Syntax[Index (Mode7 [uiDepth])]
Mode8[uiDepth] | Syntax[Index (Mode8 [uiDepth])]
… | …
 | Coding word syntax
Syntax[0] | 1
Syntax[1] | 01
Syntax[2] | 001
Syntax[3] | 0001
Syntax[4] | 00001
Syntax[5] | 000001
Syntax[6] | 0000001
Syntax[7] | 00000001
… | …
Counter(ModeA) > Counter (ModeB)
Index(ModeA) < Index(ModeB)

## Slide 5: Simulation results (vs HM2.0 Anchor)
 |  |  | Random access LoCo |  | 
 |  | Y BD-rate | U BD-rate | V BD-rate | 
 | Class A | -0.2 | -0.2 | -0.1 | 
 | Class B | 0.0 | -0.1 | 0.0 | 
 | Class C | -0.2 | -0.1 | -0.1 | 
 | Class D | -0.3 | -0.2 | -0.1 | 
 | Class E |  |  |  | 
 | All | -0.2 | -0.1 | -0.1 | 
 | Enc Time[%] | 100% |  |  | 
 | Dec Time[%] | 100% |  |  | 
 |  | Low delay LoCo |  |  | 
 |  | Y BD-rate | U BD-rate | V BD-rate | 
 | Class A |  |  |  | 
 | Class B | -0.3 | -0.1 | 0.4 | 
 | Class C | -0.4 | -0.1 | -0.3 | 
 | Class D | -0.3 | 0.0 | 0.2 | 
 | Class E | -0.3 | 0.2 | 0.2 | 
 | All | -0.3 | 0.0 | 0.1 | 
 | Enc Time[%] | 101% |  |  | 
 | Dec Time[%] | 100% |  |  | 

## Slide 6: Simulation results (vs Fixed VLC table)
* Compared with fixed codeword table (QC_LCEC_INTER_MODE disabled)
 |  |  | Random access LoCo |  | 
 |  | Y BD-rate | U BD-rate | V BD-rate | 
 | Class A | -1.8 | -1.1 | -1.0 | 
 | Class B | -1.9 | -1.9 | -1.7 | 
 | Class C | -1.5 | -1.5 | -1.5 | 
 | Class D | -1.2 | -1.1 | -1.1 | 
 | Class E |  |  |  | 
 | All | -1.6 | -1.4 | -1.4 | 
 | Enc Time[%] | 100% |  |  | 
 | Dec Time[%] | 100% |  |  | 
 |  | Low delay LoCo |  |  | 
 |  | Y BD-rate | U BD-rate | V BD-rate | 
 | Class A |  |  |  | 
 | Class B | -1.9 | -2.5 | -2.1 | 
 | Class C | -1.0 | -1.3 | -1.3 | 
 | Class D | -1.0 | -1.5 | -1.3 | 
 | Class E | -3.7 | -3.7 | -3.8 | 
 | All | -1.8 | -2.2 | -2.0 | 
 | Enc Time[%] | 100% |  |  | 
 | Dec Time[%] | 100% |  |  | 

## Slide 7: Conclusions
The proposed methods provide average 0.2% and 0.3% BD rate gain compared to HM2.0 anchor and average 1.6% and 1.8% BD rate gain compared to HM2.0 anchor with fixed VLC table.
We recommend the proposed scheme to be adopted into HM for LCEC inter mode coding.

## Slide 8
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com
Thank you!

## Slide 9: Proposed syntax table change
coding_tree( x0, y0, log2CUSize ) { | Descriptor
... | 
split_coding_unit_flag[ x0 ][ y0 ] | u(v) ¦ ae(v)
... | 
} | 
coding_unit( x0, y0, log2CUSize ) { | Descriptor
if( slice_type != I ) | 
skip_flag[ x0 ][ y0 ] | u(v) ¦ ae(v)
… | 
if( slice_type != I ¦ ¦ log2CUSize = = Log2MinCUSize ) | 
pred_mode | u(v) ¦ ae(v)
... | 
} | 
prediction_unit( x0, y0, log2PUWidth, log2PUHeight, PartIdx ) { | Descriptor
… | 
if( !InferredMergeFlag && NumMergeCand > 0 ) | 
merge_flag[ x0 ][ y0 ] | u(v) ¦ ae(v)
… | 
} |