## Slide 1: Adaptive CU Depth Range
JCTVC-E090
Copyright © MediaTek Inc. All rights reserved.
Presented by Xiang Li
5th JCTVC Meeting
16-23 March, 2011
Xiang Li, Jicheng An, Xun Guo and Shawmin Lei

## Slide 2: Introduction
CU depth range is signaled at slice level or implicitly derived at CU level
Encoding time saving is 26.5% on average for 4 inter cases, 8.5% on average for 2 intra cases.
Coding loss of 6 cases is within 0.3% (BD-rate increase)
Cross verified by Microsoft (JCTVC-E153)

## Slide 3: Current CU Depth Signaling in HM2.0
CU Depth Information in SPS
- Maximal CU depth (4) is explicitly signaled
- Minimal CU depth is always set to 0
- CU depth range (0~3) is used for all frames (sequence level)
CU Depth Range is Highly Content and Configuration Dependent
Sequence@Conditions (JCTVC-D600) | Average CU Depth
BlowingBubbles(416x240)@IHE,QP=22 | 2.91
NebutaFestival(2560x1600)@RALC,QP=37, highest slice depth | 0.02
PartyScene(832x480)@RAHE, QP=22, lowest slice depth | 2.58
Vidyo4(1280x720)@LDHE,QP=37, highest slice depth | 0.12

## Slide 4: Potential Redundancies (I)
Flag of CU Splitting
Similarly, further splitting flag is not necessary when current depth reaches the max CU depth
CU Depth | CU splitting flag
0 | 1
1 | 1, 1, 1, 1
Min CU
Depth=2
Always 1, can be skipped in bitstream

## Slide 5: Potential Redundancies (II)
Direction of inter prediction
- Three types of pred direction: F-Pred, B-Pred, Bi-Pred
- Bi-Pred is not efficient for small blocks (high CU depths) [H.-C. Lin, et al., ICIP2009]
- Bi-Pred can be disabled at high depths to reduce the table size
slice_type | inter_pred_idc | Name of inter_pred_idc
P and B | 0 | Pred_L0
 | 1 | Pred_L1
B | 2 | BiPred

## Slide 6: Determining CU Depth Range at Slice Level
Average Depth of a Frame
Adaptive CU Depth Range Based on Previously Coded Same-Type Frame
Superscript S and G indicate the depth range information at slice and global level (in SPS).
Subscript p denotes the previously coded same-type frame

## Slide 7: Simulation Results of Slice Level ACUD
Faster encoding speed (up to 28%) with little coding loss (≤0.3%)

## Slide 8: Further Improvement – ACUD at CU Level
A flag of Enabling CU-Level ACUD in SPS
No Additional Syntax Modification Compared to Slice Level ACUD
Derivation of CU Depth Range CU Level
Superscript C indicates the current CU, L and U denote the CU depths of the left and top PUs, respectively.
Additional 5% encoding time saving with less than 0.3% BD-rate increase (similar to that of slice-level ACUD)

## Slide 9: Simulation Results of CU Level ACUD

## Slide 10: Conclusions
Potential redundancies are avoided with the proposed method
Encoding time saving is up to 32% (for LDLC).
Average coding loss of 6 cases is 0.15% (0.3% at maximal)

## Slide 11
Copyright © MediaTek Inc. All rights reserved.
Thanks for your attention!

## Slide 12: Proposed Syntax Modification – Slice Level ACUD (I)
seq_parameter_set_rbsp( ) { | Descriptor
…… | 
log2_min_coding_block_size_minus3 | ue(v)
log2_diff_max_min_coding_block_size | ue(v)
seq_adaptive_CU_depth_idc | ue(v)
log2_min_transform_block_size_minus2 | ue(v)
} | 
slice_header( ) { | Descriptor
…… | 
slice_qp_delta | se(v)
if(seq_adaptive_CU_depth_idc==1) { | 
slice_CU_depth_min | ue()
slice_CU_depth_max | ue()
} | 
alf_param() | 
…… | 
} | 

## Slide 13: Proposed Syntax Modification – Slice Level ACUD (II)
coding_tree( ) { | Descriptor
if( x0 + ( 1 << log2CUSize ) <= PicWidthInSamplesL && y0 + ( 1 << log2CUSize ) <= PicHeightInSamplesL && log2CUSize > Log2MinCUSize && CurCUDepth >= MinCUDepth && CurCUDepth < MaxCUDepth) | 
split_coding_unit_flag[ x0 ][ y0 ] | u(1) ¦ ae(v)
…… | 
prediction_unit(x0, y0, log2PUWidth, log2PUHeight, PartIdx ) { | Descriptor
…… | 
if( slice_type == B) | 
inter_pred_idc[ x0 ][ y0 ] | ue(v)¦ ae(v)
…… | 
slice_type | inter_pred_idc | Name of inter_pred_idc
P and B | 0 | Pred_L0
 | 1 | Pred_L1
B | 2 | BiPred

## Slide 14: Modified LCEC for split_coding_unit_flag
Initial Joint Coding Table in HM2.0
Proposed Initial Joint Coding Table

## Slide 15: Modified LCEC for Inter Prediction Direction
Currently, inter_pred_idc is jointly coded with reference index
New initial coding table of reference index when Bi-prediction is disabled

## Slide 16: Performance of Disabling Bi-Pred and CU Depth
Chart: Encoding Time Saving
| RAHE | RALC | LDHE | LDLC
CU Level ACUD (JCTVC-E90) | -0.21151 | -0.26686 | -0.25703 | -0.31796
Only Disable BiPred | -0.11288 | -0.21826 | -0.20311 | -0.24982
Only Disable CU Depth | -0.1179 | -0.20725 | -0.1531 | -0.12789
Chart: Coding Loss in BD-Rate (Luma)
| RAHE | RALC | LDHE | LDLC
CU Level ACUD (JCTVC-E90) | 0.0021827 | 0.0033654 | 0.00063093 | 0.0030218
Only Disable BiPred | 0.00091988 | 0.0024345 | -0.00045843 | 0.0020136
Only Disable CU Depth | 0.0011822 | 0.00071445 | 0.0002362 | 0.00085159

## Slide 17: JCTVC-E090 (CU Level) vs. Encoder Only Approach
Chart: Coding Loss in BD-Rate (Luma)
| IHE | ILC | RAHE | RALC | LDHE | LDLC
CU Level ACUD (JCTVC-E90) | 0.00038445 | -0.000351 | 0.0021827 | 0.0033654 | 0.00063093 | 0.0030218
Encoder Only | 0.00062505 | 0.00061089 | 0.0046865 | 0.006482 | 0.0035512 | 0.0054638
Chart: Encoding Time Saving
| IHE | ILC | RAHE | RALC | LDHE | LDLC
CU Level ACUD (JCTVC-E90) | -0.087829 | -0.075522 | -0.21151 | -0.26686 | -0.25703 | -0.31796
Encoder Only | -0.083269 | -0.09 | -0.21278 | -0.24437 | -0.29193 | -0.32217