## Slide 1: Motion Vector Decimation for Temporal Prediction
Xun Guo, Jian-Liang Lin, Yu-Wen Huang and Shawmin Lei
MediaTek Inc.
Presented by Xun Guo
5th JCT-VC Meeting in Geneva
16-23 March, 2011
Notes: <number>

## Slide 2: Overall Summary
A motion vector decimation method is proposed
  Use the bottom right 4x4 block instead of the current top left one
  Use the reference indices of the MV decimation position accordingly
BD-rate reduction
  By replacing MVs
    BD-rate reductions of 0.3%, 0.3%, 0.5%, 0.4% for RA-HE, RA-LC, LD-HE and LD-LC, respectively
  By also replacing reference indices
    BD-rate reductions of 0.5%, 0.5%, 0.6%, 0.6% for RA-HE, RA-LC, LD-HE and LD-LC, respectively
Encoding and decoding time
  Almost the same to HM2.0
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 3: Introduction
MV compression in HM2.0
  Use a reduced size of MV buffer
  Use 16x16 MV compression unit as default setting
  Use the top left 4x4 block for MV decimation
Mismatch between MVs and reference indices
  Other blocks use the MVs of block 0 but their own reference indices
Copyright © MediaTek Inc. All rights reserved.
<number>
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 4: Proposed MV Decimation Method
Use the bottom left 4x4 block for MV decimation
Remove the mismatch between MVs and reference indices
  Use the reference indices of the bottom left 4x4 block for the whole unit
Copyright © MediaTek Inc. All rights reserved.
<number>
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 5: Experiments
Recommended test conditions in JCTVC-C600
Four configurations: RA-HE, RA-LC, LD-HE and LD-LC
Experiment 1 – use the bottom right 4x4 block
Experiment 2 – remove the mismatch based on experiment 1
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 6: Results for Experiment 1
<number>
Copyright © MediaTek Inc. All rights reserved.
 |  | HE-RA |  |  | LC-RA | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | -0.3 | -0.3 | -0.4 | -0.4 | -0.4
Class B | -0.2 | -0.1 | -0.1 | -0.1 | -0.1 | -0.1
Class C | -0.3 | -0.3 | -0.3 | -0.3 | -0.2 | -0.3
Class D | -0.5 | -0.4 | -0.4 | -0.5 | -0.5 | -0.4
Class E |  |  |  |  |  | 
All | -0.3 | -0.3 | -0.3 | -0.3 | -0.3 | -0.3
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | HE-LD |  |  | LC-LD |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.3 | -0.2 | -0.4 | -0.2 | -0.3 | 0.0
Class C | -0.5 | -0.3 | -0.5 | -0.5 | -0.5 | -0.7
Class D | -0.6 | -0.7 | -0.7 | -0.5 | -0.5 | -0.9
Class E | -0.7 | -1.0 | -0.3 | -0.4 | -0.9 | -0.5
All | -0.5 | -0.5 | -0.5 | -0.4 | -0.5 | -0.5
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
Use the bottom right 4x4 block

## Slide 7: Results for Experiment 2
<number>
Copyright © MediaTek Inc. All rights reserved.
Remove the mismatch based on experiment 1
 |  | HE-RA |  |  | LC-RA | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.4 | -0.2 | -0.5 | -0.5 | -0.4 | -0.3
Class B | -0.3 | -0.2 | -0.2 | -0.2 | -0.1 | -0.1
Class C | -0.5 | -0.5 | -0.5 | -0.5 | -0.4 | -0.3
Class D | -0.7 | -0.7 | -0.7 | -0.8 | -0.7 | -0.7
Class E |  |  |  |  |  | 
All | -0.5 | -0.4 | -0.5 | -0.5 | -0.4 | -0.4
Enc Time[%] | 100% |  |  | 102% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | HE-LD |  |  | LC-LD |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.4 | -0.2 | -0.4 | -0.4 | -0.3 | -0.1
Class C | -0.6 | -0.5 | -0.5 | -0.7 | -0.7 | -0.8
Class D | -0.8 | -0.4 | -0.8 | -0.8 | -0.7 | -0.7
Class E | -0.7 | -0.4 | -0.2 | -0.6 | -0.9 | -0.8
All | -0.6 | -0.4 | -0.5 | -0.6 | -0.6 | -0.6
Enc Time[%] | 100% |  |  | 98% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 

## Slide 8: Conclusions
A MV decimation method is proposed
  BD-rate reductions of 0.3%, 0.3%, 0.5%, 0.4% for RA-HE, RA-LC, LD-HE and LD-LC
Further improvement by removing the mismatch between MVs and reference indices
  BD-rate reductions of 0.5%, 0.5%, 0.6%, 0.6% for RA-HE, RA-LC, LD-HE and LD-LC
The complexity is almost the same to that of HM2.0
Propose to be accepted by HEVC
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 9
<number>
Copyright © MediaTek Inc. All rights reserved.