## Slide 1
<number>
<number>
JCT-VC D108
CE 8.3: Loop Filter with Directional Similarity Mapping
5th JCT-VC Meeting, Mar. 2011
PoLin Lai
Felix C. Fernandes Samsung Electronics Co., Ltd
Notes: <number>
겉표지 ( 타이틀 : Tahoma 46, Date : Arial 24 )

## Slide 2: 1. 4x4 block-based FA, with Directional features
<number>
Each 4x4 block:
Directional gradients [1, -1] or [-1,2,-1]
On 9 pixels  36 subtractions
Classify blocks into smallest gradients
Comparison operations
Currently only 4 filters
Notes: <number>

## Slide 3: 2. Filter design: f_h(ak,bk) and f_v(ak,bk)
<number>
f_h: a1~a5 and bC~b7, 14 coeff f_v: a1~a5 and bC~b7, 14 coeff
f_d: a1~a5 and bC~b6, 13 coeff f_u: a1~a5 and bC~b6, 13 coeff
Notes: Sym prevent filtering across edges
<number>

## Slide 4: 3. Similarity mapping in directional filter
<number>
Linear spatial filter  Bias filter toward neighbors
Directional filter  Bias filter along edge, not across edge
Similarity mapping with hard-thresholding:
  Preserve edges by not using pixels too different from X(i,j)
For X(i,j) to be filtered, map its neighboring pixels Xn to Xn’:
XN’ = XN if | XN - X(i,j) | ≤ σ/2
= X(i,j) if | XN - X(i,j) | > σ/2
Xn
Xn’
X(i,j)
X(i,j)
X(i,j) + σ/2
X(i,j) - σ/2
Notes: <number>

## Slide 5: Results
<number>
 | CE8.3 Directional filter 7x7 Block-based adaptation Gradient as [1, -1] |  | 
 | ( MediaTek E265 ) |  | 
 | IO | RA | LD
Class A | -0.1 | -0.5 | 
Class B | 0.0 | -0.3 | 0.5
Class C | -0.5 | -0.5 | -0.2
Class D | -0.3 | 0.6 | 0.2
Class E | -0.4 |  | 0.9
BD-rate | -0.2 | -0.2 | 0.3
Enc. Time | (163) | (125) | (117)
Dec. time | (146) | (130) | (124)
Vert. taps | 7 |  | 
# of coefs. | 25 |  | 
Notes: <number>