## Slide 1: Using MPS to encode extended UDI mode numbers for robustness
Guichun Li
Lingzhi Liu
Yongbing Lin
JCTVC-E113

## Slide 2: Introduction
Using additional non-directional prediction modes, Planar Mode, e.g., for UDI can improve not only the coding gain but also the subjective visual quality.
The mode signaling method proposed in D235 (Mode 2 shared by Planar and DC) has some potential parsing dependency and error resilience issues

## Slide 3: Introduction
Multiple Prediction Sets (MPS) method is used to code the intra prediction mode when additional non-directional modes are used
The method can resolve the parsing dependency and improve the error resilience of intra prediction of HM software

## Slide 4: Parsing Dependency and Error Resilience issues for current signaling method
Whether to decode the DC/planar flag is decided by the current decoded intra mode number:
  Parsing 1 more bit if intra mode number is 2;
  No parsing otherwise.
Current intra prediction mode is related to the intra prediction modes of its top and left neighboring blocks
The intra prediction modes of top and left are also related to their neighbors

## Slide 5: Parsing Dependency and Error Resilience issues for current signaling method (Cont.)
Whether to decode the flag bit is dependent with some syntaxes which might be far away in the bit streams.
Similar problem as AMVP parsing problem discussed in JCTVC-D126

## Slide 6: Using MPS for intra prediciton mode
MPS was introduced in JCTVC-A022E, JCTVC-C111.
The prediction modes are grouped into multiple predictor sets in which each of the predictor set has similar subset divisions.
The group number and group index of the current PU are predicted from the predictor group number and group index of neighboring PUs independently.

## Slide 7: Implementation

## Slide 8: Implementation
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 11 | 16 | 34 | 14 | 10 | 12 | 13 | 15 | 17
2 | 22 | 30 | 35 | 18 | 19 | 23 | 25 | 28 | 9
3 | 21 | 29 | 32 | 26 | 20 | 24 | 33 | 27 | 31
Improved MPS mode table

## Slide 9: Simulation Result (35 Modes) - UDI + Planar Mode
 | Intra HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.6 | -0.2 | -0.1
Class B | -0.7 | -0.3 | -0.4
Class C | -0.4 | -0.1 | -0.1
Class D | -0.3 | 0.0 | 0.0
Class E | -0.8 | -0.5 | -0.1
All | -0.6 | -0.2 | -0.2
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 

## Slide 10: Simulation Result (36 Modes) - UDI + Planar + Sub-block Based Mode
 | Intra HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.0 | -0.4 | -0.2
Class B | -1.1 | -0.5 | -0.6
Class C | -0.6 | -0.3 | -0.1
Class D | -0.5 | -0.1 | -0.1
Class E | -1.1 | -0.6 | -0.1
All | -0.9 | -0.4 | -0.2
Enc Time[%] | 103% |  | 
Dec Time[%] | 130% |  | 

## Slide 11: Conclusion
MPS Intra performs slightly lower than JCTVC-D235’s signaling method in terms of BD-rate. But it does not have the parsing dependency and error resistance problem of the D235 implementation.
It’s shown that by utilizing more additional intra modes with MPS signaling method, the performance can be further improved.
MPS Intra has the capacity of supporting up to 3 non-directional modes without increasing the cost.
Therefore it is recommended to use MPS when extra intra modes are used in UDI.
Notes: <number>

## Slide 12: Thank you!

## Slide 13: MPS Intra with Planar vs. D235 with LCEC_INTRA_MODE off
 | Intra HE |  |  | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.4 | -0.4 | -0.5 | -0.2 | -0.2
Class B | 0.1 | -0.1 | -0.1 | -0.3 | 0.1 | 0.1
Class C | 0.1 | 0.0 | -0.1 | 0.0 | 0.4 | 0.4
Class D | 0.3 | 0.0 | -0.1 | -0.1 | 0.4 | 0.3
Class E | 0.1 | -0.3 | -0.3 | -0.3 | 0.0 | 0.3
All | 0.1 | -0.1 | -0.2 | -0.3 | 0.1 | 0.2
* The tests were run on different workstations, running time comparisons are not accurate, thus not listed here

## Slide 14: Storage Problem for DC/Planar flag
Storage and video surveillance, a decoder is only required to check whether the bit stream is corresponding to the standard.
Because current intra prediction mode is predicted from its neighboring blocks, in order to decide whether the bit of mode number need to be decoded or not, the system has to store at least all the decoded intra prediction modes of a whole block-line.