## Slide 1: Evaluation results on merge mode in HM2.0
Minhua Zhou (zhou@ti.com) Texas Instruments Inc., USA
JVTVC-E115

## Slide 2: Merge mode in HM2.0
In HM2.0 merge mode is combined with direct mode, and extended to PU-level
Partial CU merge mode is also included HM2.0, for CUs of larger than 8x8, the first PU has to take merge mode if part size is 2N x N or N x 2N

## Slide 3: Comments on partial CU merge mode
The current CU may have totally different motion from its spatial and temporal neighbours; the forced merge could cause visual quality degradation and coding artefacts.
For pipelined hardware architecture in which an encoder design may choose to estimate the motion vectors for CUs in parallel, this forced merge mode causes design burden due to its irregularity.
An encoder may choose to support CU size only down to 16x16, the partial CU merge mode essentially disables 2NxN, Nx2N motion vector partitions if the partial merge mode cannot be implemented on the encoder side due to architecture constraints.

## Slide 4: Test settings
Settings | Objective
Disable merge mode but still encode merge flag in HM2.0 | Evaluate the total coding gain of the HM2.0 merge mode
Disable merge mode and skip merge flag coding in HM2.0 | Evaluate the merge flag coding overhead of the HM2.0 merge mode
Remove temporal MVP from the merge MVP list | Evaluate coding gain of PU-level adaptive temporal and spatial merge (or direct) mode
Disable partial CU merge mode in HM2.0 | Evaluate coding gain of the partial CU merge mode

## Slide 5: Experimental results
Settings | HE-RA (%) | LC-RA (%) | HE-LD (%) | LC-LD (%)
Disable merge mode but still encode merge flag in HM2.0 | 3.0 | 3.5 | 4.5 | 6.1
Disable merge mode and skip merge flag coding in HM2.0 | 2.8 | 2.8 | 4.2 | 5.0
Remove temporal MVP from the merge MVP list (cross-checked by JCTVC-E148) | 0.0 | -0.2 | -0.1 | -0.4
Disable partial CU merge mode in HM2.0 (cross-checked by JCTVC-E146) | -0.5 | -0.7 | -0.2 | -0.4

## Slide 6: Observations
The HM2.0 merge mode provides on average gain of 3.0% in HE-RA, 3.5% in LC-RA, 4.5% in HE-LD, and 6.1% in LC-LD, respectively
The overhead of coding merge mode flag is 0.2% in HE-RA, 0.7% in LC-RA, 0.3% in HE-LD, and 0.9% in LC-LD, respectively
PU-level adaptive temporal/spatial merge mode is not effective, removing the temporal MVP from the merge MVP list slightly increases quality (0.0% in HE-RA, 0.2% in LC-RA, 0.1% in HE-LD, and 0.4% in LC-LD, respectively. cross-checked by JCTVC-E148)
Disabling the partial CU merge mode leads average gain of 0.5% in HE-RA, 0.7% in LC-RA, 0.2% in HE-LD, and 0.4% in LC-LD, respectively, cross-checked by JCTVC-E146)

## Slide 7: Recommendations
Remove the temporal MVP from the merge MVP list to enhance error resiliency and reduce pruning complexity of the merge MVP list, and to improve coding efficiency
and add a high-level disabled flag to disable the partial CU merge mode to provide encoder with design choice