## Slide 1: A study on HM2.0 bitstream parsing and error resiliency issue
Minhua Zhou (zhou@ti.com) Vivienne Sze (Sze@ti.com)
Texas Instruments Inc., USA
JVTVC-E118

## Slide 2: Outline
HM2.0 bitstream parsing issue
  Problem statement
  Potential soutions
HM2.0 error resiliency issue
  Problem statement
  Potential soutions
Recommendations

## Slide 3: Diagram of HM2.0 motion information decoding
Motion information
  merge (flag, MVP_idx), skip (flag, MVP_idx), prediction direction, part size, ref_idx, MVDs, mvp_idx, intra/inter flag
Next CU
Repeat for PUs in the CU
CU data
n
n
n
y
y
y
Skip
mode?
Skip mode MVP list construction
Skip mode MVP index decoding
Motion compensation & CU reconstruction
Merge mode MVP list construction
Merge MVP List size 0?
MVD MVP list construction
Ref_idx, MVDs & MVP_idx decoding
Merge flag decoding
Merge mode ?
merge mode MVP index decoding

## Slide 4: HM2.0 bitstream parsing issue - causes
In HM2.0 bitstream parsing and motion information reconstruction are interdependent, because
MVP list construction requires full reconstruction of motion information
Merge flag coding depends on the merge mode MVP list size
  Merge flag not present in bitstream when the MVP list size is zero
  CABAC context selection for merge flag also depends on the MVP list size
MVP_idx coding of merge mode, skip mode and MVD depends on the merge/skip/MVD MVP list size
  MVP_idx not present if the MVP list size is one
  Different binarization tables are used for the MVP_idx coding based on the MVP list size

## Slide 5: HM2.0 bitstream parsing issue – problem statement
HEVC decoder will not be able to meet throughput requirements
  (a) is what is required by the current HM design
  (b) is what industry can do with great difficulty due to CABAC throughput issue

## Slide 6: Requirements for HEVC merge/skip/MVD design
Merge flag, merge/skip/MVD MVP_index coding shall be decoupled from the bitstream parsing (i.e. independent of MVP list size)
Motion information reconstruction (including the MVP list construction) shall be kept at reasonably low-complexity level. Otherwise, it could become bottleneck of decoder
  Maintaining the motion vector compression at 16x ratio is critical for keeping TMVP derivation complexity at affordable level
  Spatial MVP scaling, if adopted, shall be disabled for PUs of small block size
MVP list for merge and skip should be unified for lowering the memory bandwidth requirements on the encoder side for motion estimation
  Allowing skip mode with ref_idx != 0 requires good justification as it has significant memory bandwidth cost

## Slide 7: HM2.0 bitstream parsing issue – quality analysis
The following solution is tested to quantify the coding loss if the bitsteam parsing issue is completely removed
  Coding merge flag all the time, even if the merge mode MVP list is empty
  CABAC context selection for merge flag independent of the merge mode MVP list size (i.e. using HM1.0 method)
  MVP index binarization/LCEC coding for merge, skip and MVD using truncated unary coding with a fixed maximum length of 5, 3 and 3, respectively
    MVP index is transmitted even if the MVP list size is 1
Results (similar results can be found in JCTVC-E148)
HE-RA | LC-RA | HE-LD | LC-LD
1.1% | 2.0% | 1.2% | 3.5%

## Slide 8: Remove parsing issue in merge flag coding
Algorithm: making merge flag coding independent of the merge flag MVP list size
  Adding a zero vector to the merge mode MVP list if it is empty, so that the merge flag is always coded because the minimum merge mode MVP list size is 1
  CABAC context selection for merge flag using HM1.0 method
  Same solution is found in JCTVC-E146 for different motivation
Benefits
  The bitstream parsing issue is partially resolved
  On decoder side the merge mode MVP list does not need to be constructed if the merge mode is not used
Results (cross-checked by JCTVC-E146)
HE-RA | LC-RA | HE-LD | LC-LD
0.0% | 0.0% | -0.1% | 0.0%

## Slide 9: HM2.0 error resiliency issue – problem statement
The HM2.0 design is very sensitive to errors due to
The merge/skip/MVD MVP list construction requires full reconstruction of motion vectors, prediction direction, reference frame index, part size, and intra/inter flag, any error in those information will cause incorrect reconstruction of the MVP list and lead to bitstream parsing stop (merge flag, MVP_idx)
  This sensitivity is removed if bitstream parsing issue is resolved
Temporal co-located motion vectors are used as motion vector predictors in merge mode, skip mode and motion vector coding, if motion vector field of an reference frame is lost, the error cannot be recovered until next intra-coded frame

## Slide 10: HM2.0 error resiliency issue – quality analysis
Settings | HE-RA (%) | LC-RA (%) | HE-LD (%) | LC-LD (%)
Disabling temporal MVP in merge, skip, motion vector coding and in ME (cross-checked by JCTVC-E148) | 2.3 | 2.2 | 1.7 | 2.4
Disabling temporal MVP in merge, skip, motion vector coding but enabling it in ME | 1.9 | 1.9 | 1.6 | 2.4
Disabling temporal MVP in merge and motion vector coding but enabling it in skip mode and ME | 0.4 | 0.3 | -0.2 | 0.5
Disabling temporal MVP in merge mode only (cross-checked by JCTVC-E148) | 0.0 | -0.2 | -0.1 | -0.4

## Slide 11: Motion estimation used in test

## Slide 12: Recommendations
Bitstream parsing
  Set up CE or AHG on study solutions for resolving bitstream parsing issues caused by the MVP list size dependent MVP index coding
Error resilience
  Set up core experiments or AHG on designing tools for encoder to generate more error resilient bitstreams (e.g.)
    Adding high-level flag (or new NAL unit type as proposed in JCTVC-E148) to allow encoder to disable TMVP from skip mode and motion vector coding
    Adding high-level flag to allow encoder to disable TMVP from motion vector coding and still keep in the skip mode (AVC fashion)