## Slide 1: E130 - CE6.b.2: Report on Combined Intra Prediction with Parallel Intra Coding by BBC and Sharp
R&D
© BBC MMXI
Marta Mrak, Andrea Gabriellini (BBC)
Jie Zhao, Andrew Segall (SHARP)

## Slide 3: Intra prediction in HM2.0
intra prediction direction signalled on PU level
actual prediction performed at TU level, from neighbouring TUs
  serial dependencies
small block sizes results in more dependencies within an LCU
solution for reducing serial dependencies
  Parallel Intra Prediction (PIP) - D074, E315
  proposed for higher resolution sequences, where serial bottleneck of intra prediction is more critical issue
prediction direction
PU
 4 TUs

## Slide 4: Parallel Intra Prediction (PIP) - E315
here the focus is on 2x parallelism from E315
enables parallel processing for the smallest PUs
applied on Parallel Prediction Block (PPB)
  8 x 8 PUs, when parallelism is useful (partitioning into 4 TUs), and
  four 4 x 4 PUs  in each case there are serial dependencies between 4 x 4 TUs for intra prediction
defines 2 sets of blocks (TUs) Set 1: uses reconstructed pixels from outside PPB Set 2: uses any available pixels
blocks from each set are predicted in parallel
prediction from outside PPB can be poorer compared to the original HM design  use prediction from inside the block
HM design
PIP design

## Slide 5: Combined Intra Prediction (CIP) - D191
CIP comprises a weighted combination of
  angular prediction
  local mean prediction
not only open-loop
  weighted combination
  reconstruction process is stable and controls any noise arising from different values available on enc/dec
BD-rate gain without increase of complexity
results from D191 for intra coding
  average 0.3 % HE, 0.7 % LC Y-BD-rate gain
  larger gains for higher resolutions - Class A average results are 1.2 % HE and 2.4 LC
  higher gains when encoder's complexity increases (testing more combinations)

## Slide 6: CIP + PIP
goal is to improve prediction in PIP
  using prediction from neighboring pixels from the current block (open loop prediction component of CIP)
test include different CIP configuration
  encoder: adding more RD search options that include CIP increases complexity and BD-rate gains
  decoding complexity of each configuration same as for the base (HM or HM+PIP)
PIP + CIP design
CIP
CIP
CIP
CIP

## Slide 7: Results for CIP and PIP separately Intra coding configurations
both tools applied on luma samples only
BD-rate gain/loss in chroma components taken into account using YUV BD-rate
  derived from YUV PSNR:
  (6  PSNR_Y + PSNR_U + PSNR_V) / 8

## Slide 8: Results for CIP + PIP Intra coding configurations

## Slide 9: Conclusions
We propose the application of CIP with PIP, for the HM design.
Results show that the increased parallelization comes with little loss in coding efficiency, which can be almost completely cancelled using CIP, without increase of complexity.
With more complex setting the CIP is capable to further improve the results of HM2.0 that uses parallel intra prediction.
Given this level of performance and the significance of parallelization for future standards, we recommend CIP +PIP to be adopted in the HM.