## Slide 1: DF-combined adaptive loop filter (JCTVC-E140)
Tomohiro Ikai
Takanori Yamazaki
SHARP Corporation
5th JCT-VC Meeting, Geneva, Switzerland, March 2011
Notes: <number>

## Slide 2: Overall Summary
Performance results
  BD gains
    1.1%, 0.7%, 0.7% (non-parallel case, beta = -0.6)
    1.3%, 0.7%, 0.5% (parallel case, beta = 0)
  Enc time are 99 % to 103 %
  Dec Time are 104% to 105%
DF-combine technique
  good coding performance
  easily applicable for any other ALF techniques due to adding-only-one-pixel feature
propose to adopt this tool into HM
  WD2 base drafted text has been prepared.
<number>
Notes: <number>

## Slide 3: Contents
CE8 experiment
DF-combined ALF
Experimental results
Conclusion
<number>
Notes: <number>

## Slide 4: DF-combined ALF
Features
  Support two input in luma filtering
    pre-DF samples and post-DF samples are used.
    the number of inputs is signaled as alf_num_input_minus1
  Support parallel mode
    non-parallel mode
      use post-DF samples to apply spatial filter
    parallel mode
      use pre-DF samples to apply spatial filter
<number>
spatial filter
spatial filter
Notes: <number>

## Slide 5: Deblocking parameter adjustment
To achieve maximum performance, deblocking parameter is adjusted
  Non parallel case
    beta = -0.6 (const)
  Parallel case
    beta = 0
  Beta value is sent in the slice header as AVC/H.264
<number>

## Slide 6: CE8 Experimental results
<number>
 | Intra |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.5 | 0.0 | 0.0
Class B | -1.2 | 0.0 | 0.0
Class C | -0.9 | 0.0 | 0.0
Class D | -0.7 | 0.1 | 0.1
Class E | -1.0 | 0.0 | 0.0
All | -1.1 | 0.0 | 0.0
Enc Time[%] | 103 % |  | 
Dec Time[%] | 104 % |  | 
 | Random access |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.1 | 0.0 | 0.0
Class B | -0.9 | 0.0 | 0.1
Class C | -0.5 | 0.0 | 0.0
Class D | -0.3 | 0.0 | 0.2
Class E |  |  | 
All | -0.7 | 0.0 | 0.1
Enc Time[%] | 100 % |  | 
Dec Time[%] | 104 % |  | 
 | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -0.9 | -0.1 | -0.1
Class C | -0.4 | 0.1 | 0.1
Class D | -0.4 | 0.2 | 0.0
Class E | -1.5 | -0.4 | 0.3
All | -0.7 | 0.0 | 0.0
Enc Time[%] | 99 % |  | 
Dec Time[%] | 104 % |  | 
 | Intra |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.0 | 0.0 | 0.0
Class B | -1.4 | 0.0 | 0.0
Class C | -1.0 | 0.0 | 0.0
Class D | -0.9 | 0.1 | 0.1
Class E | -1.0 | 0.0 | 0.0
All | -1.3 | 0.0 | 0.0
Enc Time[%] | 103 % |  | 
Dec Time[%] | 104 % |  | 
 | Random access |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.1 | -0.1 | -0.3
Class B | -0.8 | 0.0 | -0.1
Class C | -0.6 | 0.0 | -0.1
Class D | -0.4 | 0.0 | 0.0
Class E |  |  | 
All | -0.7 | 0.0 | -0.1
Enc Time[%] | 100 % |  | 
Dec Time[%] | 105 % |  | 
 | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -0.6 | -0.2 | -0.6
Class C | -0.3 | 0.0 | 0.0
Class D | -0.5 | -0.5 | -0.1
Class E | -0.9 | -0.5 | 0.0
All | -0.5 | -0.3 | -0.2
Enc Time[%] | 100 % |  | 
Dec Time[%] | 104 % |  | 
Notes: <number>

## Slide 7: Memory access
Memory access does’nt increased much when DF and ALF perform simultaneously.
<number>
Wiener-based filter ( ALF )
De-blocking filter ( DF )
Wiener-based filter ( ALF )
De-blocking filter ( DF )
Internal memory
External memory
Internal memory
External memory
Conventional
system
Proposed system
Internal memory access

## Slide 8: Conclusion
Performance results
  BD gains
    1.1%, 0.7%, 0.7% (non-parallel case, beta = -0.6)
    1.3%, 0.7%, 0.5% (parallel case, beta = 0)
  Enc time are 99 % to 103 %
  Dec Time are 104% to 105%
DF-combine technique
  good coding performance
  easily applicable for any other ALF techniques due to adding-only-one-pixel feature
propose to adopt this tool into HM
  WD2 base drafted text has been prepared.
<number>
Notes: <number>

## Slide 9
<number>
Thank you
Notes: <number>

## Slide 10: Syntax
<number>
Notes: <number>