## Slide 1: Region-based adaptive loop filter using two-dimensional feature (JCTVC-E141)
Tomohiro Ikai
Takanori Yamazaki
SHARP Corporation
5th JCT-VC Meeting, Geneva, Switzerland, March 2011
Notes: <number>

## Slide 2: Overall Summary
Region-based adaptive loop filter
  Block adaptation (BA)
    4x4 block(or 4x2 block)
    6-level activity and 3-level direction
    hierarchical region representation
  Gains
    IO / RA / LD = 0.2 % / 0.5% / 0.6 %
      Enc Time: 83%, 94%, 94%
      Dec Time: 96%, 98%, 99%
propose to adopt 4x4 BA into HM
  WD2 base drafted text has been prepared.
<number>
#All HE case, negative value is better
Notes: <number>

## Slide 3: Contents
Proposed technique
Experimental result
Block size comparison
Conclusion
<number>
Notes: <number>

## Slide 4: Proposed technique
Concept
  Two-dimensional feature
    Each MxN block is classified into up-to eighteen regions using the two-dimensional feature.
      6-level activity and 3-level direction
  Hierarchical region division
    First split and second split is used for region division
  Region-based ALF
    Each divided region is filtered with the associated filter coefficients which are sent in the bitstream.
<number>
Notes: <number>

## Slide 5: Two-dimensional feature division
Image is divided into up to 18 regions
  on a 4x4 block accuracy
  depending the block’s two-dimensional feature
    Activity: up to 6 levels
    Direction: up to 3 kinds
<number>
(low)
Activity
(6 levels)
Direction (3 kinds)
(high)
2-D feature space
low activity x no directional edge
high activity x horizontal edge
medium activity x vertical edge
Image
18 regions
    Maximum number of regions is 18 = 6 x 3
Notes: <number>

## Slide 6: Activity and Direction calculation
Two features of the MxN block is calculated by the two steps.
  Step1: ActHorz and ActVert is calculated.
  Step 2: Activity and Direction is decided.
    Activity is decided with un-uniform thresholds.
<number>
M+2
M
N+2
N
Notes: <number>

## Slide 7: Hierarchical region division
First split
  Image is divided using Activity into up to 3 regions
  First split has 3 patterns
    signaled with num_first_split_minus1
<number>
Activity
Direction
First split
num_of_first_split_minus1
0
2
1
Notes: <number>

## Slide 8: Hierarchical region division
Second split
  Each first splitted region is further divided using Activity and Direction into up to 6 regions
  Second split has 8 patterns
    signaled with second_split_type
<number>
Second split
0
second_split_type
1
2
3
5
6
7
4
a first splitted region
Notes: <number>

## Slide 9: Example of hierarchical region division
First split
  Image is divided into 3 regions in first split
    low activity, medium activity and high activity regions
Second split
  low activity region is divided into 2 regions by Activity
  medium activity region is divided into 4 regions by Activity and Direction
  high activity region is divided into 3 regions by Direction
In the result
  Image is divided into 9 (=2 + 4 + 3) regions
<number>
Activity
Direction
First split
Second split
low
activity
medium
activity
high
activity
2
4
3
num of region
9
=
Notes: <number>

## Slide 10: Experimental results
<number>
reference: HM2.0
 | Intra |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.2 |  | 0.0 |  | 0.0
Class B | -0.3 |  | 0.0 |  | 0.0
Class C | -0.3 |  | 0.1 |  | 0.1
Class D | 0.0 |  | 0.2 |  | 0.2
Class E | -0.3 |  | 0.1 |  | 0.1
All | -0.2 |  | 0.1 |  | 0.1
Enc Time[%] | 83 % |  |  |  | 
Dec Time[%] | 96 %(Linux) ¦ 88 %(Win) |  |  |  | 
 | Random access |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.7 |  | 0.0 |  | 0.0
Class B | -0.8 |  | 0.0 |  | 0.0
Class C | -0.4 |  | 0.0 |  | 0.1
Class D | -0.2 |  | -0.1 |  | 0.0
Class E |  |  |  |  | 
All | -0.5 |  | 0.0 |  | 0.0
Enc Time[%] | 94 % |  |  |  | 
Dec Time[%] | 98 %(Linux) ¦ 90 % (Win) |  |  |  | 
 | Low delay |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A |  |  |  |  | 
Class B | -0.7 |  | 0.3 |  | 0.2
Class C | -0.5 |  | 0.2 |  | 0.1
Class D | -0.5 |  | -0.3 |  | 0.0
Class E | -1.0 |  | 0.6 |  | 0.6
All | -0.6 |  | 0.1 |  | 0.2
Enc Time[%] | 94 % |  |  |  | 
Dec Time[%] | 99 %(Linux) ¦ 90 %(Win) |  |  |  | 
Notes: <number>

## Slide 11: Block size comparison
The smaller block size is the better coding efficiency, while the encoding time and decoding time increases.
<number>
 | Intra |  |  |  | 
 | 4x4※ | 4x2 | 4x1 | 2x2※ | 1x1
Class A | -0.2 | -0.3 | -0.4 | -0.4 | -0.5
Class B | -0.3 | -0.3 | -0.4 | -0.4 | -0.4
Class C | -0.3 | -0.4 | -0.4 | -0.5 | -0.6
Class D | 0.0 | -0.1 | -0.2 | -0.3 | -0.4
Class E | -0.3 | -0.4 | -0.4 | -0.6 | -0.6
All | -0.2 | -0.3 | -0.3 | -0.4 | -0.5
Enc Time[ %] | 83 % | 86 % | 92 % | 94 % | 125 %
Dec Time[%] | 96 % | 96 % | 100 % | 103 % | 108 %
 | Random access |  |  |  | 
 | 4x4※ | 4x2 | 4x1 | 2x2※ | 1x1
Class A | -0.7 | -0.8 | -0.9 | -0.8 | -0.9
Class B | -0.8 | -1.0 | -1.0 | -1.1 | -1.1
Class C | -0.4 | -0.6 | -0.6 | -0.7 | -0.8
Class D | -0.2 | -0.3 | -0.4 | -0.5 | -0.6
Class E |  |  |  |  | 
All | -0.5 | -0.7 | -0.7 | -0.8 | -0.9
Enc Time[%] | 94 % | 95 % | 97 % | 97 % | 106 %
Dec Time[%] | 98 % | 98 % | 103 % | 104 % | 114 %

## Slide 12: Conclusion
Region-based adaptive loop filter
  Block adaptation (BA)
    4x4 block(or 4x2 block)
    6-level activity and 3-level direction
    hierarchical region representation
  Gains
    IO / RA / LD = 0.2 % / 0.5% / 0.6 % in 4x4 block
      Enc Time: 83%, 94%, 94%
      Dec TIme: 96%, 98%, 99%
        on Windows 88%, 90%, 90%
    IO / RA / LD = 0.4 % / 0.8% / 1.0 % in 2x2 block
      Enc Time: 94%, 97%, 97%
      Dec TIme: 103%, 104%, 106%
        on Windows 93%, 95%, 96%
propose to adopt 4x4 BA into HM
  WD2 base drafted text has been prepared.
<number>
#All HE case, negative value is better
Notes: <number>

## Slide 13
<number>
Thank you
Notes: <number>