## Slide 1: CE5: Counter based adaption for LCEC
Liwei Guo, Bin Li, Xianglin Wang, Marta Karczewicz and Jizheng Xu
Qualcomm University of Science &Technology of China Microsoft

## Slide 2: LCEC
Lookup table is widely used
Current design
  Directly swap when one code word comes

## Slide 3: Counter based adaptation
Adapted to
  CBF tables (the first four codewords)
  Split tables for inter mode (the first four codewords)
  Block CBP tables (the first two codewords)
  MI1 table for inter prediction direction and reference frame index (the first two codewords)
  Four sum counters for each table
  4 bits for sum counters and 5 bits for codeword counters

## Slide 4: Counter adaptation
Swap when counter[i] >= counter[i-1]
When sum counter reaches 16
  Each counter shift right one bit
  Set sum counter zero

## Slide 5: Experiment result
 | AI_LC | RA_LC | LD_LC
Class A | -0.2 | -0.5 | N/A
Class B | -0.1 | -0.5 | -0.9
Class C | -0.1 | -0.6 | -1.0
Class D | -0.1 | -0.6 | -0.7
Class E | -0.3 | N/A | -0.8
All | -0.2 | -0.5 | -0.8
Enc Time | 100% | 98% | 99%
Dec Time | 100% | 100% | 100%

## Slide 6: Conclusion
Performance improvement without noticeable impact on complexity
Suggest to adopt counter base LCEC in HM