## Slide 1: CE12, Subset 1: Report of Deblocking for Large-size Blocks
Zhongbo Shi
Xiaoyan Sun
Jizheng Xu
Microsoft

## Slide 2: Outline
Deblocking for large-size blocks revisit
  Which has been presented in JCTVC-C273 and JCTVC-D137
  General idea: a stronger deblocking for large blocks (smooth regions)
CE results
Conclusion

## Slide 3: Deblocking for Large-size Blocks
Perform a strong and long filter to some TU boundaries
  Apply to smooth region to further reduce blocking artifacts
Deblocking is changed to TUs, which satisfy the following conditions
  The two adjacent TU’s related to the TU boundary are both in intra-coded CU’s
  The smaller transform size between the two TU's is larger than a certain value(set to 8 in the proposed scheme)
  The larger transform size between the two TU's is larger than a certain value(set to 16 in the proposed scheme)
  The sum of absolute difference between the luminance values inside two TUs and average values of tow TU’s boundary pixels is smaller than a certain threshold(set to 512 in the proposed scheme)
  For luminance, an additional condition should be satisfied:
  All the pixels at the TU boundaries should be processed as strong filtering in default filtering mode

## Slide 4: The proposed deblokcing filter

## Slide 5: Experiments
HM2.0
Compared with the anchors for all test sequences

## Slide 6: Experimental results – All Intra
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.1 | -0.1 | 0.0 | 0.0 | 0.0
Class B | 0.0 | -0.1 | -0.1 | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.0 | -0.2 | -0.2 | 0.0 | 0.0 | 0.0
All | 0.0 | -0.1 | -0.1 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 102% |  | 

## Slide 7: Experimental results – random access
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.2 | -0.2 | 0.0 | 0.0 | 0.0
Class B | 0.0 | 0.0 | -0.1 | 0.0 | 0.0 | 0.0
Class C | 0.0 | -0.1 | -0.1 | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E |  |  |  |  |  | 
All | 0.0 | 0.0 | -0.1 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 98% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 8: Experimental results – low delay
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.0 | -0.1 | 0.0 | 0.0 | 0.1
Class C | 0.0 | 0.2 | 0.2 | -0.1 | 0.0 | -0.2
Class D | 0.0 | 0.0 | -0.2 | 0.0 | -0.1 | -0.1
Class E | -0.1 | -0.2 | 0.4 | 0.0 | 0.2 | 0.2
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 9: Visual quality evaluation
Visual improvements (Less blocking artifacts)
For Kimono(sky and face area) and Parkscene( trunk area)
All Intra, Low-delay and RA at low bit-rates (QP37 or 32)

## Slide 10: Visual comparison
Examples extracted from Kimono( All Intra, HE, QP37)
The Anchor

## Slide 11: Visual comparison
Examples extracted from Kimono( All Intra, HE, QP37)
The Proposal

## Slide 12: Conclusion
A stronger deblocking applied to large smooth region
Little impact on the objective quality and complexity
Better visual quality by further reducing blocking artifacts
Can be more useful for even higher resolution videos
Propose to consider a stronger deblocking for large blocks in the design