## Slide 1: On merge candidate construction
Bin Li, Jizheng Xu, Feng Wu and Houqiang Li
University of Science & Technology of China Microsoft

## Slide 2: Merge mode
Partial merge
Unclear when the first part is inferred as merge mode but the number of candidates is 0

## Slide 3: Solution
Add one all 0 candidate, when the set of merge candidate is empty
  list 0 prediction
  reference frame index = 0
  mv_x = mv_y = 0

## Slide 4: Result of adding zero merge candidate
Do not have impact on RD performance and complexity
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 0.0 | -0.1 |  | 
Class B | 0.0 | 0.0 | 0.0 | 0.0
Class C | -0.1 | -0.1 | 0.0 | 0.0
Class D | 0.0 | 0.0 | -0.1 | 0.0
Class E |  |  | -0.2 | 0.0
All | 0.0 | 0.0 | -0.1 | 0.0
Enc Time | 102% | 99% | 101% | 100%
Dec Time | 100% | 100% | 100% | 100%

## Slide 5: Merge candidate independent merge flag decoding
Decoding process of merge flag in the current HM

## Slide 6: Proposed decoding of merge flag
The merge candidates only needs to be constructed when it is merge mode

## Slide 7: Extension of the solution
Add zero motion to the candidate list
  Handle the cases when there is no candidate
  Lead to always coding of merge flag
Always code merge flag
  Make merge flag coding independent of the number of different candidates
  No need to construct MVP candidates when merge is not used
    Reduce complexity

## Slide 8: Results
Do not have much impact on RD performance and complexity
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 0.0 | -0.1 |  | 
Class B | 0.0 | 0.0 | 0.0 | 0.0
Class C | 0.0 | -0.1 | 0.0 | 0.0
Class D | 0.0 | 0.0 | -0.1 | 0.0
Class E |  |  | 0.1 | 0.0
All | 0.0 | 0.0 | 0.0 | 0.0
Enc Time | 101% | 99% | 102% | 100%
Dec Time | 100% | 100% | 100% | 100%

## Slide 9: Similar solution
In JCTVC-E118, similar algorithm, similar result
Difference is when it is inter B slice, the added merge candidate is bi-direction prediction
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 0.1 | 0.0 |  | 
Class B | 0.0 | 0.0 | -0.1 | 0.0
Class C | 0.0 | -0.1 | 0.0 | -0.1
Class D | 0.0 | 0.0 | -0.1 | 0.0
Class E |  |  | -0.1 | 0.0
All | 0.0 | 0.0 | -0.1 | 0.0
Enc Time |  |  |  | 
Dec Time |  |  |  | 

## Slide 10: Conclusion
Add zero merge candidate when the set of merge candidate is empty
Make the parsing of merge flag independent with the merge candidate
Propose that these two modifications to be adopted by HM