## Slide 1: On motion information compression
University of Science and Technology of China Microsoft

## Slide 2: Current MV compression
Use the mv in block 0

## Slide 3: improvement
Not only compress the MV, but also compress the mode and reference frame index
  Mode to decide using temporal MV or not
  Reference frame index used to scale
  Should not mismatch
Use the mv in block 15 (last block)
Scan in 15, 11, 7, and 3 to find the first available one
Slightly change the center position of TMVP
  Change from A to B

## Slide 4: Mode and ref idx compression(1)
Looks like a bug fix
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 0.1 | 0.1 |  | 
Class B | 0.0 | 0.0 | 0.0 | -0.1
Class C | 0.0 | 0.0 | -0.1 | -0.1
Class D | -0.1 | -0.1 | -0.2 | -0.1
Class E |  |  | -0.1 | -0.1
All | 0.0 | 0.0 | -0.1 | -0.1
Enc Time | 100% | 98% | 100% | 100%
Dec Time | 101% | 101% | 101% | 101%

## Slide 5: (1) + using the MV in block 15(2)
Performance gain significantly without impact on complexity
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | -0.5 | -0.5 |  | 
Class B | -0.3 | -0.5 | -0.4 | -0.7
Class C | -0.5 | -0.6 | -0.6 | -0.8
Class D | -0.9 | -0.9 | -0.8 | -0.8
Class E |  |  | -0.8 | -0.5
All | -0.5 | -0.6 | -0.7 | -0.7
Enc Time | 100% | 98% | 101% | 100%
Dec Time | 101% | 101% | 101% | 101%

## Slide 6: (1) + scan(3)
Similar result to (2), a little improvement
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | -0.5 | -0.5 |  | 
Class B | -0.4 | -0.3 | -0.4 | -0.5
Class C | -0.6 | -0.6 | -0.7 | -0.8
Class D | -0.9 | -0.9 | -0.8 | -0.8
Class E |  |  | -0.8 | -0.6
All | -0.6 | -0.6 | -0.7 | -0.7
Enc Time | 100% | 99% | 100% | 99%
Dec Time | 100% | 101% | 101% | 101%

## Slide 7: Disabling TMVP in merge mode(4)
Performance gain
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 0.0 | -0.1 |  | 
Class B | 0.0 | -0.2 | 0.0 | -0.5
Class C | -0.1 | -0.2 | 0.0 | -0.3
Class D | 0.0 | -0.2 | -0.3 | -0.4
Class E |  |  | -0.3 | -0.4
All | 0.0 | -0.2 | -0.1 | -0.4
Enc Time | 96% | 97% | 96% | 100%
Dec Time | 101% | 100% | 99% | 100%

## Slide 8: (2)+(4)
These two methods do not conflict with each other
The result roughly equals to the result in (2)and the result in (4)
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | -0.4 | -0.6 |  | 
Class B | -0.3 | -0.7 | -0.4 | -1.1
Class C | -0.6 | -0.7 | -0.7 | -1.1
Class D | -0.9 | -1.0 | -1.0 | -1.2
Class E |  |  | -0.9 | -0.9
All | -0.5 | -0.7 | -0.7 | -1.1
Enc Time | 95% | 100% | 95% | 97%
Dec Time | 100% | 100% | 99% | 100%

## Slide 9: (2) + slightly change the center position of TMVP
Further improvement
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | -0.6 | -0.6 |  | 
Class B | -0.5 | -0.7 | -0.5 | -0.8
Class C | -0.6 | -0.7 | -0.7 | -0.8
Class D | -1.0 | -1.0 | -0.9 | -0.8
Class E |  |  | -0.6 | -0.8
All | -0.7 | -0.7 | -0.7 | -0.8
Enc Time | 99% | 98% | 98% | 99%
Dec Time |  |  |  | 

## Slide 10: Conclusion
Disabling TMVP in merge mode
Compress the mode and reference frame index together as a bug fix
Using the MV in the last block instead of the MV in the first block
Slightly change the center position of TMVP