## Slide 1: Simplification of transform coefficients coding in LCEC (JCTVC-E156)
Yukinobu Yasugi
Tomoyuki Yamamoto
SHARP Corporation
JCT-VC 5th meeting, Geneva, CH, 16-25 March, 2011

## Slide 2: Summary
Simplification of transform coeff coding in CAVLC
Change:
  bypass run mode when last_coeff_level>1 in intra TU
Simplification:
  reduce some process in codeNum derivation in run mode
  reduce size of table used to derive codeNum by 20%
Coding efficiency impact:
  Negligible --- 0.0% on average
Cross check
  E169 by Sony

## Slide 3: Coefficient coding in HM-2.0
Three steps of coefficient coding:
  Last non-zero coefficient
  Run mode loop
    code {run-level} pairs
    conditions to exit loop
    executed once at least to exit
  Level mode loop
    code coeffs one-by-one
parse/code Coeff
Run-mode loop
Level-mode loop
Last non-zero coeff
Done
Block size | condition
4x4 | Level>1
8x8+ | Level>1 && (pos>th ¦¦ sum_of_big_coeff>2)
8x8+ intra luma | Level >1 (because th=0)

## Slide 4: Coefficient coding in HM-2.0
Run-mode is sometimes executed unnecessarily.
0 0 0 0 0 2 0 2 2 1 2 1 1 4 3 5
4x4 coeffs
last non-zero coeff (level>1)
second last non-zero coeff
DC coeff
Run-mode
Level-mode
5 3 2 1
4 1 2 0
1 0 0 0
2 0 0 0
0 0 0 0 0 2 0 2 2 1 2 1 2 4 3 5
In such a case, Level-mode will be enough and simple.
HM-2.0:
ideal:
scan

## Slide 5: Simplification of Run-mode coding (1)
Bypassing run-mode
  to avoid entering unnecessary run-mode
  bypassing is selected depending on the last coeff’s level (i.e. bypass if last_level>1)
  apply only to Luma-Intra blocks
    relatively high levels
  reduce some codes and tables regarding last_level>1 case inside run-mode loop
parse/code Coeff
Run-mode loop
Level-mode loop
Last non-zero coeff
level>1 && Luma Intra Block?
Run-mode Bypassing
Done
Yes
No

## Slide 6: Simplification of Run-mode coding (2)
  example: reduction of codeNum mapping function
__inline UInt xRunLevelInd(Int lev, Int run, Int maxrun, UInt lrg1Pos)
{
UInt cn;
if ( lrg1Pos > 0 )
{
if ( lev == 0 )
{
if ( run < lrg1Pos )
cn = run;
else
cn = (run << 1) - lrg1Pos + 1;
}
else
{
if ( run > (maxrun - (Int)lrg1Pos + 1) )
cn = maxrun + run + 2 ;
else
cn = lrg1Pos + (run << 1);
}
}
else
{
cn = (run << 1);
if ( lev == 0 && run <= maxrun )
{
cn++;
}
}
return(cn);
}
__inline UInt xRunLevelInd(Int lev, Int run, Int maxrun, UInt lrg1Pos)
{
UInt cn;
if ( lev == 0 )
{
if ( run < lrg1Pos )
cn = run;
else
cn = (run << 1) - lrg1Pos + 1;
}
else
{
if ( run > (maxrun - (Int)lrg1Pos + 1) )
cn = maxrun + run + 2 ;
else
cn = lrg1Pos + (run << 1);
}
return(cn);
}
(a) Original
(b) Simplified

## Slide 7: Experimental results
Reference: HM2.0(rev.572)
Evaluated: Reference + proposed modification
No significant impact on BD-rates and complexity.
 | Intra LoCo |  |  | Random access LoCo |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 |  |  | 
Class B | 0.0 | 0.0 | 0.1 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | 0.2
Class C | 0.0 | 0.0 | 0.0 | 0.0 | -0.2 | 0.1 | -0.1 | -0.1 | -0.2
Class D | -0.1 | 0.0 | 0.0 | 0.0 | -0.1 | 0.0 | 0.1 | 0.1 | 0.1
Class E | 0.0 | 0.0 | 0.1 |  |  |  | 0.1 | -0.6 | 0.3
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | 0.1
Enc Time | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time | 100% |  |  | 99% |  |  | 101% |  | 

## Slide 8: Conclusion
Simplification of transform coeff coding in CAVLC
Change:
  bypass run mode if last_coeff>1 in intra TU
Simplification:
  reduce some process in codeNum derivation in run mode
  reduce size of table used to derive codeNum by 20%
Coding efficiency impact:
  Negligible --- 0.0% on average
Cross check
  E169 by Sony
Recommend to adopt Run-mode bypassing into HM