## Slide 1: Modified joint coding on Prediction mode signaling
Jaehyun Lim
LG Electronics
JCTVC-E160

## Slide 2: Introduction
Prediction mode signaling in HM 2.0
  Joint coding of prediction mode & partition size
  Adaptive mapping between symbol and codeword index (CU based)
prediction mode | partitioning type | symbol | 
 |  | CU size > min | CU size = min
SPLIT |  | 0 | -
SKIP |  | 1 | 1
CU MRG |  | 2 | 2
INTER | 2Nx2N | 3 | 3
 | 2NxN | 4 | 4
 | Nx2N | 5 | 5
 | NxN | - | 6
INTRA | 2Nx2N | 6 | 
 | NxN | - | 
Symbols for representing prediction mode and partitioning type in HM 2.0

## Slide 3: Introduction
Motivation
  The effect of the mapping table adaptation is occurred in the trade off of positive case and negative case
  By the statistical analysis, the range of prediction mode signaling is limited to commonly selected modes (e.g. SPLIT, SKIP, MRG, …)
  Through the limitation of joint coding range to prediction mode, the negative case can be reduced

## Slide 4: Proposed method
prediction mode | partitioning type | symbol | 
 |  | CU size > min | CU size = min
SPLIT |  | 0 | -
SKIP |  | 1 | 0
CU MRG |  | 2 | 1
INTER | 2Nx2N | 3 | 2
 | 2NxN |  | 
 | Nx2N |  | 
 | NxN | - | 4
INTRA | 2Nx2N | 4 | 3
 | NxN | - | 
Modification of joint coding range
  Limited to prediction mode only
  After decision of INTER or INTRA mode, partition indicator is signaled
Symbols for representing prediction mode and partitioning type in the proposed method

## Slide 5: Proposed method
Initial mapping table rearrangement
  Reflecting the distribution of each prediction modes
  Independent rearrangement by depth
Chart: 
| 64x64 | 32x32 | 16x16 | 8x8
split | 55.2197 | 46.8067 | 26.5596 | 0
skip | 25.2618 | 19.1571 | 21.7807 | 21.5383
MRG | 8.3892 | 12.3519 | 19.3374 | 30.4585
INTER | 10.8256 | 19.3058 | 25.099 | 28.7254
INTRA | 0.30371 | 2.3786 | 7.2233 | 17.01
NxN INTER | 0 | 0 | 0 | 2.2678

## Slide 6: Experimental Results
BD rate(%) reduction of the proposed method
BD-rate reduction & complexity
  Avg. gain for RA LoCo: 0.1%
  Avg. gain for LD LoCo: 0.1%
  No change in encoder/decoder complexity
 | Random access LoCo |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.1 | -0.1 |  |  | 
Class B | 0.0 | 0.0 | 0.0 | -0.1 | 0.0 | 0.0
Class C | -0.1 | -0.1 | -0.1 | -0.2 | -0.2 | -0.6
Class D | -0.2 | -0.2 | -0.2 | -0.2 | -0.5 | -0.3
Class E |  |  |  | 0.2 | 0.0 | -0.2
All | -0.1 | -0.1 | -0.1 | -0.1 | -0.2 | -0.3
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 7: Conclusion
Modified Joint coding of prediction mode signaling is proposed.
The proposed scheme shows bit-rate reduction without any computational change.