## Slide 1: Wavefront Parallel Processing JCTVC-E196
Félix Henry, Stéphane Pateux – ORANGE LABS
Notes: presentation title
<number>

## Slide 2: Introduction
Method to perform high-level parallel video encoding and decoding using HEVC
Evolution of interleaved entropy slice
  JCT-VC-D070/D073 Entropy Slices presented by Sharp
  VCEG-AK25 “Ordered Entropy Slices for Parallel CABAC” from Mediatek
    Showing importance of preserving LCU dependencies and influence of context initialization
  VCEG-AL21 “Massively Parallel CABAC” and JCTVC-D243 “Analysis of entropy slice approaches” from TI
    Introducing interleaved entropy slices
    Recommending them for
      throughput
      memory (no need to buffer syntax elements)
Notes: presentation title
<number>

## Slide 3: Sequential processing of HEVC LCUs
Single-thread processing of HEVC encoding/decoding
X
Pixel and MV dependency
Probabilties dependency
X
Block(s) being encoded
CABAC probabilitites
KEY
JCTVC-E196
Notes: presentation title
<number>

## Slide 4: Wavefront processing of HEVC LCUs (ideally)
X
X
X
X
Pixel and MV dependency
Probabilties dependency
X
Block(s) being encoded
CABAC probabilitites
KEY
JCTVC-E196
Parallel processing without breaking pixel/MV dependency
Notes: presentation title
<number>

## Slide 5: Wavefront processing of HEVC LCUs (problem)
Probabilities not available on first LCU of the line!
If we re-initialize at the beginning of each LCU line, performance degradation (cf. related contributions)
X
X
X
X
Probabilities not available!
Notes: presentation title
<number>

## Slide 6: Proposal: Wavefront Parallel Processing of LCUs (WPP)
Synchronize CABAC probabilities with upper-right LCU
  Upper-right LCU available anyway, due to spatial/MV dependency
  Efficiently carries over quick vertical learning of probabilities
  Only one additional CABAC context buffer shared between all threads
X
X
X
X
Notes: presentation title
<number>

## Slide 7: Performance
Test conditions
  HM2.0
  JCT-VC-D600 conditions
  High Efficiency
  Intra, Low delay, Random Access
  Anchors are basic HM2.0 (no slices)
  Includes substream signalling
    Performance presented for 2 substreams
    The cost of adding one more substream is only the substream entry points and terminating bits (less than 0.1% per substream with our dumb substream pointers)
  Has been combined with SHARP’s JCTVC-E409 proposal on substream headers (contribution JCTVC-E470)
JCTVC-E196
Notes: presentation title
<number>

## Slide 8: Advantages
Several advantages already described in references
Size of « content » part of the bitstream is independent from the number of threads
  Only add substream entry points and terminating bits
Transcoding to any level of parallelism is an entropy-level operation
  Special interest to transcode non-parallel to parallel-friendly
Compatible with other approaches (Tiles, Entropy Slices…)
JCTVC-E196

## Slide 9: Conclusion
Full Wavefront Parallel Processing is made possible without large R/D performance loss (I 0.1%, RA 0.8%, LD 1.3%)
There are several advantages to this approach
We would like to submit for adoption
Verification performed by SHARP (JCTVC-E415)
JCTVC-E196
Notes: presentation title
<number>