## Slide 1: Comments on the Common Test Conditions for ALF (JCTVC-E197)
Ming LI, Ping Wu, Lei Wang, Wen Zhang

## Slide 2: Introduction
In the current recommended common test conditions,
  ALF is On for RAHE and LDHE;
  ALF is Off for RALC and LDLC for its complexity problem.
To tackle the complexity problem, two alternative configurations for ALF are proposed to reduce the computational burden as
  For RA cases using the dyadic hierarchical prediction structure, ALF is applied to the frames which are employed as reference for coding successive frames.
  For LD cases using hierarchical QP assignment, ALF is applied to I-frames and the P/B frames with the smallest QP (currently QPI + 1).

## Slide 3: Experimental Results
 |  | Random access | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.6 | -0.1 | -0.1
Class B | 0.4 | -0.1 | -0.1
Class C | 0.2 | -0.1 | -0.1
Class D | 0.3 | -0.1 | -0.1
Class E |  |  | 
All | 0.3 | -0.1 | -0.1
Enc Time[%] | 96% |  | 
Dec Time[%] | 69% |  | 
 | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 2.1 | 0.7 | 0.4
Class C | 1.2 | 0.6 | 0.9
Class D | 1.0 | -0.3 | -0.2
Class E | 1.3 | -0.8 | -0.2
All | 1.4 | 0.1 | 0.2
Enc Time[%] | 96% |  | 
Dec Time[%] | 70% |  | 

## Slide 4: Conclusions
In this document, two alternative configurations for ALF are proposed for the inter frame test conditions recommended in JCTVC-D600.
Based on the experimental results, it is suggested to adopt the proposed configurations to RAHE and LDHE test conditions for the trade-off between coding efficiency and complexity.