## Slide 1: Constrained Intra Prediction for Flexible-Sized Prediction Units in HEVC
Viktor Wahadaniah
Chong Soon Lim
Sue Mon Thet Naing
Panasonic Corporation
JCTVC-E203
5th JCT-VC meeting, Geneva, 16-23 March 2011

## Slide 2: Summary
AVC-style constrained intra prediction (JCTVC-D086) was adopted into HM 2.0 in Daegu meeting.
This contribution presents HM-2.0-based experimental results for HEVC-adapted constrained intra prediction scheme initially proposed in JCTVC-D094.
Basic concept:
  Due to flexible-sized prediction units in HEVC, intra-prediction reference samples are partially available in some cases. Such available samples can be used for deriving non-available reference samples.
  Currently not done in AVC-style constrained intra prediction of HM 2.0.
Luma BD-rate gains of HEVC-adapted constrained intra prediction scheme are 0.2% (Random access), 0.3% (Random access LoCo), 0.1% (Low delay), and 0.1% (Low delay LoCo), without increase in encoder/decoding runtime. We thank NEC for cross-checking this proposal.
Recommendations:
  Include the proposed “design bugfix” into HM 3.0.
  Investigate constrained intra prediction design for other intra prediction schemes besides directional intra prediction scheme.

## Slide 3: AVC-Style Constrained Intra Prediction Scheme
In this example, some neighboring PUs are intra-predicted (blocks C, G, J, and K).
Using AVC-style constrained intra prediction:
  Only DC intra prediction mode can be used.
  DC-mode prediction value is set to 128 (neighboring intra-predicted samples are ignored).

## Slide 4: Proposed Scheme
pT = target inter-predicted sample
pLB = left or below intra-predicted sample
pRA = right or above intra-predicted sample
samples to be re-calculated
Inter-predicted reference samples (blocks A, B, D, E, F, H, and I) are re-calculated using intra-predicted samples:
  When samples on both sides are available:
  pT = (pLB + pRA + 1) >> 1
  When only one side is available:
  pT = pLB -OR- pT = pRA
All directional intra prediction modes remain available to be used.

## Slide 5: Experimental Results on HM-2.0-dev-nec (rev 597)
Table below shows BD-rates of proposed scheme with reference to AVC-style constrained intra prediction scheme (negative value indicates coding gain).
Encoding and decoding runtime is very close (100% for all 4 test settings)
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.04 | -0.24 | -0.11 | -0.10 | -0.18 | -0.66
Class B | -0.15 | -0.27 | -0.32 | -0.32 | -0.50 | -0.45
Class C | -0.29 | -0.39 | -0.48 | -0.48 | -0.74 | -0.89
Class D | -0.25 | -0.28 | -0.24 | -0.37 | -0.59 | -0.56
Class E |  |  |  |  |  | 
All | -0.18 | -0.29 | -0.29 | -0.32 | -0.50 | -0.63
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.06 | -0.11 | -0.15 | -0.11 | -0.30 | -0.25
Class C | -0.07 | -0.13 | -0.09 | -0.17 | -0.34 | -0.33
Class D | -0.03 | 0.22 | -0.62 | -0.09 | -0.26 | 0.08
Class E | -0.13 | -0.68 | -0.12 | -0.11 | 0.27 | 0.02
All | -0.07 | -0.14 | -0.25 | -0.12 | -0.20 | -0.14
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 6: Conclusions
Constrained intra prediction is necessary for controlling spatial error propagation. AVC-style constrained intra prediction (JCTVC-D086) has been adopted in HM 2.0.
AVC-style constrained intra prediction scheme of HM 2.0 does not consider flexible-sized PUs of HEVC.
By adapting constrained intra prediction design to HEVC characteristics, coding efficiency is improved. BD-rate gains of 0.1% to 0.3% are observed without changes in encoding/decoding runtime.
Recommendations:
  Include the proposed “design bugfix” into HM 3.0.
  Investigate constrained intra prediction design for other intra prediction schemes besides directional intra prediction scheme.

## Slide 7: Thank you