## Slide 1: JCTVC-E217: Improved dQP Calculation Method proposed by HKUST
PANG, Chao Oscar C. Au
Hong Kong Univ of Science & Technology
<number>

## Slide 2: Outline
Introduction
  Delta-QP
  Existing dQP signaling methods
Proposed two dQP signaling methods
Experimental Results
Conclusion
<number>

## Slide 3: Proposed Two Methods
In this proposal, the QP prediction method in AVC is extended (with certain modification) to the HM in two different methods.
  Method1: Use the QP value of the previous CU in the coding order;
  Method2: Use the QP value of the left CU.
<number>
Notes: We consider that extension of the QP prediction method in AVC may be a simple and straightforward solution.
<number>

## Slide 4: Proposed Method
For method 2:
  position of the upper-left pixel in current CU is (xc, yc)
  the left CU is the CU that contains the pixel at the position of (xc-1, yc).
  With this specification of the left CU, the left prediction can be applied to the current HM
  Note that the prediction can cross neighbor LCUs
<number>
(a) Method 1
(b) Method 2
Notes:   With this specification of the left CU, the left prediction can be applied to the current HM
where neighboring CUs may have different sizes.
<number>

## Slide 5: Experimental Results
Experiments are conducted based on the numbers of non-zero dQP values using these two QP prediction methods.
  13 internal test sequences are used
  MB-level subjective quality rate control method is employed.
  The detailed results are shown in Table 1.
<number>
Notes:   Context of the sequences are regular
<number>

## Slide 6: Experimental Results
<number>
 | number of non-zero dQP values using Method 1 | number of non-zero dQP values using Method 2 | reduction of number of non-zero dQP values
Sequence 1 | 47884 | 19985 | 58.26%
Sequence 2 | 129832 | 65092 | 49.86%
Sequence 3 | 39401 | 14338 | 63.61%
Sequence 4 | 34268 | 26202 | 23.54%
Sequence 5 | 242069 | 183295 | 24.28%
Sequence 6 | 43892 | 31641 | 27.91%
Sequence 7 | 37144 | 24728 | 33.43%
Sequence 8 | 67174 | 34018 | 49.36%
Sequence 9 | 102506 | 61838 | 39.67%
Sequence 10 | 70733 | 42090 | 40.49%
Sequence 11 | 67572 | 39803 | 41.10%
Sequence 12 | 37571 | 23128 | 38.44%
Sequence 13 | 39363 | 14563 | 63.00%
Average |  |  | 42.54%
Notes: Using the QP of left CU as the QP predictor, on average, the number of non-zero dQP values is reduced by 42%.
<number>

## Slide 7: Conclusion
In this proposal, the QP prediction method in AVC is extended to HM
  the experimental results show that the prediction with the left CU can achieve potentially high efficient dQP computation
  Suggest adopt into the next version of HM or adopt in new CE for further study
<number>

## Slide 8
<number>