## Slide 1: Line memory reduction for ALF decoding
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
5th JCT-VC meeting, Geneva 16.-23. March 2011

## Slide 2: Outline
Introduction
Line memory reduction for ALF decoding
Experiments and results
Conclusion

## Slide 3: Summary
Line memory reduction for ALF by using the pre-deblocked signal at the bottom of LCUs
Significant reduction of decoder line memory by 33% for luma and 20% for chroma components
Same coding efficiency as HM2.0

## Slide 4: Deblocking filtering in HM2.0
Example LCU consisting of four
CUs of 8x8 samples
Deblocking needs to be delayed since the LCU below is not available

## Slide 5: ALF in HM2.0
Not yet deblocked pixels
that delay ALF
Region that can be processed
by both Deblocking filter and ALF
Central filter tap
Required line memory: 9 lines

## Slide 6: Proposed line memory reduction
Basic concept:
ALF uses non-deblocked pixels at the bottom of LCUs
3 lines of non-deblocked
pixels are used by ALF
Central filter tap
Region that can be processed
by both Deblocking filter and ALF
Required line memory: 6 lines

## Slide 7: Results of experiments using common conditions
=> Same coding efficiency

## Slide 8: Complexity analysis
Decoder: Significant reduction of line memory:
  33% for luma
  20% for chroma
Encoder: Marginal increase of required memory: Storage of 3 lines of each LCU of the non-deblocked signal

## Slide 9: Option to avoid the additional memory in encoders
At the bottom of LCUs the encoder decides between:
  Applying ALF using non-deblocked lines
  Applying no ALF
Decision is signaled to the decoder either in the picture or sequence parameter set

## Slide 10: Option to reduce column memory in addition
Not yet deblocked pixels
that delay ALF
Not yet deblocked pixels
that delay ALF
Region that can be processed
by both Deblocking filter and ALF

## Slide 11: Option to reduce column memory in addition
Not yet deblocked pixels
are used by ALF
Region that can be processed
by both Deblocking filter and ALF
Not yet deblocked pixels
are used by ALF

## Slide 12: Option to reduce column memory in addition
=> Same coding efficiency

## Slide 13: Conclusion
Line memory reduction for ALF by using the non-deblocked signal at the bottom of LCUs
Results:
  Significant reduction of decoder line memory:
    33% for luma
    20% for chroma
  Same coding efficiency as HM2.0
  Marginally increased memory requirement in the encoder
Possible options:
  Switch to disable ALF at the bottom of LCUs
    Same significant reduction of decoder line memory
    No increase of memory in encoder
    Slightly decreased coding efficiency (I-HE: 0.14%, RA-HE: 0.21%, LD-HE: 0.32%)
  Additional reduction of column memory
    Same coding efficiency as HM2.0
Proposal: Include into next version of the HM