## Slide 1: JCTVC-E241
Low complexity bi-predictive interpolation with 6-tap DCT-IF filter
Kemal Ugur, Jani Lainema

## Slide 2
At the Daegu meeting, it was decided to use 8-tap DCT-IF for both high efficiency and low complexity
This has some complexity impact compared to previous low complexity configuration:
  ~ 2x average computational complexity increase
  ~30% memory bandwidth increase due to increased tap-length
This proposal aims to reduce especially the worst-case complexity related to interpolation filters.
  Motion-comp. worst-case happens when the motion block is bi-predicted
It is proposed to use 6-tap DCT-IF filter (instead of 8-tap) for bi-prediction for low-complexity
  Same DCT-IF coefficients as in JCTVC-D344, but using 6-bit accuracy (same accuracy as 8-tap DCT-IF)
Proposal is closely related to Sony’s earlier proposals on using different filters for single/bi prediction
  JCTVC-C164, JCTVC-D090, JCTVC-E128
The worst-case interpolation complexity and memory bandwidth is reduced by ~ 30%
For low complexity configuration there is an average 0.5% coding efficiency loss. However:
  When BQSquare is removed, the coding efficiency is unchanged.
  For high-resolution classes (Class A,B,E), the coding efficiency is improved by 0.8%

## Slide 3: JCTVC-E241
The main idea of the proposal is the same as Sony’s CE3 response JCTVC-E128
  Use a different interpolation filter for bi/uni prediction
  Here, the motivation is to reduce the worst-case complexity using a filter with shorter tap-length for bi prediction
Filter for uni-prediction:
Half pixel: [-1, 4,-11, 40, 40,-11, 4, -1]
Quarter pixel: [-1, 4,-10, 57, 19, -7, 3, -1]
Filter for bi-prediction :
Half pixel: [1, -8, 39, 39,-8, 1]
Quarter pixel: [2, -8, 57, 18,-6, 1]

## Slide 4: JCTVC-E241
The proposal aims to reduce the complexity but comes with a gain in coding efficiency for high-resolution sequences
  The gain in coding efficiency is attributed to slight variation in filter responses for uni- and bi-prediction

## Slide 5: Results - Coding Efficiency
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.2 | 0.4 | 0.2 | -0.6 | 0.1 | 0.1
Class B | 0.1 | 0.1 | 0.1 | -0.4 | 0.0 | 0.0
Class C | 1.0 | 0.7 | 0.6 | 1.4 | 0.6 | 0.6
Class D | 2.2 | 1.8 | 1.7 | 3.5 | 1.5 | 1.5
Class E |  |  |  |  |  | 
All | 0.8 | 0.7 | 0.6 | 0.9 | 0.5 | 0.5
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.1 | 0.1 | -0.6 | 0.2 | 0.4
Class C | 0.7 | 1.0 | 0.9 | 0.8 | 0.4 | 0.3
Class D | 1.2 | 2.0 | 1.7 | 2.0 | 0.5 | 0.7
Class E | 0.1 | -0.3 | 0.7 | -2.0 | -0.6 | -0.1
All | 0.5 | 0.7 | 0.8 | 0.1 | 0.2 | 0.3
Some notes:
Majority of the loss is due to Class-D BQSquare sequence (when that sequence is excluded, loss becomes 0 for low-complexity)
For high resolution sequences (Class A, B, E), there is 0.8% improvement on average for low complexity.

## Slide 6: Results - Complexity
The complexity of 6-tap DCT-IF filter is around 70% of 8-tap DCT-IF (using Daegu CE3 complexity estimate).
  This means that the worst-case interpolation complexity is reduced by around 30%.
The worst case memory bandwidth is also reduced by around 33%, due to the reduced number of filter taps.
Very similar to JCTVC-E134 idea but uses 6-tap for all the positions.
JCTVC-E134

## Slide 7: Conclusions
At the last meeting, the 8-tap DCT-IF interpolation filter was adopted, which had a significant complexity increase for low-complexity configuration
This proposal aims to reduce the complexity by using fewer taps for bi-prediction in low-complexity configuration.
The benefits of this proposal are as follows:
  Both the worst-case interpolation complexity and worst-case memory bandwidth is reduced by around 30%.
  This complexity benefit is coming with a small penalty on coding efficiency. (majority of the loss is due to the low resolution BQSquare sequence and when that sequence is excluded, the loss becomes 0.)
  For high resolution sequences (Class A, B, E) where HEVC is arguably more relevant, there is a 0.8% coding efficiency improvement on average for low complexity config.
  The proposal is utilizing well-known 6-tap separable filter using the DCT-IF coefficients, which is earlier shown to be implementation friendly.
  We argue that performance on low-resolution sequences should have less priority when:
    A proposal aims to reduce the complexity and brings coding efficiency for other classes.

## Slide 8: Thank you