## Slide 1: CE4 Subset1: Ericsson fine granularity slices
JCTvc-E260
Rickard Sjöberg, per wennersten
ericsson AB

## Slide 2: problem statement
WD2 restricts slice boundaries to largest CU resolution (LCU)
  Common conditions specifies LCU size of 64x64
  This is 16 times larger than a 16x16 macroblock
  Makes slice size control difficult, e.g. to create slices of max 1500 bytes
  For highly active and hard-to-compress areas, one single CU may be larger than the target number of slice bytes
Reducing the LCU size
  Cost between 1.7% (all Intra) to 3.2% (LD) to go from 64x64 LCU to 32x32 for 1500 byte slices (source: CE4 report JCTVC-E024)
  No guarantee that every 32x32 LCU is smaller than MTU size
Fine granularity slices
  Introduced in October 2010
  Two cross-checked independent implementations presented at this meeting
  Cost compared to HM-2.0-dev-slices for 1500 byte slices is in the 0.1% BDR range

## Slide 3: proposal
We propose to define slices as a sequence of CU blocks instead of maximum CU blocks, i.e. removing the restriction to align slices on LCU boundaries
Fig 1 - 64x64 block split down to 8x8 blocks
Slice address specified by min CU block number
Decoder starts by decoding the largest possible CU at that starting coordinate

## Slide 4: proposal
Slice address signaling is currently using UVLC which may lead to very long VLC code words, close to 32 bits
Entropy of the address is not matched by the UVLC
We propose to replace UVLC coding of slice start by fixed length coding (FLC) with one-bit shortcut for the first block
1920x1080 example: Each picture contains of 32,640 min CU:s of size 8x8
Block nr | UVLC | FLC
0 | 1 | 1
1 | 010 | 0000000000000000
2 | 011 | 0000000000000001
... |  | 
32639 | 00000000000000111111110000000 | 0111111101111111
1 or 16 bits (average = 16.00 bits)
1-29 bits (average for all block numbers = 26.99 bits)
Bitrate saving of 11 bits per additional slice in a picture = 0.1% for those slices assuming 1500 byte slices

## Slide 5: experimental results 1
Anchor: HM-2.0 No slices
Test: Fine-granularity slices 1500 byte slices

## Slide 6: experimental results 2
Anchor: HM-2.0-dev-slices 1500 byte slices
Test: Fine-granularity slices 1500 byte slices
Note that the anchor exceeds the byte limit when single LCUs exceed 1500 bytes

## Slide 7: summary
Removing the restriction of slices to be LCU aligned provides better slice size control
Overhead is in the 0.1 percent range
Well tested by two completely independent parties with cross-checkers
We support the CE conclusion to adopt fine-granularity slices

## Slide 9: Syntax and semantics
first_sctb_is_zero_flag indicates whether the slice address is 0 or not. If first_sctb_is_zero_flag is 1, the variable SliceAddress is set to 0 and the decoding starts with the first LCTB in the picture.
first_sctb_in_slice_minus_1 specifies the address of the first smallest coding tree block in the slice and shall be represented by Ceil(Log2(NumSCTBsInPicture-1)) bits in the bitstream where NumSCTBsInPicture is the number of SCTB:s in a picture. The slice decoding starts with the largest coding unit possible at the slice starting coordinate given by the address.
The slice address is specified as follows:
SliceAddress = first_sctb_in_slice_minus_1 + 1
slice_header( ) { | C | Descriptor
first_sctb_is_zero_flag | 2 | u(1)
if(first_sctb_is_zero_flag == 0) { |  | 
first_sctb_in_slice_minus_1 | 2 | u(v)
} |  | 
See input document for full syntax and semantics changes