## Slide 1: Ericsson deblocking filter
JCTVC-E276
Andrey Norkin, Kenneth Andersson, Rickard Sjöberg
Ericsson

## Slide 2: Reasoning for improving HEVC deblocking
  HEVC deblocking filter:
   = ( 13(q0-p0) + 4(q1-p1) - 5(q2-p2) ) / 32
  p0’ = p0 + 
  q0’ = q0 - 
  p1’ = p1 + /2
  q1’ = q1 - /2
  Things that can be improved:
  Usage of same  for both p1 and q1 even when structure on sides of block boundary is different
  Chroma is only filtered when at least one of adjacent blocks is intra. Therefore, almost no chroma filtering happens on low-delay configuration
p2
p1
p0
q0
q1
q2

## Slide 3: Proposed modifications
Luma filter:
  Filter that has different  values for p1 and q1
  Check for natural edges
  Decision whether to filter one or two pixels
Chroma filter:
  Perform filtering of chroma boundary when there are coefficients in one of two adjacent blocks

## Slide 4: Filter description
 = ( 9(q0 - p0) - 3(q1 - p1) ) /16
p0’ = p0 + 
q0’ = q0 - 
p1 = (p0 - 2p1+ p2 + 2)/4;
p1’ = p1 + p1
q1 = (q0 - 2q1 + q2 - 2)/4;
q1’ = q1 + q1
Filter features:
Different  values for p1 and q1
Modifications of p1 and q1 are adaptive to local structure
Deltas are equal to zero if p2...p0,q0...q2 lie on the same line
p1
p0
q0
q1
q2
p2

## Slide 5: Check for natural edges
  Filter a line across block boundary only if abs() < thr1
q0
q1
q2
p0
p1
p2
p2
p1
p0
q0
q1
q2
abs() = 0
abs() > 0
thr1 = tc(QP)*10

## Slide 6: Number of pixels to be modified
Block P
Block Q
0
0
1
1
2
2
dp = |p22 - 2*p12 + p02| + |p25 - 2*p15 + p05|
dq = |q22 - 2*q12 + q02| + |q25 - 2*q15 + q05|
If dp < thr2
modify p1
If dq < thr2
modify q1
Modify p0 and q0
if the line is to be filtered
thr2= β(QP)/6

## Slide 7: Chroma change
Current HEVC deblocking
  Filter chroma boundary only if one of the adjacent blocks is intra
Proposed modification
  Filter chroma boundary if one of the adjacent blocks is intra
  OR one of the adjacent chroma blocks has coefficients for the corresponding chroma component
Advantages
  Improved chroma performance on low-delay configurations

## Slide 8: Compression performance All-intra
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.0 | 0.0 | 0.0 | -1.5 | 0.0 | 0.0
Class B | -0.7 | 0.0 | 0.0 | -0.8 | 0.0 | 0.0
Class C | -0.6 | 0.0 | 0.0 | -0.8 | 0.0 | 0.0
Class D | -0.5 | 0.0 | 0.0 | -0.6 | 0.0 | 0.0
Class E | -0.9 | 0.0 | 0.0 | -1.0 | 0.0 | 0.0
All | -0.7 | 0.0 | 0.0 | -0.9 | 0.0 | 0.0
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 9: Compression performance Random access
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.1 | 0.0 | 0.0 | -1.4 | 0.8 | 1.1
Class B | -0.9 | -0.2 | -0.4 | -1.0 | -0.1 | -0.1
Class C | -0.8 | -0.2 | -0.2 | -0.8 | 0.3 | 0.0
Class D | -0.6 | -0.3 | -0.3 | -0.6 | -0.1 | 0.0
Class E |  |  |  |  |  | 
All | -0.9 | -0.2 | -0.2 | -0.9 | 0.2 | 0.2
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 10: Compression performance Low delay
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -1.4 | -1.3 | -1.4 | -1.3 | -0.9 | -0.4
Class C | -1.0 | -0.5 | -0.6 | -0.8 | 0.3 | -0.2
Class D | -0.9 | -0.7 | -0.8 | -0.6 | 0.2 | 0.2
Class E | -3.3 | -3.8 | -3.2 | -2.6 | -4.7 | -3.3
All | -1.5 | -1.4 | -1.4 | -1.2 | -1.0 | -0.7
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 98% |  |  | 101% |  | 

## Slide 11: Decoding time on same platform
Configuration | Dec. time proposal [s] | Dec. time HM2.0 [s] | Dec. time proposal [%]
Random access | 3560.64 | 3577.89 | 99.5%
Low delay | 1693.05 | 1682.46 | 100.6%
All intra | 2466.53 | 2507.11 | 98.4%
Random access loco | 1220.62 | 1209.93 | 100.9%
Low delay loco | 7198.41 | 7209.22 | 99.9 %
All intra loco | 2777.47 | 2765.52 | 100.4%
Average |  |  | 99.9%

## Slide 12: Subjective performance
Informal subjective viewing by experts has been performed in Ericsson
Blind viewing of HM2.0 and the proposal repeatedly without knowing which is which (A and B)
After deciding if they are similar or one is better, identities were revealed
Outcome was that proposal is slightly better on average than anchor

## Slide 13: Conclusions
Modifications to HEVC deblocking are small
  Modifications for luma are about 38 lines of code
  Modifications for chroma include 43 lines of code
Deblocking tables, tc and β thresholds are the same as in the HM2.0
BD-rate = -1.0 % on average
Decoding time = 99.9% of HM2.0 on average
Subjective quality is slightly better that HEVC
Source code is attached from time of document submission
Proposal is cross-verified by: MediaTek, SKKU, Samsung, Toshiba
It is proposed to adopt the changes in the next version of HM