## Slide 1: JCTVC-E281: Slice Parameter Sets
Stephan Wenger, Jill Boyce
Vidyo

## Slide 2: One Slide Summary
Proposed are Slice Parameter Sets
  Similar to picture parameter sets, except that activation occurs at slice boundary
  Proposed for those parameters that can change at slice level, but may have value beyond a single slice
    ALF coefficients? Weighted prediction? CABAC initialization? Others?
Slice header references Slice Parameter Set
Slice Parameter Set contains link to Picture Parameter Set

## Slide 3: Refresh: High level syntax structures
 | Required for Decoding | Not Required
Synchronous w/ Pictures/Slices | Slice Data | SEI Picture Delimiter (SVC payload PACSI)
Not Synchronous | Parameter Sets | VUI

## Slide 4: Slice Parameter Set
slice_parameter_set_id identifies the (storage location of the) slice parameter set. The value of slice_parameter_set_id shall be in the range of 0 to 254, inclusive. (255 reserved for future extensions)
pic_parameter_set_id identifies the picture parameter set that is referred to by the slice parameter set. The value of pic_parameter_set_id shall be in the range of 0 to 63, inclusive.

## Slide 5: Use of Slice Parameter Set on isochronous, high quality links (broadcast)
Use Slice parameter sets like a slice header whose values persist over slice and picture boundaries (unless overwritten)
An encoder can, of course, always reference an earlier slice parameter set, even within a given picture
Activation rules are straightforward
  Each slice header can activate a different slice parameter set, as long as the indirectly referenced (picture/sequence) parameter sets stay the same
SE
P
S
S
Pd
S

## Slide 6: Use of Slice Parameter Sets in error prone conditions
Due to time-critical nature, slice parameter sets must likely be transported in band
RFC3984 (and successors) compound packets allow aggregating slice data with parameter set data to keep packetization overhead low and ensure delivery w/ slice data
Redundant sending of slice parameter sets over error prone link
SE
P
S
S
Pd
S
SE
P
S
S