## Slide 1
<number>
JCTVC-E284: An Adaptive Interpolation Filtering Technique
Faouzi Kossentini
5th JCT Meeting in Geneva
16-23 March 2011

## Slide 2: Outline
<number>
Motivation
Proposed Technique: AIF using adaptive filters
  Filter selection & grouping
  Newly-generated filters
    High Efficiency profiles
    Low Complexity profiles
Simulation Results
Performance & Complexity Analysis
Recommendation

## Slide 3: Motivation
<number>
HM 2.0 filtering does not allow for the use of content- and/or application-adaptive AIF filters.

## Slide 4: AIF Using Adaptive Filters
<number>
AIF Filter Selection:
  For each reference picture list, select between HM 2.0 one/two 8-tap filter(s) or corresponding new AIF filters for each picture/slice & sub-sample position
  New AIF filters can be determined by a specific application and/or generated on-line (i.e., optimized for the picture/slice)
Sub-sample position grouping (as in HM 2.0)
  Employ at most two 8-tap AIF filters for each one of four groups of sub-sample positions
  Side information (i.e., the decision & coefficient bits) is reduced without significant coding efficiency loss

## Slide 5: AIF Using Adaptive Filters
<number>

## Slide 6: AIF Using Adaptive Filters
<number>
Predefined (HM2.0) 8-tap filters (6-bit)
Newly-generated 8-tap filters (6-bit)
¼ | {-1, 4, -10, 57, 19, -7, 3, -1 }
½ | {-1, 4, -11, 40, 40, -11, 4, -1 }
¼ | {a0, a1, a2, a3, a4, a5, a6, a7}
½ | {b0, b1, b2, b3, b3, b2, b1, b0}

## Slide 7: AIF Using Adaptive Filters
<number>
AIF Filter Generation:
  Step 1: Estimate MVs using HM 2.0 filters
  Step 2: Estimate the Most referenced picture by the current one
  Step 3: Estimate filter coefficient values by minimizing the energy of prediction errors after performing MC prediction using MVs from Step 1
AIF Filter Transmission
  Clip the filter coefficient values:
  Compute differences between filter coefficient values and corresponding HM 2.0 filter coefficient values
  Transmit differences
Coefficient index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
clip value | 7 | 15 | 31 | 63 | 63 | 31 | 15 | 7

## Slide 8: Simulation Results
<number>
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.3 | 0.0 | 0.1 | -2.1 | 0.4 | 0.6
Class C | -0.3 | 0.1 | 0.0 | -1.1 | -0.3 | -0.3
Class D | -0.1 | 0.2 | 0.0 | -0.4 | 0.1 | 0.1
Class E | -0.1 | 0.3 | 0.6 | -2.7 | 0.3 | 0.8
All | -0.2 | 0.1 | 0.1 | -1.6 | 0.1 | 0.3
Enc Time[%] | 119 % |  |  | 130 % |  | 
Dec Time[%] | 100 % |  |  | 100 % |  | 

## Slide 9: Simulation Results
<number>
 | Random Access |  |  | Random Acces LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.7 | -1.0 | -1.2 | -2.7 | -1.9 | -2.0
Class B | -0.1 | -0.1 | 0.0 | -0.9 | -0.2 | -0.4
Class C | 0.1 | 0.0 | 0.0 | -0.2 | -0.1 | 0.0
Class D | 0.6 | 0.3 | 0.4 | 0.4 | 0.3 | 0.4
Class E |  |  |  |  |  | 
All | -0.03 | -0.2 | -0.2 | -0.9 | -0.5 | -0.5
Enc Time[%] | 120 % |  |  | 134 % |  | 
Dec Time[%] | 100 % |  |  | 100 % |  | 

## Slide 10: Simulation Results
<number>
 | Sequences | Random Access | Random Access LoCo | LowDelay | LowDelay LoCo
S01 | Traffic | 0.1 | -1.4 |  | 
S02 | PeopleOnStreet | 0.1 | -0.9 |  | 
S0X | Nebuta | -2.2 | -4.6 |  | 
S0Y | SteamLocomotive | -0.8 | -4.0 |  | 
S03 | Kimono | -2.2 | -0.7 | -0.1 | -3.3
S04 | ParkScene | -0.8 | 0.1 | -0.1 | -1.4
S05 | Cactus | 0.1 | -0.5 | -0.1 | -1.4
S06 | BasketballDrive | -2.2 | -0.9 | -0.5 | -1.4
S07 | BQTerrace | -0.8 | -2.4 | -0.7 | -3.1
S08 | BasketballDrill | 0.0 | 0.1 | -0.4 | -1.0
S09 | BQMall | 0.1 | -0.1 | -0.3 | -1.3
S10 | PartyScene | 0.3 | 0.4 | -0.2 | -0.5
S11 | RaceHorses | -0.2 | -1.3 | -0.1 | -1.6
S12 | BasketballPass | 0.3 | 0.2 | -0.4 | -1.2
S13 | BQSquare | 0.8 | 0.6 | 0.0 | 0.0
S14 | BlowingBubbles | 0.6 | 0.8 | -0.1 | 0.0
S15 | RaceHorses | 0.7 | 0.1 | 0.0 | -0.6
S16 | Vidyo1 |  |  | -0.7 | -1.4
S17 | Vidyo3 |  |  | 0.2 | -4.4
S18 | Vidyo4 |  |  | 0.2 | -2.2
Average | All | -0.03 | -0.9 | -0.2 | -1.6

## Slide 11: Performance Analysis
<number>
The proposed technique provides an average of 0.7% reduction in BD-Rate for the Luminance samples when compared to the HM 2.0 technique.
The coding efficiency gains increase for the large video sequences (Classes E, A and B).
The coding efficiency gains are particularly high (more than 3% on average) for the new Class Test sequences.

## Slide 12: Complexity Analysis
<number>
Decoder complexity
  Similar to that of the HM 2.0
  Worst-case additional complexity: Decoding of at most four AIF filters for each video picture/slice (No additional complexity requirement for at least 50% of the video pictures/slices ).
Encoder complexity
  Encoding of at most four AIF filters for each video picture/slice
  Additional complexity depends on the application at hand:
    It can be as large as 25% (MV search, coefficient generation, decision).
    It can have no additional complexity: Use four pre-determined AIF filters for sets of video sequences having similar characteristics.

## Slide 13: Recommendation
<number>
We recommend that the JCT-VC committee adopt the proposed technique into the HM.