## Slide 1: JCTVC-E286: CE6 Subset A: Report of Improved Intra prediction for positive directions in UDI
Yongbing Lin, Changcai Lai,
Jianhua Zheng, Lingzhi Liu

## Slide 2: Introduction
  Positive direction in UDI can find two corresponding reference pixels form main and side arrays, respectively.
    It means both the arrays can be used to improve the prediction accuracy.
  Bi-predictive UDI mode (BUDI) has been proposed in JCTVC-D300
    Taking place of the existing Intra mode 6 (i.e. ver+8 ), can improve the coding performance.
  In this document, BUDI is extended to other positive directions to verify its potential performance.

## Slide 3: BUDI extended to other positive directions
  BUDI is extended to 3 prediction modes: ver+8, ver+5 and hor+6
    it is found that replacing all positive modes with BUDI prediction is not the optimal solution, so these three Intra modes are chosen for simulation.
  Two issues for extending BUDI to other modes
  Unlike to mode ver+8, other modes may require additional 1/32 linear interpolation to generate sub-pixel as reference
  In addition, division operation is introduced by BUDI, so division-free BUDI approach is also implemented by using an approximate weighing algorithm

## Slide 4: Test results
Common test conditions
Anchor: HM2.0
BUDI with replacement of mode ver+8, ver+5 and hor+6
BUDI with replacement of mode ver+8
Division-free BUDI with replacement of mode ver+8, ver+5 and hor+6
Notes: The extended BUDI approach achieves 0.6% and 0.8% bit-rate reduction over HM2.0 with minimum increase of encoding and decoding time for both all Intra HE and LC configurations.

## Slide 5: Conclusion
The performance of the extended BUDI approaches have been reported
  0.6% and 0.8% bit-rate reduction over HM2.0 for all Intra HE and LC configurations
The BUDI approach with replacement of mode ver+8
  0.4% and 0.5% bit-rate reduction with almost the same encoding and decoding time
  better trade-off between performance and complexity
  advantage that the two corresponding reference pixels are integer pixel
It is suggested to adopt the BUDI with replacement of mode ver+8 into HM test model
Many thanks to our cross-checker: Jizheng Xu from Microsoft

## Slide 7: Observation
Positive direction in UDI can find two corresponding reference pixels form main and side arrays, respectively, which means both the arrays can be used to improve the prediction accuracy.
Bi-predictive UDI mode is proposed in JCTVC-D300
  An improved Intra prediction is proposed by taking place of the existing mode ver+8