## Slide 1: JCTVC-E289: Simplified Planar Intra Prediction
26/7/31
Yongbing Lin, Lingzhi Liu,
Jianhua Zheng, Changcai Lai
Notes: <number>

## Slide 2: Introduction
  Planar Intra Prediction (PIP) has been investigated in CE6.e
    First of all, the samples at bottom and right borders of current block are predicted
    Then inner samples are predicted with bilinear interpolation
    It has been reported that PIP improves both objective and subjective performance
  This document aims to reduce the calculation complexity of PIP and proposes two simplified PIP methods
    diagonal-based Intra planar prediction
    sub-block based Intra planar prediction
Page <number>

## Slide 3: Diagonal-based Intra prediction
The samples at diagonal line of current block are firstly predicted by using its left and above reference samples
The other samples can be predicted by linear interpolation with reference of the prediction value of its corresponding diagonal sample and its above/left reference sample.
No bilinear interpolation is required
Page <number>
a) Prediction for the samples at diagonal line
P’ = (LeftRef + AboveRef +1) >>1
b) Prediction for the other samples by
using linear interpolation

## Slide 4: Sub-block based Intra prediction
  A block is divided into a series of 2x2 sub-blocks, and each sub-block is predicted with reference of the prediction value of its neighbor above and left sub-blocks
  2x2 based Intra prediction has lower calculation complexity than the existing PIP
    3 additions and 1.5 shift operations per sample
  As for the aspect of parallel processing
    it is possible for the different rows of 2x2 sub-blocks to be processed with pipelining
Page <number>
P3 = ( b + d +1) >>1
P1 = (b + d + (b<<1) +2) >>2
P2 = (b + d + (d<<1) + 2) >>2
P0 = ( a + c + b + d +2) >>2
P3 = ( b + d +1) >>1
P1 = ( P3 + b +1) >>1 OR
P2 = ( P3 + d +1) >>1
P0 = ( a + c + P1 + P2 +2) >>2
Notes: Multiplying by 3 can be easily implemented with shift and addition operations.
<number>

## Slide 5: 4x4 sub-block Intra prediction
Page <number>
Prediction for right and bottom borders
P15 = ( D + H +1) >>1
P3 = ( P15 + 3*D +2) >>2
P7 = ( P15 + D +1) >>1
P11 = ( 3*P15 + D +2) >>2
P12 = ( P15 + 3*H +2) >>2
P13 = ( P15 + H +1) >>1
P14 = ( 3*P15 + H +2) >>2
Prediction for Inner Samples
P0 = (P12 + 3*A + P3 + 3*E + 4) >>3
P1 = (P13 + 3*B + 2*P3 + 2*E + 4) >>3
P2 = (P14 + 3*C + 3*P3 + E + 4) >>3
P4 = (2*P12 + 2*A + P7 + 3*F + 4) >>3
P5 = (2*P13 + 2*B + 2*P7 + 2*F + 4) >>3
P6 = (2*P14 + 2*C + 3*P7 + F + 4) >>3
P8 = (3*P12 + A + P11 + 3*G + 4) >>3
P9 = (3*P13 + B + 2*P11 + 2*G + 4) >>3
P10 = (3*P14 +C + 3*P11 + G + 4) >>3
For a block of 16x16, the count of bilinear interpolation can be reduced by 36%
    3x3x16=144 of bilinear interpolations for 4x4 sub-block Intra prediction
  15x15 = 225 of bilinear interpolations for the existing planar Intra prediction
Notes: Multiplying by 2 or 3 can be easily implemented with shift and addition operations.
<number>

## Slide 6: Test results
Common test conditions
Anchor: HM2.0
Implementation
  CE6.e reference software
  provided by DOCOMO
  as an additional Intra mode
Page <number>
Performance of Diagonal-based Intra prediction
Performance of the existing Planar Intra prediction (JCTVC-D235)
Notes: Diagonal-based Intra prediction achieves the reduced encoding time while keeps similar performance as the existing planar prediction.
The reduction of encoding time can be explained by the simplification on calculation complexity.
<number>

## Slide 7: Test results
Common test conditions
Anchor: HM2.0
Implementation
  CE6.e reference software
  provided by DOCOMO
  as an additional Intra mode
Page <number>
Performance of 2x2-based Intra prediction
Performance of the existing Planar Intra prediction (JCTVC-D235)
Performance of 4x4-based Intra Prediction
Notes: 2x2 based Intra prediction achieves the reduced encoding time while keeps similar performance as the existing planar prediction.
The reduction of encoding time can be explained by the simplification on calculation complexity.
4x4 based Intra prediction reduces encoding time while keeps almost the same performance as the existing planar Intra prediction.
<number>

## Slide 8: Conclusion
Simplification for PIP is discussed
  Diagonal-based Intra prediction
  Sub-block based Intra prediction
Test results show the proposed methods have lower calculation complexity with similar performance as the existing PIP
It is suggested to adopt the proposed Intra prediction into HM
Page <number>
Many thanks to our cross-checker: Sejong Univ., Korea

## Slide 9
Notes: <number>