## Slide 1: CE11: Adaptive coefficients scanning for inter-frame coding
Huawei Tech. Co, Ltd

## Slide 2: JCTVC-D311
In JCTVC-D311[1], the best scanning pattern for every Transform Unit (TU) is chosen based on the texture direction of reference block and no flag is sent to the decoder side.
Decoding procedure of D311
Problems:
In the parsing procedure, a memory access module should be added.
Parsing procedure will be delayed

## Slide 3: JCTVC-E296
In this proposal a modified adaptive coefficients scanning is contributed. One flag is explicitly signaled to the decoder side to indicate whether the scanning pattern is zigzag or the pattern based on the texture direction. If the scanning pattern is not zigzag, the texture direction is detected after the parsing procedure to achieve the real residual block.

## Slide 4: JCTVC-E296
Decoding procedure of E296
Parsing Procedure
Decompress Procedure

## Slide 5: Experimental results
BD-rate | Y | U | V | Enc | Dec
HE Random access | -0.3 | -0.1 | -0.1 | 102% | 103%
HE Low delay | -1.0 | -0.1 | -0.1 | 102% | 102%
JCTVC-D311
BD-rate | Y | U | V | Enc | Dec
HE Random access | -0.3 | -0.1 | -0.1 | 106% | 101%
HE Low delay | -0.8 | -0.1 | -0.1 | 106% | 101%
JCTVC-E296

## Slide 6: Experimental results
Moreover in an improved method, luma scanning pattern of the same block is applied for chroma TU.
BD-rate | Y | U | V | Enc | Dec
HE Random access | -0.3 | -0.1 | -0.1 | 106% | 101%
HE Low delay | -0.8 | -0.1 | -0.1 | 106% | 101%
JCTVC-E296 only Luma
BD-rate | Y | U | V | Enc | Dec
HE Random access | -0.3 | -0.4 | -0.4 | 107% | 97%
HE Low delay | -0.8 | -0.8 | -0.9 | 106% | 99%
JCTVC-E296 Luma and Chroma