## Slide 1
Security Level：Internal
Lei Zhang
Qiu Shen
Qingpeng Xie
Haoping Yu
Modification for
robust parsing of AMVP

## Slide 2
Introduction
There is a problem of error resilience still existing in current version of HEVC. Decoding will be possibly crushed if the reference frames lost when current frame using temporal motion vector prediction (MVP). So a method is needed to solve this problem.
Page <number>

## Slide 3
Problem statement
In the current HM2.0 design, the number of MVP candidates has been reduced to three, including left MVP, above MVP and temporal MVP.
The coding bitstream is related to MVP numbers and MVP index, as follows.
With the temporal MVP used in AMVP, the parsing problem still exists. For example, if reference frame is lost, the temporal MVP used in MVP candidates of current frame is possibly wrong, and which will influence the number of MVP candidates. If the number of MVP is wrong, decoder would not know how many bits on earth should be parsed, which may induce the parsing problem.
Page <number>
MVPIdx | MVPNum =1 | MVPNum=2 | MVPNum=3
0 | (inferred) | 0 | 0
1 |  | 1 | 10
2 |  |  | 11

## Slide 4
Testing of robust solutions
Page <number>
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.4 | 0.5 | 0.2 | 0.8 | 0.7 | 0.6
Class B | 0.3 | 0.4 | 0.4 | 0.8 | 0.7 | 0.7
Class C | 0.6 | 0.6 | 0.6 | 1.0 | 0.9 | 0.9
Class D | 0.7 | 0.6 | 0.8 | 1.1 | 0.9 | 1.0
Class E |  |  |  |  |  | 
All | 0.5 | 0.5 | 0.5 | 0.9 | 0.8 | 0.8
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.4 | 0.7 | 0.3 | 1.3 | 0.6 | 0.8
Class C | 0.7 | 0.9 | 0.7 | 1.2 | 0.7 | 0.8
Class D | 0.8 | 1.0 | 0.6 | 1.3 | 0.7 | 0.7
Class E | 0.4 | 0.7 | 1.2 | 4.2 | 2.4 | 3.2
All | 0.6 | 0.8 | 0.6 | 1.8 | 1.0 | 1.2
All wo E | 0.6 | 0.9 | 0.5 | 1.3 | 0.7 | 0.7
Robust reference 1 -- “Spatial Left”
When three MVP candidates all exist, including left MVP, above MVP and temporal MVP, merge the two spatial MVP candidates (left MVP and above MVP) into one spatial MVP, the method is getting rid of above MVP. Only one spatial MVP and one temporal MVP exist now, so just one bit needed to be coded and decoded.

## Slide 5
Testing of robust solutions
Page <number>
Robust reference 2 -- “Spatial Above”
When three MVP candidates all exist, including left MVP, above MVP and temporal MVP, merge the two spatial MVP candidates (left MVP and above MVP) into one spatial MVP, the method is getting rid of left MVP. Only one spatial MVP and one temporal MVP exist now, so just one bit needed to be coded and decoded.
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.5 | 0.6 | 0.4 | 0.9 | 0.8 | 0.8
Class B | 0.4 | 0.4 | 0.5 | 0.9 | 0.7 | 0.7
Class C | 0.6 | 0.5 | 0.6 | 0.9 | 0.8 | 0.8
Class D | 0.7 | 0.6 | 0.8 | 1.1 | 1.0 | 1.1
Class E |  |  |  |  |  | 
All | 0.5 | 0.5 | 0.6 | 0.9 | 0.8 | 0.9
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.4 | 0.7 | 0.6 | 1.3 | 0.6 | 0.6
Class C | 0.6 | 0.9 | 0.9 | 1.1 | 0.8 | 0.7
Class D | 0.7 | 0.4 | 0.5 | 1.2 | 0.9 | 0.5
Class E | 0.3 | 0.8 | 1.1 | 4.2 | 2.5 | 3.1
All | 0.5 | 0.7 | 0.7 | 1.8 | 1.1 | 1.1
All wo E | 0.6 | 0.7 | 0.6 | 1.2 | 0.8 | 0.6

## Slide 6
Testing of robust solutions
Page <number>
Robust reference 3 -- “Spatial Average”
When three MVP candidates all exist, including left MVP, above MVP and temporal MVP, merge the two spatial MVP candidates (left MVP and above MVP) into one spatial MVP, the method is get the average of two spatial MVP candidates. Only one spatial MVP and one temporal MVP exist now, so just one bit needed to be coded and decoded.
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.3 | 0.5 | 0.4 | 0.7 | 0.6 | 0.5
Class B | 0.2 | 0.3 | 0.3 | 0.6 | 0.5 | 0.5
Class C | 0.4 | 0.4 | 0.5 | 0.7 | 0.7 | 0.7
Class D | 0.6 | 0.4 | 0.5 | 0.8 | 0.7 | 0.7
Class E |  |  |  |  |  | 
All | 0.4 | 0.4 | 0.4 | 0.7 | 0.6 | 0.6
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.4 | 0.7 | 0.4 | 1.3 | 0.7 | 0.7
Class C | 0.6 | 0.8 | 0.6 | 1.0 | 0.7 | 0.6
Class D | 0.6 | 0.7 | 0.6 | 1.2 | 0.7 | 0.4
Class E | 0.2 | 0.6 | 0.7 | 4.2 | 2.9 | 3.3
All | 0.5 | 0.7 | 0.6 | 1.7 | 1.1 | 1.1
All wo E | 0.5 | 0.7 | 0.5 | 1.2 | 0.7 | 0.6

## Slide 7
Proposal: description and results
Page <number>
The proposed method is based on robust reference 3 (Spatial Average)
If there is any spatial MVP existing, it should be coded MVP index, and if there is no spatial MVP existing in MVP candidates, the MVP index is not coded, which can be inferred in the decoder. And it would not influence the decoder parsing even if any packets lost happen.
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.2 | 0.3 | 0.0 | 0.5 | 0.4 | 0.4
Class B | 0.0 | 0.2 | 0.2 | 0.4 | 0.4 | 0.4
Class C | 0.2 | 0.2 | 0.3 | 0.5 | 0.5 | 0.5
Class D | 0.3 | 0.3 | 0.4 | 0.5 | 0.5 | 0.4
Class E |  |  |  |  |  | 
All | 0.2 | 0.2 | 0.2 | 0.5 | 0.4 | 0.4
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.5 | 0.3 | 0.8 | 0.4 | 0.7
Class C | 0.2 | 0.6 | 0.3 | 0.6 | 0.5 | 0.3
Class D | 0.2 | 0.3 | -0.1 | 0.6 | 0.2 | 0.0
Class E | 0.3 | 0.8 | 0.9 | 3.6 | 2.9 | 3.0
All | 0.2 | 0.5 | 0.3 | 1.2 | 0.8 | 0.9
All wo E | 0.2 | 0.4 | 0.1 | 0.7 | 0.4 | 0.4

## Slide 8
Conclusion
The proposed robust method not only solves the parsing problem, but also without too much performance loss. Consequently, we recommend the adoption of the modified advanced motion vector prediction for packets lost. Furthermore, the proposed robust method is just for AMVP parsing problem, meanwhile merge mode has the similar parsing problem to be solved.
Page <number>