## Slide 1: Parallel Prediction Unit for Parallel Intra Coding JCTVC-E315 Jie Zhao and Andrew Segall
l
Notes: <number>

## Slide 2: Overview
We have shown parallel intra prediction (PIP) in previous proposal JCTVC-D074.
Our goal is to Reduce serial dependencies in the intra-prediction process
Here, we review this technology first and then provide updated results of PIP in HM2.0.

## Slide 3: Parallel Prediction Unit
Motivation:
  Intra-prediction design in HM results in a significant bottleneck
    Due to the casual prediction of pixel values (top/left/left top neighbors)
    Small block sizes results in more dependencies within an LCU
    This impacts designs for all architectures
Our solution –Parallel Prediction Unit
  Defines a CU size within a LCU that can be encoded/decoded in parallel
  For CUs that are larger than a defined PPU size, traditional sequential prediction is performed
  Benefit: Enables parallelism for as serial dependencies increase (small blocks) within an LCU
LCU
CU/PU/TU
CU
CU
CU
CU/PU/TU
CU/PU/TU
CU/PU/TU
PPU

## Slide 4: Parallel Intra Prediction (2x)
Steps of Parallel Intra Prediction:
  Divide parallel unit into two sets of blocks
  1st set of blocks predicted using neighbors outside parallel unit
  2nd set of blocks predicted using neighbors outside parallel unit and reconstructed 1st pass blocks.
Benefit: 2X parallelism for intra-prediction on small blocks
To be clear:
    CU/PU with intra split flag on
    PU split to four TUs.
First set blocks
Second set blocks

## Slide 5: Parallel Intra Prediction (2x)
  Second set prediction
    Prediction using upper/left neighbors and bottom/right neighbors using weighted combination
    We use a fixed prediction weighting table
    Weighting is signaled on a slice basis
      Encoder friendly
      When enabled, the number of modes is the same – the HM direction and its mirror are used
    Motivation: prediction of 1st pass block losses coding efficiency compared to serial processing; we make up the performance with improved 2nd pass prediction.
First set blocks
Second set blocks

## Slide 6: Performance
Performance
  Compare parallel intra prediction versus current (serial) approach
  Conditions
    HM2.0
    All 6 standard test Configurations
    PPU of 8x8 (HD only)
Average Impact on BD rate
  Intra (HC&LC): 0.3%
  Randomaccess (HC&LC): 0.1%
  Lowdelay (HC&LC): 0.0%
So, reduce the serial bottleneck of small block sizes on large resolution pictures with negligible impact on coding efficiency

## Slide 7: Compatibility and Future Extensions
Extensions
  In this meeting cycle, we combined Parallel Intra Prediction method with Combined Intra Prediction (from BBC)
    Results are reported in E130 and show further improvement in coding efficiency
  Additionally, we have extended our technique to higher degrees of parallelism (8x).
    Results are reported in the document and show 8x is possible with 0.1%, 0.2% and 0.4% for AI, LD and RA.

## Slide 8: Conclusions
Conclusions
  We presented parallel intra prediction technique for HEVC design.
  Provides parallelism for both encoder and decoder.
    Parallelism is achieved by partitioning a PPU into two sets
      First set predicted from boundaries of PPU
      Second set predicted from all available pixels.
  Result is 2x parallelism for small block sizes (most critical bottleneck)
  Performance -- impact on average BD rate
    Intra (both HC and LC): 0.3%
    Random access (both HC and LC): 0.1%
    Low delay (both HC and LC): 0.0%
  Method verified by Toshiba (JCTVC-E208)
  Method extensible (combined with CIP/E130 and extensible to 8x/E315)
  Propose to adopt this technique to HM.