## Slide 1: JCTVC-E323 CE9: Qualcomm’s proposal for block based adaptive loop filter

## Slide 2: Motivations
  In the Daegu meeting,
  Concerns about the pixel based classification in current adaptive loop filter (ALF) in HM2.0
Two approaches to enhance pixel based ALF
  Block based Laplacian Activity for each 4x4 block
  Block based directional information on top of Laplacian activity

## Slide 3: Block based pixel classification
Block based Laplacian Activity for each 4x4 block
  Averaged sum of Laplacian metric (SLM) for each 4x4 block
Block based directional information on top
  Derive Direction using 1D Laplacian metric (reuse SLM computations)
    Vertical activity = sumi,j| (R(i,j)<<1) –R(i-1,j)-R(i+1,j)| with i,j =0…3
    Horizontal activity = sumi,j| (R(i,j)<<1) –R(i,j-1)-R(i,j+1)| with i,j=0…3
    Direction = 1, if Vertical activity > threshold*Horizontal activity,
    Direction = 2, if Horizontal activity > threshold* Vertical activity
    Direction = 0, otherwise
Activity Metric = 3*Laplacian Activity + Direction
Minor code changes from HM2.0
  No Syntax changes
  No encoding/ decoding changes
  Pixel classifications are modified (2~3 functions)

## Slide 4: Results
HE cases only
Cross checked by Sharp/Samsung

## Slide 5: Results
 | Intra |  |  |  | Random access |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.2 | 0.0 | 0.0 | -0.5 | 0.1 | -0.1 |  |  | 
Class B | -0.2 | 0.1 | 0.1 | -0.7 | 0.0 | 0.0 | -0.4 | -0.1 | 0.0
Class C | -0.3 | 0.2 | 0.2 | -0.4 | 0.1 | 0.1 | -0.4 | 0.2 | 0.3
Class D | -0.1 | 0.2 | 0.2 | -0.2 | 0.2 | 0.1 | -0.2 | 0.2 | -0.4
Class E | -0.2 | 0.2 | 0.2 |  |  |  | -0.5 | -0.1 | 0.6
All | -0.2 | 0.1 | 0.1 | -0.5 | 0.1 | 0.0 | -0.4 | 0.0 | 0.1
Enc Time[%] | 102% |  |  | 102% |  |  | 102% |  | 
Dec Time[%] | 93% |  |  | 92% |  |  | 94% |  | 

## Slide 6: Results- Block based SLM only
 | Intra |  |  |  | Random access |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | 0.2 | 0.2 | -0.1 |  |  | 
Class B | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.2 | 0.1 | -0.1
Class C | 0.2 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1
Class D | 0.1 | 0.0 | 0.0 | 0.1 | 0.0 | 0.1 | -0.1 | 0.1 | -0.1
Class E | 0.0 | -0.1 | -0.1 |  |  |  | -0.2 | -0.5 | 0.1
All | 0.1 | 0.0 | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  |  | 99% |  | 
Dec Time[%] | 95% |  |  | 95% |  |  | 93% |  | 

## Slide 7: Conclusion
Better performance than pixel based classifications
  0.2/0.5/0.4% BD rate reduction (Intra/RA/LD)
Lower decoder complexity
  6-8% decoder speed up
With minor changes from anchor in HM2.0
  No syntax changes
  No encoder/decoder changes except pixel classification

## Slide 8: Switching of Single filter and Block based ALF
  In CE8: Subset 2
  Candidate 1 :Switching of Single filter and pixel based ALF
  Candidate 2: Block based ALF
Switching of Single filter and Block based ALF
  Replace pixel based ALF in Candidate 1 with block based ALF in Candidate 2
  Single filter ALF: 16 groups of pixel classifications
    16 regions: Divide each picture into 16 regions
  Block based ALF: 16 groups of pixel classifications
    16 Activity metric (SLM + direction) for each 4x4 blocks
  Both are block based.
  No syntax changes except one slice level flag (for switching)
  Minor code changes compared to anchor in HM2.0
    Pixel classifications
    In encoder, comparison between Single filter/Block based ALF

## Slide 9: Results
 | Intra |  |  |  | Random access |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.1 | 0.0 | 0.0 | -0.5 | 0.1 | 0.0 |  |  | 
Class B | -0.1 | 0.1 | 0.1 | -0.7 | 0.1 | 0.1 | -0.9 | -0.1 | 0.0
Class C | -0.2 | 0.1 | 0.1 | -0.5 | 0.2 | 0.2 | -0.8 | 0.2 | 0.1
Class D | 0.0 | 0.1 | 0.1 | -0.2 | 0.1 | 0.1 | -0.3 | -0.3 | -0.1
Class E | -0.1 | 0.1 | 0.1 |  |  |  | -1.3 | 0.1 | 0.0
All | -0.1 | 0.1 | 0.1 | -0.5 | 0.1 | 0.1 | -0.8 | 0.0 | 0.0
Enc Time[%] | 105% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 94% |  |  | 91% |  |  | 93% |  |