## Slide 1: JCTVC-E338 CE11: Parallel context processing for the significance map in high coding efficiency
J. Sole, R. Joshi, M. Karczewicz

## Slide 2: Summary
CE11: Coefficient scanning and coding
Parallel coding for the significance map for high efficiency
  Separation of the significance and last flags
  Explicit signaling of the location of the last significant coefficient
    Code the (X,Y) coordinates of the last coefficient
Implementation in HM2.0
  Reduction of number of bins (5% for AI, 2% RA, 0% LD)
  BD-rate reduction
    Luma: -0.03% (AI) 0.01% (RA) -0.10% (LD)
    Chroma: -0.02% (AI) -0.85% (RA) -1.90% (LD)

## Slide 3: Background
In HEVC, significance map is coded is by interleaving the bins of
  Significance of a coefficient
  Last significant within the block (when the coefficient is significant)
Significance map represents the largest number of bins
  43% for Intra, 36% for random access and low delay
Data dependencies in context selection
Difficult to parallelize due to the interleaving of syntax elements

## Slide 4: Explicit signaling of the last significant coefficient
Separate the coding of the significance and the last
  Code the position (X, Y) of the last significant coefficient
  Code all the significance flags
Code the (X,Y) coordinates of the last significant coefficient
  X and Y coded independently
    First X, then Y
  Truncated unary code
  Simple contexts

## Slide 5: Context Selection in CABAC
Last significant coefficient position
  Context depends only on the row/column number and the block size
    4×4: 3 contexts per coordinate (X,Y)
    8×8: 7 contexts
    16×16: 12 contexts
    32×32: 16 contexts
Significance map context
  If the last coefficient is in the first 10 coefficients in scanning order, then the context depends only on the position
  Otherwise, regular contexts are used

## Slide 6: Results: BD-rate
BD-rate and encoding/decoding times
  * Thanks to Panasonic (JCTVC-E164) and Sony (JCTVC-E300) for the cross-check
BD-rate | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.17 | -0.22 | -0.14 | -0.07 | -1.10 | -0.92 |  |  | 
Class B | -0.07 | 0.06 | 0.07 | -0.02 | -0.62 | -0.46 | -0.07 | -1.36 | -1.74
Class C | 0.11 | 0.10 | 0.06 | 0.07 | -0.94 | -0.83 | -0.06 | -1.51 | -1.40
Class D | -0.06 | -0.05 | 0.10 | 0.05 | -1.15 | -0.86 | -0.19 | -2.87 | -3.07
Class E | 0.09 | -0.05 | -0.18 |  |  |  | -0.11 | -2.26 | -1.06
All | -0.03 | -0.03 | -0.01 | 0.01 | -0.94 | -0.75 | -0.10 | -1.94 | -1.86
Enc T[%] | 100% |  |  | 100% |  |  | 98% |  | 
Dec T[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 7: Results: bin counts
Average bin count with respect to HM2.0
Worse-case number of bins for last flag is reduced
  N×N block: maximum bins reduced from N*N-1 to 2N-2
    For 32×32: from 1023 bins to 62
%bins | Total | Sig Coef | Last
Intra | 95% | 94% | 77%
Random access | 98% | 96% | 93%
Low delay | 100% | 96% | 115%

## Slide 8: Conclusions
Proposed an algorithm to parallelize the significance map coding
  Separation of the significance and last coefficient planes
  X and Y components are coded independently
  Simple context selection
  Parallelization benefits and better performance

## Slide 9
Thank you!