## Slide 1: On num_reorder_frames and max_dec_frame_buffering
JCTvc-E339
Rickard Sjöberg
ericsson AB

## Slide 2: background
max_dec_frame_buffering and num_reorder_frames is part of the optional VUI parameters of the H.264 SPS
The VUI syntax is inherited from H.264 into HEVC that says the following:
  max_dec_frame_buffering The coded video sequence shall not require a decoded picture buffer with size of more than Max( 1, max_dec_frame_buffering ) frame buffers to enable the output of decoded pictures
  num_reorder_frames “num_reorder_frames indicates the maximum number of frames ... that precede any frame ... in the coded video sequence in decoding order and follow it in output order “
When VUI parameters are not present, both max_dec_frame_buffering and num_reorder_frames are set to MaxDpbFrames

## Slide 3: example
Consider a low-delay encoding of the 416x240 60Hz BQSquare sequence that uses two reference pictures
The max macroblock processing rate (MaxMBPS) is 23,400
Since MaxMBPS of level 2.2 is 20,250 while for level 3 it is 40,500 the lowest level possible for this sequence is a level 3
Level 3 has a Max decoded picture buffer size (MaxDpbMbs) of 8,100
MaxDpbFrames then becomes MaxDpbFrames = Min( MaxDpbMbs / ( PicWidthInMbs * FrameHeightInMbs ), 16 ) = 16
If VUI syntax is not sent, max_dec_frame_buffering and num_reorder_frames both becomes 16

## Slide 4: example
The decoded picture buffer immediately after decoding a picture will generally look as follows:
But the decoder does not know that this situation will never happen:
non-ref
n
Type
POC
non-ref
n+1
non-ref
n+2
ref
n+14
ref
n+15
ref
n+16
...
...
...
non-ref
n+1
Type
POC
non-ref
n+2
non-ref
n+3
ref
n+15
ref
n+16
ref
n
...
...
...

## Slide 5: proposal
We propose to mandate num_reorder_frames and dec_ref_frame_buffering in the SPS
The advantage of a mandatory dec_ref_frane_buffering is that decoders will know how much memory to allocate and not having to allocate the maximum amount
The advantage of a mandatory num_reorder_frames is to minimize unnecessary delay at the decoder