## Slide 1: Context Reduction of the Last Transform Position in JCTVC-D262 for CE 11.1
Cheung Auyeung, Wei Liu
Sony
March 10, 2011
<number>
JVTVC-E344

## Slide 2: Summary
Objective
  Reduce the number of context for coding the position of the last transform coefficient proposed in JCTVC-D262 within CE 11.1.
Status
  Reduced the number of context for YUV 4:2:0 video from 120 to 82 context.
  “No change” in coding efficiency when compared with the cross-checked results of JCTVC-D262 in CE 11.1.
Cross-Checking
  Being done by Panasonic
<number>

## Slide 3: JCTVC-D262 in CE 11.1
Separate the encoding of the significant_coeff_flag and the last_significant_coeff_flag:
  First, code the position of the last significant coefficient
  Second, code the significance coefficient flags
Code the (X,Y) coordinates of the last significant coefficient independently
  Use truncated unary code for binarization.
    3 bins for block width of 4
    7 bins for block width of 8
    15 bins for block with of 16
    31 bins for block width of 32
  Context depends on chroma/luma, block size, and the bit position in the binarization.
  For YUV 4:2:0 format video, the X and Y have 60x2 contexts
    38x2 contexts for luma.
    22x2 contexts for chroma.
<number>

## Slide 4: Context Assignments in JCTVC-D262
The X and Y context assignments are the same.
  For YUV 4:20: video, the X has 60 contexts, and the Y has 60 contexts.
X luma coordinate with width of 4 has 3 contexts.
X luma coordinate with width of 8 has 7 contexts.
X luma coordinate with width of 16 has 12 contexts.
X luma coordinate with width of 32 has 16 contexts.
To reduce the number of contexts, this contribution removed the contexts 4, 6, 8, 10, 15, and some 11 (in orange).
<number>
0
1
2
7
8
8
9
3
4
5
6
9
10
10
11
11
12
12
12
12
13
13
13
13
14
14
14
14
15
15
15
0
1
2
7
8
8
9
3
4
5
6
9
10
10
11
0
1
2
3
4
5
6
0
1
2
<number>

## Slide 5: Proposed Context Assignments
Reduced the number of contexts from 60x2 to 41x2 for YUV 4:2:0 video.
X luma coordinate with width of 4 has 3 contexts.
X luma coordinate with width of 8 has 5 contexts.
X luma coordinate with width of 16 has 7 contexts.
X luma coordinate with width of 32 has 11 contexts.
To reduce the number of contexts, this contribution
  Removed the contexts with context number 4, 6, 8, 10, 15 and some 11.
  Re-assigned the context 3, 5, 7, 9, 11, 12, 13, 14 (in yellow).
<number>
0
1
2
7
7
7
7
3
3
5
5
9
9
9
9
11
11
11
11
12
12
12
12
13
13
13
13
14
14
14
14
0
1
2
7
7
7
7
3
3
5
5
9
9
9
9
0
1
2
3
3
5
5
0
1
2

## Slide 6: BD-Rate Compared to HM-2.0
<number>
JCTVC-E344 vs HM2.0
JCTVC-E338 vs HM2.0
 | Intra |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.16 | -0.23 | -0.19
Class B | -0.07 | 0.04 | 0.06
Class C | 0.12 | 0.12 | 0.05
Class D | -0.05 | -0.05 | 0.07
Class E | 0.10 | -0.07 | -0.21
All | -0.02 | -0.03 | -0.03
Enc Time[%] | #NUM! |  | 
Dec Time[%] | #NUM! |  | 
 |  | Random access | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.11 | -1.00 | -1.53
Class B | -0.02 | -0.57 | -0.60
Class C | 0.09 | -0.87 | -0.74
Class D | 0.04 | -1.30 | -0.79
Class E |  |  | 
All | 0.00 | -0.92 | -0.89
Enc Time[%] | #NUM! |  | 
Dec Time[%] | #NUM! |  | 
 | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -0.11 | -1.31 | -1.81
Class C | -0.05 | -1.45 | -1.25
Class D | -0.25 | -3.04 | -2.76
Class E | -0.18 | -2.04 | -0.83
All | -0.14 | -1.92 | -1.72
Enc Time[%] | #NUM! |  | 
Dec Time[%] | #NUM! |  | 
BD-rate | Intra |  | 
 | Y | U | V
Class A | -0.17 | -0.22 | -0.14
Class B | -0.07 | 0.06 | 0.07
Class C | 0.11 | 0.10 | 0.06
Class D | -0.06 | -0.05 | 0.10
Class E | 0.09 | -0.05 | -0.18
All | -0.03 | -0.03 | -0.01
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
BD-rate | Random access |  | 
 | Y | U | V
Class A | -0.07 | -1.10 | -0.92
Class B | -0.02 | -0.62 | -0.46
Class C | 0.07 | -0.94 | -0.83
Class D | 0.05 | -1.15 | -0.86
Class E |  |  | 
All | 0.01 | -0.94 | -0.75
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
BD-rate | Low delay |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.07 | -1.36 | -1.74
Class C | -0.06 | -1.51 | -1.40
Class D | -0.19 | -2.87 | -3.07
Class E | -0.11 | -2.26 | -1.06
All | -0.10 | -1.94 | -1.86
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 

## Slide 7: Bin Statistics Compared to JCTVC-D262
<number>
 |  |  | Proposed |  |  |  |  |  |  | JCTVC-D262 |  | 
 | Intra |  |  |  |  |  |  | Intra |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass |  | % sig | % last | % coeff | % reg | % bypass
Class A | 0% | 32% | 9% | 30% | 84% | 16% |  | 32% | 9% | 30% | 84% | 16%
Class B | 0% | 33% | 11% | 24% | 85% | 15% |  | 33% | 11% | 24% | 85% | 15%
Class C | 0% | 27% | 13% | 24% | 85% | 15% |  | 27% | 13% | 24% | 85% | 15%
Class D | 0% | 26% | 13% | 25% | 84% | 16% |  | 26% | 13% | 25% | 84% | 16%
Class E | 0% | 26% | 11% | 24% | 86% | 14% |  | 26% | 11% | 24% | 86% | 14%
All | 0% | 29% | 11% | 25% | 85% | 15% |  | 29% | 11% | 25% | 85% | 15%
 | Random access |  |  |  |  |  |  | Random access |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass |  | % sig | % last | % coeff | % reg | % bypass
Class A | 0% | 29% | 8% | 18% | 85% | 14% |  | 29% | 8% | 18% | 85% | 14%
Class B | 0% | 28% | 9% | 16% | 87% | 13% |  | 28% | 9% | 16% | 87% | 13%
Class C | 0% | 23% | 10% | 15% | 86% | 13% |  | 23% | 10% | 15% | 86% | 13%
Class D | 0% | 22% | 10% | 15% | 87% | 13% |  | 22% | 10% | 15% | 87% | 13%
Class E |  |  |  |  |  |  |  |  |  |  |  | 
All | 0% | 26% | 9% | 16% | 86% | 13% |  | 26% | 9% | 16% | 86% | 13%
 | Low delay |  |  |  |  |  |  | Low delay |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass |  | % sig | % last | % coeff | % reg | % bypass
Class A |  |  |  |  |  |  |  |  |  |  |  | 
Class B | 0% | 29% | 10% | 13% | 88% | 11% |  | 29% | 10% | 13% | 88% | 11%
Class C | 0% | 25% | 10% | 13% | 88% | 12% |  | 25% | 10% | 13% | 88% | 12%
Class D | 0% | 25% | 11% | 12% | 88% | 12% |  | 25% | 11% | 12% | 88% | 12%
Class E | 0% | 22% | 8% | 8% | 89% | 8% |  | 22% | 8% | 8% | 89% | 8%
All | 0% | 26% | 10% | 11% | 88% | 11% |  | 26% | 10% | 11% | 88% | 11%
The proposed reduction of the number of context has the same bin statistics as JCTVC-D262

## Slide 8: Bin Statistics Compared to HM2.0
<number>
 |  |  | PROPOSED |  |  |  |  |  |  | ANCHOR |  | 
 | Intra |  |  |  |  |  |  | Intra |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass |  | % sig | % last | % coeff | % reg | % bypass
Class A | -7% | 32% | 9% | 30% | 84% | 16% |  | 30% | 14% | 27% | 85% | 15%
Class B | -4% | 33% | 11% | 24% | 85% | 15% |  | 32% | 14% | 23% | 86% | 14%
Class C | -5% | 27% | 13% | 24% | 85% | 15% |  | 28% | 14% | 23% | 85% | 15%
Class D | -5% | 26% | 13% | 25% | 84% | 16% |  | 27% | 15% | 24% | 85% | 15%
Class E | -5% | 26% | 11% | 24% | 86% | 14% |  | 27% | 13% | 23% | 87% | 13%
All | -5% | 29% | 11% | 25% | 85% | 15% |  | 29% | 14% | 24% | 86% | 14%
 | Random access |  |  |  |  |  |  | Random access |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass |  | % sig | % last | % coeff | % reg | % bypass
Class A | -4% | 29% | 8% | 18% | 85% | 14% |  | 28% | 11% | 17% | 86% | 14%
Class B | -1% | 28% | 9% | 16% | 87% | 13% |  | 28% | 10% | 16% | 87% | 13%
Class C | -2% | 23% | 10% | 15% | 86% | 13% |  | 23% | 10% | 15% | 86% | 13%
Class D | -1% | 22% | 10% | 15% | 87% | 13% |  | 23% | 10% | 15% | 86% | 13%
Class E |  |  |  |  |  |  |  |  |  |  |  | 
All | -2% | 26% | 9% | 16% | 86% | 13% |  | 26% | 10% | 16% | 86% | 13%
 | Low delay |  |  |  |  |  |  | Low delay |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass |  | % sig | % last | % coeff | % reg | % bypass
Class A |  |  |  |  |  |  |  |  |  |  |  | 
Class B | 0% | 29% | 10% | 13% | 88% | 11% |  | 29% | 10% | 13% | 88% | 11%
Class C | 0% | 25% | 10% | 13% | 88% | 12% |  | 26% | 9% | 13% | 87% | 12%
Class D | 1% | 25% | 11% | 12% | 88% | 12% |  | 26% | 9% | 12% | 88% | 12%
Class E | 1% | 22% | 8% | 8% | 89% | 8% |  | 23% | 7% | 8% | 89% | 9%
All | 0% | 26% | 10% | 11% | 88% | 11% |  | 27% | 9% | 12% | 88% | 11%

## Slide 9: Conclusions
Reduced the number of context in parallel processing friendly proposal JCVC-D262 in CE 11.1 from 120 contexts to 82 contexts for YUV 4:2:0 video with no loss in BD performance.
Results are being cross-checked in similar manner as in CE11 by Panasonic.
Propose to JCT-VC to adopt it with JCTVC-D262 as a part of HM 3.0 for better parallel processing and throughput.
<number>